## Slide 1
Quality Control

## Slide 2: Overview
Introduction
Statistical Concepts in Quality Control
Control Charts
Acceptance Plans
Computers in Quality Control
Quality Control in Services
Wrap-Up: What World-Class Companies Do

## Slide 3: Introduction
Quality control (QC) includes the activities from the suppliers, through production, and to the customers.
Incoming materials are examined to make sure they meet the appropriate specifications.
The quality of partially completed products are analyzed to determine if production processes are functioning properly.
Finished goods and services are studied to determine if they meet customer expectations.

## Slide 4: QC Throughout Production Systems
Raw Materials,
Parts, and
Supplies
Production
Processes
Products and
Services
Inputs
Conversion
Outputs
Control Charts
and
Acceptance Tests
Control Charts
and
Acceptance Tests
Control Charts
Quality of
Inputs
Quality of
Outputs
Quality of
Partially Completed
Products

## Slide 5: Services and Their Customer Expectations
Hospital
  Patient receive the correct treatments?
  Patient treated courteously by all personnel?
  Hospital environment support patient recovery?
Bank
  Customer’s transactions completed with precision?
  Bank comply with government regulations?
  Customer’s statements accurate?

## Slide 6: Products and Their Customer Expectations
Automaker
  Auto have the intended durability?
  Parts within the manufacturing tolerances?
  Auto’s appearance pleasing?
Lumber mill
  Lumber within moisture content tolerances?
  Lumber properly graded?
  Knotholes, splits, and other defects excessive?

## Slide 7: Sampling
The flow of products is broken into discrete batches called lots.
Random samples are removed from these lots and measured against certain standards.
A random sample is one in which each unit in the lot has an equal chance of being included in the sample.
If a sample is random, it is likely to be representative of the lot.

## Slide 8: Sampling
Either attributes or variables can be measured and compared to standards.
Attributes are characteristics that are classified into one of two categories, usually defective (not meeting specifications) or nondefective (meeting specifications).
Variables are characteristics that can be measured on a continuous scale (weight, length, etc.).

## Slide 9: Size and Frequency of Samples
As the percentage of lots in samples is increased:
  the sampling and sampling costs increase, and
  the quality of products going to customers increases.
Typically, very large samples are too costly.
Extremely small samples might suffer from statistical imprecision.
Larger samples are ordinarily used when sampling for attributes than for variables.

## Slide 10: When to Inspect During the Production Process
Inspect before costly operations.
Inspect before operations that are likely to produce faulty items.
Inspect before operations that cover up defects.
Inspect before assembly operations that cannot be undone.
On automatic machines, inspect first and last pieces of production runs, but few in-between pieces.
Inspect finished products.

## Slide 11: Central Limit Theorem
The central limit theorem is: Sampling distributions can be assumed to be normally distributed even though the population (lot) distributions are not normal.
The theorem allows use of the normal distribution to easily set limits for control charts and acceptance plans for both attributes and variables.

## Slide 12: Sampling Distributions
The sampling distribution can be assumed to be normally distributed unless sample size (n) is extremely small.
The mean of the sampling distribution ( x ) is equal to the population mean (m).
The standard error of the sampling distribution (sx ) is smaller than the population standard deviation (sx ) by a factor of 1/
=
-

## Slide 13: Population and Sampling Distributions
f(x)
Population Distribution
Sampling Distribution
of Sample Means
Mean = m
Std. Dev. = sx
Mean = x = m
Std. Error =
=
x

## Slide 14: Control Charts
Primary purpose of control charts is to indicate at a glance when production processes might have changed sufficiently to affect product quality.
If the indication is that product quality has deteriorated, or is likely to, then corrective is taken.
If the indication is that product quality is better than expected, then it is important to find out why so that it can be maintained.
Use of control charts is often referred to as statistical process control (SPC).

## Slide 15: Constructing Control Charts
Vertical axis provides the scale for the sample information that is plotted on the chart.
Horizontal axis is the time scale.
Horizontal center line is ideally determined from observing the capability of the process.
Two additional horizontal lines, the lower and upper control limits, typically are 3 standard deviations below and above, respectively, the center line.

## Slide 16: Constructing Control Charts
If the sample information falls within the lower and upper control limits, the quality of the population is considered to be in control; otherwise quality is judged to be out of control and corrective action should be considered.
Two versions of control charts will be examined
  Control charts for attributes
  Control charts for variables

## Slide 17: Control Charts for Attributes
Inspection of the units in the sample is performed on an attribute (defective/non-defective) basis.
Information provided from inspecting a sample of size n is the percent defective in a sample, p, or the number of units found to be defective in that sample divided by n.

## Slide 18: Control Charts for Attributes
Although the distribution of sample information follows a binomial distribution, that distribution can be approximated by a normal distribution with a
  mean of p
  standard deviation of
The 3s control limits are
-

## Slide 19: Example: Attribute Control Chart
Every check cashed or deposited at Lincoln Bank must be encoded with the amount of the check before it can begin the Federal Reserve clearing process. The accuracy of the check encoding process is of upmost importance. If there is any discrepancy between the amount a check is made out for and the encoded amount, the check is defective.

## Slide 20: Example: Attribute Control Chart
Twenty samples, each consisting of 250 checks, were selected and examined. The number of defective checks found in each sample is shown below.

## Slide 21: Example: Attribute Control Chart
The manager of the check encoding department knows from past experience that when the encoding process is in control, an average of 1.6% of the encoded checks are defective.
She wants to construct a p chart with 3-standard deviation control limits.

## Slide 22: Example: Attribute Control Chart

## Slide 23: Example: Attribute Control Chart

## Slide 24: Control Charts for Variables
Inspection of the units in the sample is performed on a variable basis.
The information provided from inspecting a sample of size n is:
  Sample mean, x, or the sum of measurement of each unit in the sample divided by n
  Range, R, of measurements within the sample, or the highest measurement in the sample minus the lowest measurement in the sample

## Slide 25: Control Charts for Variables
In this case two separate control charts are used to monitor two different aspects of the process’s output:
  Central tendency
  Variability
Central tendency of the output is monitored using the x-chart.
Variability of the output is monitored using the R-chart.

## Slide 26: x-Chart
The central line is x, the sum of a number of sample means collected while the process was considered to be “in control” divided by the number of samples.
The 3s lower control limit is x - AR
The 3s upper control limit is x + AR
Factor A is based on sample size.
=
=
=

## Slide 27: R-Chart
The central line is R, the sum of a number of sample ranges collected while the process was considered to be “in control” divided by the number of samples.
The 3s lower control limit is D1R.
The 3s upper control limit is D2R.
Factors D1and D2 are based on sample size.

## Slide 28: 3s Control Chart Factors for Variables
Control Limit Factor Control Limit Factor
Sample for Sample Mean for Sample Range
Size n A D1 D2
2 1.880 0 3.267
3 1.023 0 2.575
4 0.729 0 2.282
5 0.577 0 2.116
10 0.308 0.223 1.777
15 0.223 0.348 1.652
20 0.180 0.414 1.586
25 0.153 0.459 1.541
Over 25 0.45+.001n 1.55-.0015n

## Slide 29: Example: Variable Control Chart
Harry Coates wants to construct x and R charts at the bag-filling operation for Meow Chow cat food. He has determined that when the filling operation is functioning correctly, bags of cat food average 50.01 pounds and regularly-taken 5-bag samples have an average range of .322 pounds.

## Slide 30: Example: Variable Control Chart
Sample Mean Chart
x = 50.01, R = .322, n = 5
  UCL = x + AR = 50.01 + .577(.322) = 50.196
  LCL = x - AR = 50.01 - .577(.322) = 49.824
=
=
=

## Slide 31: Example: Variable Control Chart

## Slide 32: Example: Variable Control Chart
Sample Range Chart
x = 50.01, R = .322, n = 5
  UCL = RD2 = .322(2.116) = .681
  LCL = RD1 = .322(0) = 0
=

## Slide 33: Example: Variable Control Chart

## Slide 34: Acceptance Plans
Trend today is toward developing testing methods that are so quick, effective, and inexpensive that products are submitted to 100% inspection/testing
Every product shipped to customers is inspected and tested to determine if it meets customer expectations
But there are situations where this is either impractical, impossible or uneconomical
  Destructive tests, where no products survive test
In these situations, acceptance plans are sensible

## Slide 35: Acceptance Plans
An acceptance plan is the overall scheme for either accepting or rejecting a lot based on information gained from samples.
The acceptance plan identifies the:
  Size of samples, n
  Type of samples
  Decision criterion, c, used to either accept or reject the lot
Samples may be either single, double, or sequential.

## Slide 36: Single-Sampling Plan
Acceptance or rejection decision is made after drawing only one sample from the lot.
If the number of defectives, c’, does not exceed the acceptance criteria, c, the lot is accepted.

## Slide 37: Single-Sampling Plan
Lot of N Items
Random
Sample of
n Items
N - n Items
Inspect n Items
c’ > c
c’ < c
Replace
Defectives
n Nondefectives
c’ Defectives
Found in Sample
Reject Lot
Accept Lot

## Slide 38: Double-Sampling Plan
One small sample is drawn initially.
If the number of defectives is less than or equal to some lower limit, the lot is accepted.
If the number of defectives is greater than some upper limit, the lot is rejected.
If the number of defectives is neither, a second larger sample is drawn.
Lot is either accepted or rejected on the basis of the information from both of the samples.

## Slide 39: Double-Sampling Plan
Lot of N Items
Random
Sample of
n1 Items
N – n1 Items
Inspect n1 Items
c1’ > c2
c1’ < c1
Replace
Defectives
n1 Nondefectives
c1’ Defectives
Found in Sample
Reject Lot
Accept Lot
Continue
c1 < c1’ < c2
(to next slide)

## Slide 40: Double-Sampling Plan
(c1’ + c2’) > c2
N – n1 Items
Random
Sample of
n2 Items
N – (n1 + n2)
Items
Inspect n2 Items
Replace
Defectives
n2 Nondefectives
c2’ Defectives
Found in Sample
Reject Lot
Accept Lot
Continue
(c1’ + c2’) < c2
(from previous slide)

## Slide 41: Sequential-Sampling Plan
Units are randomly selected from the lot and tested one by one.
After each one has been tested, a reject, accept, or continue-sampling decision is made.
Sampling process continues until the lot is accepted or rejected.

## Slide 42: Sequential-Sampling Plan
0 10 20 30 40 50 60 70 80 90 100 110 120 130
3
1
2
Units Sampled (n)
6
Number of Defectives
4
5
7
0
Reject Lot
Accept Lot
Continue Sampling

## Slide 43: Definitions
Acceptance plan - Sample size (n) and maximum number of defectives (c) that can be found in a sample to accept a lot
Acceptable quality level (AQL) - If a lot has no more than AQL percent defectives, it is considered a good lot
Lot tolerance percent defective (LTPD) - If a lot has greater than LTPD, it is considered a bad lot

## Slide 44: Definitions
Average outgoing quality (AOQ) – Given the actual % of defectives in lots and a particular sampling plan, the AOQ is the average % defectives in lots leaving an inspection station
Average outgoing quality limit (AOQL) – Given a particular sampling plan, the AOQL is the maximum AOQ that can occur as the actual % defectives in lots varies

## Slide 45: Definitions
Type I error - Based on sample information, a good (quality) population is rejected
Type II error - Based on sample information, a bad (quality) population is accepted
Producer’s risk (a) - For a particular sampling plan, the probability that a Type I error will be committed
Consumer’s risk (b) - For a particular sampling plan, the probability that a Type II error will be committed

## Slide 46: Considerations in Selecting a Sampling Plan
Operating characteristics (OC) curve
Average outgoing quality (AOQ) curve

## Slide 47: Operating Characteristic (OC) Curve
An OC curve shows how well a particular sampling plan (n,c) discriminates between good and bad lots.
The vertical axis is the probability of accepting a lot for a plan.
The horizontal axis is the actual percent defective in an incoming lot.
For a given sampling plan, points for the OC curve can be developed using the Poisson probability distribution

## Slide 48: Operating Characteristic (OC) Curve
.10
.20
.30
.40
.50
.60
.70
.80
.90
Probability of Accepting the Lot
0 5 10 15 20 25
1.00
% Defectives
in Lots
AQL = 3%
LTPD = 15%
Consumer’s Risk (b) = 8.74%
Producer’s Risk (a) = 3.67%
n = 15, c = 0

## Slide 49: OC Curve (continued)
Management may want to:
  Specify the performance of the sampling procedure by identifying two points on the graph:
    AQL and a
    LTPD and b
  Then find the combination of n and c that provides a curve that passes through both points

## Slide 50: Average Outgoing Quality (AOQ) Curve
AOQ curve shows information depicted on the OC curve in a different form.
Horizontal axis is the same as the horizontal axis for the OC curve (percent defective in a lot).
Vertical axis is the average quality that will leave the quality control procedure for a particular sampling plan.
Average quality is calculated based on the assumption that lots that are rejected are 100% inspected before entering the production system.

## Slide 51: AOQ Curve
Under this assumption,
      AOQ = p[P(A)]/1
where: p = percent defective in an incoming lot
P(A) = probability of accepting a lot is
obtained from the plan’s OC curve
As the percent defective in a lot increases, AOQ will increase to a point and then decrease.

## Slide 52: AOQ Curve
AOQ value where the maximum is attained is referred to as the average outgoing quality level (AOQL).
AOQL is the worst average quality that will exit the quality control procedure using the sampling plan n and c.

## Slide 53: Computers in Quality Control
Records about quality testing and results limit a firm’s exposure in the event of a product liability suit.
Recall programs require that manufacturers
  Know the lot number of the parts that are responsible for the potential defects
  Have an information storage system that can tie the lot numbers of the suspected parts to the final product model numbers
  Have an information system that can track the model numbers of final products to customers

## Slide 54: Computers in Quality Control
With automation, inspection and testing can be so inexpensive and quick that companies may be able to increase sample sizes and the frequency of samples, thus attaining more precision in both control charts and acceptance plans

## Slide 55: Quality Control in Services
In all services there is a continuing need to monitor quality
Control charts are used extensively in services to monitor and control their quality levels

## Slide 56: Wrap-Up: World-Class Practice
Quality cannot be inspected into products. Processes must be operated to achieve quality conformance; quality control is used to achieve this.
Statistical control charts are used extensively to provide feedback to everyone about quality performance
. . . more

## Slide 57: Wrap-Up: World-Class Practice
Where 100% inspection and testing are impractical, uneconomical, or impossible, acceptance plans may be used to determine if lots of products are likely to meet customer expectations.
The trend is toward 100% inspection and testing; automated inspection and testing has made such an approach effective and economical.

## Slide 58
End of Chapter 17