## Slide 1
Stage-Gate Process & Qualify Function Deployment
Rev: Dec, 2012
POSTECH Strategic Management of Information and Technology Laboratory
(POSMIT: http://posmit.postech.ac.kr)
Dept. of Industrial & Management Engineering POSTECH

## Slide 2: Stage-Gate Process (1/4)
Stage-Gate Process
  Introduced by Robert G. Copper in 1990
  Conceptual and operational road map for moving a new-product project from idea to launch
  Blueprint for managing the new-product process to improve effectiveness and efficiency
Generic flow of the Stage-Gate Process
  Stages
    Stages are where cross-functional action occurs: There is no R&D or marketing stage
    Each stage consists of a set of parallel activities undertaken by people from different functional areas in the firm, working together as a team and led by a project team leader
  Gates
    At the entrance to each stage is a gate, which serves as the quality control and Go/Kill check point in the process
Idea
Gate
1
Idea Screen
Stage 1
Gate
2
Second
Screen
Stage 2
Gate
3
Decision
to Develop
Stage 3
Gate
4
Decision to Test
Stage 4
Gate
5
Decision to Launch
Stage 5
$
Scoping
Building Business case
Development
Testing &
Validation
Launch
Post-Launch
Review

## Slide 3: Stage-Gate Process (2/4)
Stage 1: Scoping
  A quick investigation and sculpting of the project
Stage 2: Building business case
  The detailed homework and up-front investigation work leading to a business case; a defined product, a business justification and a detailed plan of action for the next stages
Stage 3: Development
  The actual design and development of the new product
  The manufacturing (or operations) process is mapped out, the marketing launch and operating plans are developed, and the test plans for the next stage are defined
Stage 4: Testing and validation
  The verification and validation of the proposed new product, its marketing and production
Stage 5: Launch
  Full commercialization of the product - the beginning of full production and commercial launch and selling
Discovery
Stage
Gate
1
Idea
Screen
Stage 1
Gate
2
Second
Screen
Stage 2
Gate
3
Decision
to Develop
Stage 3
Gate
4
Decision to Test
Stage 4
Gate
5
Decision to Launch
Stage 5
$
Scoping
Building Business Case
Development
Testing &
Validation
Launch
Post-Launch
Review

## Slide 4: Stage-Gate Process (3/4)
Common roles of gate
  Quality-control checkpoints: Checking whether this project is being executed in a quality fashion
  Go/Kill and prioritization decision points: Gates provide the funnels where mediocre projects are successively culled out
  Path forward for the next stage decision points: Gate meetings are usually staffed by senior managers from different functions, who own the resources the project leader and team require for the next stage
Common formats related to each gate
  Criteria (input): Questions or metrics on which the project is judged in order to make the Go/Kill and prioritization decision
  Decision (output): Results of the gate review - a decision (Go/Kill/Hold/Recycle)
  Approved action plan (output): Date and deliverables for the next gate
Gate
1
Idea
Screen
Stage 1
Gate
2
Second
Screen
Stage 1
Gate
3
Decision
to Develop
Stage 3
Gate
4
Decision to Test
Stage 4
Gate
5
Decision to Launch
Stage 5
Preliminary Investigation
Detailed
Investigation
Development
Testing &
Validation
Launch
Discovery
Stage
$
Post-Launch
Review

## Slide 5: Stage-Gate Process (4/4)
Action items of each stage and gate in Stage-Gate process
Stage/Gate | Action Items
Gate 1. Idea Screen | • Does the idea merit any work?
Stage 1. Scoping | • Prelim market assessment • Prelim technical assessment • Prelim financial & business assessment • Action plan for Stage 2
Gate 2. Second Screen | • Does the idea justify extensive investigation?
Stage 2. Building Business Case | • User needs & wants study • Competitive analysis • Value proposition defined • Technical feasibility assessment • Operations assessment • Product Definition
Gate 3. Decision to Develop | • Is the business case sound?
Stage 3. Development | • Technical development work • Rapid prototypes • Initial customer feedback • Prototype development • In-house product testing • Operations process development • Full launch & operations plans
Gate 4. Decision to Test | • Should the project be moved to external testing?
Stage 4. Testing & Validation | • Extend in-house testing • Customer field trials • Acquisition of production equipment • Production/operation trials • Test market/trial sell • Finalized launch and operations plans • Post-launch & life cycle plans
Gate 5. Decision to Launch | • Is the product ready for commercial launch?
Stage 5. Launch | • Market launch & roll-out • Full production/operations • Selling begin • Results monitoring • Post-Launch & life cycle plans under way

## Slide 6: Quality Function Deployment (1/6)
Quality Function Deployment (QFD)
  Method to transform user demands into design quality, to deploy the functions forming quality, and to deploy methods for achieving the design quality into subsystems and component parts, and ultimately to specific elements of the manufacturing process
  Developed by Yoji Akao in 1966

## Slide 7: Quality Function Deployment (2/6)
Benefits of QFD
  Customer Driven
    Creates Focus On Customer Requirements
    Uses Competitive Information Effectively
    Prioritizes Resources
    Identifies Items That Can Be Acted On
    Structures Resident Experience/Information
  Reduces Implementation Time
    Decreases Midstream Design Change
    Limits Post Introduction Problems
    Avoids Future Development Redundancies
    Identifies Future Application Opportunities
    Surfaces Missing Assumptions

## Slide 8: Quality Function Deployment (3/6)
Benefits of QFD (Cont’d)
  Promotes Teamwork
    Based On Consensus
    Creates Communication At Interfaces
    Identifies Actions At Interfaces
    Creates Global View-Out Of Details
  Provides Documentation
    Documents Rationale For Design
    Is Easy To Assimilate
    Adds Structure To The Information
    Adapts To Changes (Living Document)
    Provides Framework For Sensitivity Analysis

## Slide 9: Quality Function Deployment (4/6)
Voice of the Customer
  Driving Force Behind QFD
    Customer Dictates Attributes Of Product
  Customer Satisfaction
    Meeting Or Exceeding Customer Expectations
    Customer Expectations Can Be Vague & General In Nature
    Customer Expectations Must Be Taken Literally, Not Translated Into What The Organization Desires
Collecting Customer Information
  What Does Customer Really Want?
  What Are Customer’s Expectations?
  Are Customer’s Expectations Used To Drive Design Process?
  What Can Design Team Do To Achieve Customer Satisfaction?

## Slide 10: Quality Function Deployment (5/6)
House of Quality
  Introduced by John R. Hauser and Don Clausing in 1988
Technical Descriptors
(Voice of the organization)
Prioritized Technical
Descriptors
Interrelationship
between
Technical Descriptors
Customer Requirements
(Voice of the Customer)
Prioritized Customer
Requirements
Relationship between
Requirements and Descriptors

## Slide 11: Quality Function Deployment (6/6)
Building A House Of Quality
  List Customer Requirements (What’s)
  List Technical Descriptors (How’s)
  Develop Relationship (What’s & How’s)
  Develop Interrelationship (How’s)
  Competitive Assessments
  Prioritize Customer Requirements
  Prioritize Technical Descriptors

## Slide 12: QFD Matrix
Absolute Weight and Percent
Prioritized Technical Descriptors
Degree of Technical Difficulty
Relative Weight and Percent
Target Value
Customer Requirements
Prioritized Customer
Requirements
Technical Descriptors
Primary
Primary
Secondary
Secondary
Technical
Competitive
Assessment
Customer
Competitive
Assessment
Our
A’s
B’s
Customer Importance
Target Value
Scale-up Factor
Sales Point
Absolute Weight
Our
A’s
B’s
Relationship between
Customer Requirements and
Technical Descriptors
WHATs vs. HOWs
Strong
Medium
Weak
+9
+3
+1
Strong Positive
Positive
Negative
Strong Negative
+9
+3
-3
-9
Interrelationship between
Technical Descriptors
(correlation matrix)
HOWs vs. HOWs

## Slide 13: Customer Requirements (What’s)
Customer Requirements
(WHATs)
Primary
Secondary
Tertiary

## Slide 14: Technical Descriptors (How’s)
Technical Descriptors
(HOWs)
Primary
Secondary
Tertiary

## Slide 15: L - Shaped Diagram
Customer Requirements
Technical Descriptors
Primary
Primary
Secondary
Secondary

## Slide 16: Relationship Matrix
Customer
Requirements
Technical Descriptors
Primary
Primary
Secondary
Secondary
Relationship between
Customer Requirements and
Technical Descriptors
WHATs vs. HOWs
Strong
Medium
Weak
+9
+3
+1

## Slide 17: Correlation Matrix
Customer Requirements
Technical Descriptors
Primary
Primary
Secondary
Secondary
Relationship between
Customer Requirements and
Technical Descriptors
WHATs vs. HOWs
Strong Positive
Positive
Negative
Strong Negative
+9
+3
-3
-9
Interrelationship between Technical
Descriptors (correlation matrix)
HOWs vs. HOWs
Strong
Medium
Weak
+9
+3
+1

## Slide 18: Customer Competitive Assessment
Customer Requirements
Customer
Competitive
Assessment
Ours
A’s
B’s
5
3
1
2
5
1
4
4
Relationship between
Customer Requirements and
Technical Descriptors
WHATs vs. HOWs
Strong
Medium
Weak
+9
+3
+1

## Slide 19: Technical Competitive Assessment
1 3 4 2
1 2 1 4
Customer Requirements
Customer
Competitive
Assessment
Our
A’s
B’s
5
3
1
2
5
1
4
4
Relationship between
Customer Requirements and
Technical Descriptors
WHATs vs. HOWs
Strong
Medium
Weak
+9
+3
+1
Technical
Competitive
Assessment
Our
A’s
B’s

## Slide 20
7
3
9
10
2
4
8
1
Customer Requirements
Prioritized Customer
Requirements
Technical Descriptors
Primary
Primary
Secondary
Secondary
Technical
Competitive
Assessment
Customer
Competitive
Assessment
Our
A’s
B’s
Customer Importance
Target Value
Scale-up Factor
Sales Point
Absolute Weight
1 3 4 2
1 2 1 4
5
3
1
2
5
1
4
4
5
3
2
3
5
2
4
4
1.5
1
1.2
1.5
1
1
1.5
1
1.5
1
15
3
Our
A’s
B’s
Relationship between
Customer Requirements and
Technical Descriptors
WHATs vs. HOWs
Strong
Medium
Weak
+9
+3
+1

## Slide 21
Absolute Weight and Percent
Prioritized Technical Descriptors
Degree of Technical Difficulty
Relative Weight and Percent
Target Value
1 8 4 2
9 8 2 5
90
133
2 3 4 3
1 3 1 5
7
3
9
10
2
4
8
1
Customer Requirements
Prioritized Customer
Requirements
Technical Descriptors
Primary
Primary
Secondary
Secondary
Technical
Competitive
Assessment
Customer
Competitive
Assessment
Our
A’s
B’s
Customer Importance
Target Value
Scale-up Factor
Sales Point
Absolute Weight
1 3 4 2
1 2 1 4
5
3
1
2
5
1
4
4
5
3
2
3
5
2
4
4
1.5
1
1.2
1.5
1
1
1.5
1
1.5
1
15
3
Our
A’s
B’s
Relationship between
Customer Requirements and
Technical Descriptors
WHATs vs. HOWs
Strong
Medium
Weak
+9
+3
+1
Strong Positive
Positive
Negative
Strong Negative
+9
+3
-3
-9
Interrelationship between
Technical Descriptors
(correlation matrix)
HOWs vs. HOWs

## Slide 23: QFD Process
WHATs
HOW MUCH
HOWs
WHATs
HOW MUCH
HOWs

## Slide 24: Phase I Product Planning
Design
Requirements
Customer
Requirements

## Slide 25: Phase II Part Development
Part Quality
Characteristics
Design
Requirements

## Slide 26
Phase III Process Planning
Key Process
Operations
Part Quality
Characteristics

## Slide 27
Phase IV Production Planning
Production
Requirements
Key Process
Operations
Production Launch

## Slide 28: QFD Summary
Orderly Way Of Obtaining Information & Presenting It
Shorter Product Development Cycle
Considerably Reduced Start-Up Costs
Fewer Engineering Changes
Reduced Chance Of Oversights During Design Process
Environment Of Teamwork
Consensus Decisions
Preserves Everything In Writing

## Slide 29
Beyond the House
Setting target value for closing energy gives us a goal, but not a door.
To get the door, we need the right parts, the right process to manufacture the parts and assemble the product, and the right production plan to get it built.
If our team is truly interfunctional, we can eventually take the “hows” from our house of quality and make them the “whats” of another house.