## Slide 1: Introduction to Quality of Service
Klara Nahrstedt
CS 538

## Slide 2: Distributed Multimedia Applications
Image/Video
Capture
Image/Video Information
Representation
Media
Server
Storage
Transmission
Compression
Processing
Audio/Video
Presentation
Playback
Audio/Video
Perception/ Playback
Audio Information
Representation
Transmission
Audio
Capture
A/V
Playback

## Slide 3: Distributed Multimedia Applications
Image/Video
Capture
Image/Video Information
Representation
Media
Server
Storage
Transmission
Compression
Processing
Audio/Video
Presentation
Playback
Audio/Video
Perception/ Playback
Audio Information
Representation
Transmission
Audio
Capture
A/V
Playback

## Slide 4: Distributed Multimedia Applications
Image/Video
Capture
Image/Video Information
Representation
Media
Server
Storage
Transmission
Compression
Processing
Audio/Video
Presentation
Playback
Audio/Video
Perception/ Playback
Audio Information
Representation
Transmission
Audio
Capture
A/V
Playback

## Slide 5: Distributed Multimedia Applications
Image/Video
Capture
Image/Video Information
Representation
Media
Server
Storage
Transmission
Compression
Processing
Audio/Video
Presentation
Playback
Audio/Video
Perception/ Playback
Audio Information
Representation
Transmission
Audio
Capture
A/V
Playback

## Slide 6: Multimedia Distributed System and Network
Network
MM
Application
OS/Distributed
Systems/Network
MM
Application
OS/DS/Network
Sender/Server
Receiver/Client
Capture AV
Code AV
Display AV
Decode AV
Stream AV, Sync AV, Schedule AV,
Queue/Buffer AV, Shape AV,
Manage AV, Route AV, Retrieve AV,
Pre-fetch/Cache AV, Record AV

## Slide 7: AV Requirements: Real-Time and Multimedia
Difference between RT requirements for traditional RT systems and Multimedia systems
  Soft deadlines versus hard deadlines
  Periodic behavior versus random behavior
  Bandwidth requirements

## Slide 8: AV Requirements on MM Systems and Networks (1)
Transport system – guaranteed delivery with respect to metrics such as delay, reliability, bandwidth requirements
OS process management – real-time processing of continuous data, communication and synchronization between processes/ threads

## Slide 9: AV Requirements on MM Systems and Networks (2)
Memory/Buffer management – guaranteed timing delay and efficient data manipulation
File system/Media Servers – transparent and guaranteed continuous retrieval of audio/video
Device management – integration of audio and video

## Slide 10: Result of AV Requirements
Need Resource Management to coordinate
  Transport/Network Resources,
  CPU/OS Resources
  Memory/Buffer Resources
  Storage/Disk Resources
  Device Resources

## Slide 11: Resource Management (Why do we need resource management?)
Limited capacity in digital distributed systems despite data compression and usage of new technologies
Need adherence for processing of continuous data by every hardware and software component along the data path
Competition for resources exist in an integrated multimedia system

## Slide 12: Window of Resources
Network
File access
High-quality
Audio
HDTV
Interactive
HDTV-quality
multi-view video
abundant
Sufficient
Sufficient but
Scarce to
Sufficient
Insufficient -
Sufficient
But scarce
1980
1990
2000
insufficient
Sufficient
But scarce
insufficient
2010
2020
Sufficient
To
abundant
abundant
insufficient
sufficient
Requirements
Hardware
support

## Slide 13: Quality of Service (How to parameterize services?)
To manage resources, we need services over resources
  to schedule AV data, to shape access for AV data, to process AV data, to move AV data, etc.
Multimedia systems consist of set of AV-specific services
  Processing (media-related) services: retrieve audio/video, record video/audio, compress audio/video, fast forward video, rewind video
  Transport (network) services: Stream video, fast forward video, rewind video
To provide multimedia services, services get parameterized with quality levels called Quality of Service
QoS parameters versus performance metrics!!

## Slide 14: Layered Model for QoS
Quality of
Experience
Quality of
Service

## Slide 15: Application AV QoS Parameters
QoS for Audio service:
    Sample rate – 8000 samples/second (8KHz), 44.1 KHz
    Sample resolution – 8 bits per sample, 16 bits per sample
QoS for Video service:
    Video frame rate – 25 frames per second, 30 frames per second
    Frame Period – 40 ms, 30 ms, 25 ms, …
    Frame resolution – 320x240 pixels, 640x480 pixels, 1920x1080 pixels, …
    Pixel resolution – 24 bits per pixel, 8 bits per pixel
    Frame size – 64KB
    Compression rate – 8:1

## Slide 16: Network QoS
Bandwidth – Rate of data transfer, Bit Rate
      e.g., 1 Gbps (Ethernet throughput) – level 1
      e.g., 100 Mbps (WiFi throughput) – level 2
      e.g., 128 kbps (ISDN throughput) – level 3
  measured in bits per second
Throughput – rate of successful message delivery over communication channel
  Measured in packets per second, data packets per time slot, or bits per second
      30 packets per second; 128 kbps, 10 packets per time slot

## Slide 17: Network QoS
Connection setup time
      time how long it take to connect the sender and receiver
      e.g., 50 ms, 10 ms, …
Error Rate
  Measures the total number of bits (packets) that were corrupted or incorrectly received compared with the total number of transmitted bits (packets)
    Bit Error Rate (BER) – at physical/MAC layer
      In fiber optics, bit error rate (BER) is of the order of 10-8 to 10-12.
      In satellite networks, BER is of the order 10-7
    Packet Error Rate (PER) – at IP/transport/application layer – also called Packet Loss Rate

## Slide 18: Network QoS
Delay
  Latency
    End-to-end delay in telecommunication
  Response time
    Round-trip delay in telecommunication
End-to-End Delay
      time interval from the time packet is sent from the sender until the time it is received at the receiver (Treceive – Tsend)
      e.g., 80 ms, 100 ms, 160 ms

## Slide 19: Network QoS
Response Time
  Measured as round-trip delay and is the total time required for sender to send a packet and receive an acknowledgement from the receiver. It can be described as sum of network delay and interface delay.
    Network delay – composed of transit delay and transmission delay
      Transit delay is caused by time needed to send data on a physical connection between sender and receiver
      Transmission delay is time needed to transmit packet through network as result of processing delays (e.g., look up routing tables)
    Interface delay – incurred between the time a sender is ready to begin sending and the time a network is ready to accept and transmit the data (due to traffic policing and shaping)

## Slide 20: Network QoS
Jitter
  Undesired deviation from true periodicity in telecommunication
    Also called packet delay variation – important QoS factor in assessment of network performance
Packet jitter
  Variation in latency as measured in the variability over time of the packet latency across network.

## Slide 21: Conclusion
QoS – an important concept in multimedia systems
Very different types of QoS parameters and values
Important relation between QoS and Resources
Need to understand operations on QoS and their impact on resource management