## Slide 1: Embedded and Cyber-Physical Systems in a Nutshell
Peter Marwedel
Technische Universitat Dortmund, Dortmund, Germany
Presented by:
Yogesh Sur
CS ID: ysur@cs.odu.edu

## Slide 2: About the Author
Prof. Dr. Peter Marwedel - Head of Design Automation for Embedded Systems Group at Technische Universitat Dortmund
CURRENT RESEARCH ACTIVITIES
WCET-aware Compilation
Source Code Optimization Techniques for Data Flow Dominated Embedded Software
Memory architecture aware compilation
Mapping of applications to multiprocessor systems
Resource Constraint Computing
Dependable Embedded Real-Time Systems

## Slide 3: Abstract
This article presents a brief overview of key topics for research and development in embedded systems. Following a hypothetical design flow, special characteristics of embedded/cyber-physical systems with respect to specification techniques and modeling, embedded hardware, standard software, evaluation and validation, mapping of applications to execution platforms, optimizations and testing are presented.

## Slide 4: Key Terms
Embedded Systems: Information processing systems embedded into enclosing products.
Examples: Systems with real-time constraints and efficiency requirements like automobiles, telecommunication or fabrication equipment
Cyber-Physical Systems: Integrations of computation and physical processes.
Example: Networked systems of embedded computers linking together a range of devices and sensors for information sharing

## Slide 5: Index
Introduction
Specification and Modeling
Embedded System Hardware
Standard Software
Evaluation and Validation
Mapping of Applications to Execution Platforms
Optimization
Testing
My views on the paper
References

## Slide 6: Introduction
Introduction
  Difference between Embedded and Cyber-Physical System
  Simplified Design Flow
Specification and Modeling
Embedded System Hardware
Standard Software
Evaluation and Validation
Mapping of Applications to Execution Platforms
Optimization
Testing
My views on the paper
References

## Slide 7: Difference between Embedded and Cyber-Physical System
Embedded system is system integrated with physical processes. The technical problem is managing time and concurrency in computational systems.
However, the link to physics has recently been stressed even more by the introduction of the term “cyber-physical systems”.
The new term emphasizes the link to physical quantities such as time, energy and space since it is frequently ignored in a world of applications running on PCs
The new term encompasses most embedded systems
The article uses the two terms interchangeably.

## Slide 8: Simplified Design Flow
The structure of this article follows a hypothetical, generic design flow, as shown
There should be ideas that incorporate knowledge about application area
These ideas must be captured in a design specification
Standard hardware and system software components are available and should be reused whenever possible

## Slide 9: Simplified Design Flow
In this diagram, boxes with rounded corners for stored information, and rectangles for transformations on data
In particular, information is stored in the design repository that allows keeping track of design models using which design decisions can be taken in an iterative fashion
At each iteration, design model information must be retrieved, considered and evaluated for mapping to hardware devices
New design is generated using applicable optimizations

## Slide 10: Specification and Modeling
Introduction
Specification and Modeling
  Models
  Early Design Phases
  Communicating Finite State Machines
  Data flow
  Petri nets
  Discrete event based languages
  Von Neumann languages
  Comparing different models of communication
Embedded System Hardware
Standard Software
Evaluation and Validation
Mapping of Applications to Execution Platforms
Optimization
Testing
My views on the paper
References

## Slide 11: Models
Models of computation (MoCs) describe simplified mechanism for performing computations. These include components like procedures, processes, functions, finite state machines etc
Components are strictly different from communication protocols. Protocols describe methods for communication between components

## Slide 12: Early Design Phases
Description of the system under design (SUD) should be encoded in the format of some word processor and stored by a tool managing design documents.
Eg. DOORS®[IBM10]
Use cases describe possible applications of the SUD. For use cases, there is neither a precisely specified model of the computations nor communication.
At a detailed level, the sequences of messages are exchanged between components in SUD using Sequence charts (SCs)
Sequence charts use one dimension of a 2-dimensional chart to denote sequences and the second dimension to reflect the different communicating components

## Slide 13: Communicating Finite State Machines
If we start to represent our SUD at a more detailed level, we need Finite state machines (FSMs). Figure 2 shows an example of a classical state diagram, representing an FSM
Communicating finite state machines (CFSMs) denotes several FSMs communicating with each other
In order to model time, classical FSMs have been extended to also include timing information. Timed automata extend classical automata with timing information
But timed automata does not provide hierarchy and concurrency

## Slide 14: Communicating Finite State Machines
StateCharts extend classical automata describing hierarchy and concurrency
Hierarchy is introduced by means of super-states
States comprising other states are called super-states
States included in super-states are called sub-states of the super-states

## Slide 15: Communicating Finite State Machines
Hierarchical State Diagram:
Super-state S includes states A,B,C,D and E
Suppose the FSM is in state Z. Now, if input m is applied to the FSM, then A and S will be the new active states
If the FSM is in S and input k is applied, then Z will be the new active state, regardless of whether the FSM is in sub-states A,B,C,D or E of S
All states contained in S are non-hierarchical states
In general, sub-states of S could again be super-states consisting of sub-states themselves.
Also, whenever a sub-state of some super-state is active, the super-state is active as well.

## Slide 16: Communicating Finite State Machines
Hierarchical State Diagram with Concurrency
To describe concurrency, State-Charts provide a second class of super-states, so called AND-states
Super-states S are called AND-super-states if the system containing S will be in all of the sub-states of S whenever it is in S
In the figure, two concurrent sub-states U and V are shown separated by a dashed line
When in state Z, an input of m will cause a transition into simple states A and F and into hierarchical states S, U and V
Whenever the system is in state S, it will be in states U and V as well
Whenever the system leaves U, it will leave V as well

## Slide 17: Communicating Finite State Machines
In StateCharts, Variables are assumed to be globally accessible
This means that StateCharts can be implemented easily for shared memory-based platforms
Less appropriate for message passing and distributed systems

## Slide 18: Data flow
It is the process of identifying, modeling and documenting how data moves around an information system
A data flow program is specified by a directed graph where the nodes (vertices), called actors, represent computations and the arcs represent communication channels
Synchronous data flow (SDF) are based on the assumption that all actors execute in a single clock cycle
SDF are not Turing complete
Turing machines are used as the standard model of universal computers

## Slide 19: Data Flow
Kahn process networks (KPN) allow actors to execute with any finite delay
KPNs are very powerful: they are Turing complete

## Slide 20: Petri nets
Model only control and control dependencies
Focus on the modeling of causal dependencies
Do not assume any global synchronization and are therefore especially suited for modeling distributed systems
Key Elements:
Conditions, events and a flow relation are the key elements of Petri nets
Conditions are either satisfied or not satisfied
Events can happen
The flow relation describes the conditions that must be met before events can happen

## Slide 21: Discrete Event Based Languages
Based on the idea of firing (or executing) a sequence of discrete events
Firings are resulting in actions
Actions comprise the generation of events like the assignment of values to variables
Firings are the result of internally or externally generated events which are sorted by the time at which they should be processed
Hardware description languages (HDLs) are designed to model hardware

## Slide 22: Von Neumann Languages
The von Neumann model of sequential execution in combination with some communication technique is called MoC
But it has some problems for embedded systems:
Facilities to describe timing are lacking
Based on accesses to globally shared memory. So mutual exclusion should be guaranteed
However libraries extend these languages such that they can be used to model concurrency and communication

## Slide 23: Comparing different models of communication
There is no single “ideal” model of computation
In general, more powerful models are less analyzable
Absence of deadlocks can be shown for SDF models, but not for general von Neumann models
Designers must be made aware of advantages and limitations of certain models before selecting design tools

## Slide 24: Embedded System Hardware
Introduction
Specification and Modeling
Embedded System Hardware
Hardware in a loop
Sensors
Discretization
Processing units
D/A-conversion
Output
Secure hardware
IV. Standard Software
V. Evaluation and Validation
VI. Mapping of Applications to Execution Platforms
VII. Optimization
VIII. Testing
IX. My views on the paper
X. References

## Slide 25: Hardware in a loop
In many cyber-physical systems, hardware is used in a loop
Information about the physical environment is made available through sensors
Typically, sensors generate continuous sequences of analog values
Sample-and-hold-circuits and analog-to-digital (A/D) converters convert analog signals to discrete sequences of values
After such conversion, information can be processed digitally
Generated results can be displayed and also used to control the physical environment through actuators

## Slide 26: Sensors
A wide variety of physical effects can be exploited in the construction of sensors
There are sensors for weight, velocity, acceleration, electrical current, voltage, temperature, etc

## Slide 27: Discretization
Sample-and-hold circuits are used to convert continuous domain signals into the discrete domain
Circuit consists of a clocked transistor and a capacitor
Transistor operates like a switch
When switch is closed by the clock signal, the capacitor is charged so that its voltage h(t) is practically the same as the incoming voltage e(t)
After opening the switch again, this voltage will remain essentially unchanged until the switch is closed again
Each of the values stored on the capacitor can be considered as an element of a discrete sequence of values h(t)

## Slide 28: Processing Units
Currently available embedded systems require electrical energy to operate
Energy efficiency and flexibility in programming a processing unit are conflicting goals
Application-specific integrated circuits (ASICs): Their energy efficiency is largest
Processors: Application domain-specific processors (such as DSPs) and application-specific instruction set processors (ASIPs) can provide high energy efficiency
FPGAs: Reconfigurable logic provides a solution if algorithms can be efficiently implemented in custom hardware. Neither expensive like ASICs nor slow or energy-consuming like software based solutions

## Slide 29: Processing Units
4. Communication: Various components in an embedded system must be able to communicate.
For all systems that need to met real-time constraints, communication times must also be guaranteed. For example, time-division multiple-access (TDMA) is an efficient technique to set communication times
Efficiency of communication hardware is frequently an issue. So, power may need to be distributed via the communication medium

## Slide 30: D/A-conversion
Digital information must first be converted by digital-to-analog (D/A) converters.
A standard design uses weighted resistors to generate a current which is proportional to the digital number.
This current is then turned into a proportional voltage by using an operational amplifier

## Slide 31: Output
Output devices of embedded/cyber-physical systems include displays and electro-mechanical devices
The latter are called actuators
Actuator is a mechanism that puts something into automatic action

## Slide 32: Secure Hardware
May need to be guaranteed for communication and for storage
Security might demand special equipment(hardware security modules) for the generation of cryptographic keys

## Slide 33: Standard Software
Introduction
Specification and Modeling
Embedded System Hardware
Standard Software
Embedded Operation Systems
Real-time Operating Systems
Middleware
V. Evaluation and Validation
VI. Mapping of Applications to Execution Platforms
VII. Optimization
VIII. Testing
IX. My views on the paper
X. References

## Slide 34: Embedded Operation Systems
Standard software components that can be reused include system software components such as embedded operating systems (OS), real-time databases, and other forms of middleware
Scheduling, task switching, and I/O require the support of an operating system suited for embedded applications
Embedded operating systems should provide a high level of configurability

## Slide 35: Real-time operating systems
Real-time operating system is an operating system that supports the construction of real-time systems
The timing behavior of the OS must be predictable
In particular, the scheduling policy of RTOS’s must be deterministic
The OS must manage the scheduling of tasks based on execution time or priority

## Slide 36: Middleware
Any software in between the operating system and the application software is called middleware
Communication software may be the most important type of middleware

## Slide 37: Evaluation and Validation
Introduction
Specification and Modeling
Embedded System Hardware
Standard Software
Evaluation and Validation
Definition
Multi-objective Optimization
Execution Time
VI. Mapping of Applications to Execution Platforms
VII. Optimization
VIII. Testing
IX. My views on the paper
X. References

## Slide 38: Definition
Validation is the process of checking whether or not a certain (possibly partial) design is appropriate for its purpose, meets all constraints, and will perform as expected
Evaluation is the process of computing quantitative information of some key characteristics (or “objectives”) of a certain (possibly partial) design.

## Slide 39: Multi-objective Optimization
Consider an m-dimensional space X. Dimensions reflect objectives
For this space X, we define an n-dimensional function
  which evaluates designs with respect to several criteria or objectives
Let S belonging to F be a subset of vectors in the objective space. V belonging to F is called a non-dominated solution with respect to S if there does not exist any element w belonging to S such that w is not worse than v with respect to any objective and better than v with respect to at least one objective

## Slide 40: Multi-objective Optimization
Different areas in the objective space, relative to design point
Figure shows a set of Pareto points, i.e., the so-called Pareto front. Design space exploration (DSE) based on Pareto points is the process of finding and returning a set of Pareto-optimal designs to the user, enabling the user to select the most appropriate design.

## Slide 41: Execution Time
The worst-case execution time is the largest execution time of a program for any input and any initial execution state
It is undecidable whether or not the WCET is finite
So upper bounds WCETEST should have properties:
1) The bounds should be safe (WCETEST ≥ WCET)
2) The bounds should be tight (WCETEST – WCET << WCET)

## Slide 42: Mapping of Applications to Execution Platforms
Introduction
Specification and Modeling
Embedded System Hardware
Standard Software
Evaluation and Validation
Mapping of Applications to Execution Platforms
Purpose and Scope
Simple Scheduling Policies
Hardware/Software codesign
VII. Optimization
VIII. Testing
IX. My views on the paper
X. References

## Slide 43: Purpose and Scope
It is a characteristic of embedded systems that both hardware and software have to be considered during their design.
Therefore, this type of design is also called hardware/software codesign

## Slide 44: Simple Scheduling Policies
In earliest deadline first (EDF) scheduling, the task whose deadline is the earliest among all tasks is executed first.
For EDF scheduling, the task to be executed next must be computed dynamically
Rate monotonic scheduling(RMS) schedules according to priorities based on task periods
Violations cannot occur, if
where n is the number of tasks, ci is the execution time of task i and pi is the period of task i. This relation guarantees schedulability

## Slide 45: Hardware/Software codesign
Methods for partitioning applications into functionality mapped to hardware and functionality mapped to software

## Slide 46: VII. Optimization
Software transformations: frequently, software can be transformed such that the generated program can be implemented more efficiently than the original program
Hardware optimizations: Hardware platforms can be optimized for the applications at hand
Runtime optimizations: There are techniques which change the behavior at runtime in order to become more efficient with respect to the objectives considered.

## Slide 47: VIII. Testing
Testing of embedded systems needs special attention for following reasons:
Embedded/cyber-physical systems integrated into a physical environment may be safety-critical.
Testing of timing-critical systems must validate the correct timing behavior. This means that testing only the functional behavior is not sufficient.

## Slide 48: IX. My views on the paper: Pros & Cons
Pros: The article gave me an overview of cyber physical/embedded systems like specification and modeling, hardware-software, evaluation and validation, mapping of applications to platforms, optimization and the special characteristics of embedded system testing
Cons: The section on processing units like DSPs, FPGAs and ASICs focuses on performance GFLOPs/J vs time graph

## Slide 49: X. References
Embedded and Cyber-Physical Systems in a Nutshell, Design and Automation Conference, 2010
[Peter Marwedel]