## Slide 1: Synthesizable, Application-Specific NOC Generation using CHISEL
Maysam Lavasani †, Eric Chung † †, John Davis † † † : The University of Texas at Austin
† †: Microsoft Research
Acknowledgement: Jonathan Bachrach and rest of CHISEL team.
Notes: In case you don’t know chisel.
Chisel is a new hardware description language or as its authors call a hardware generation language based on SCALA.
As processors hit the power wall their energy efficiency becomes a major design requirement. Meanwhile, the required energy for communication is projected to be a major source of power consumption in future CMPs [12]. Customizing NOCs for different applications and even for different input sets of a single application improves the energy efficiency of communication. Such customizations require tools that enable the design space exploration as a first order design consideration. In this research we study the use of such a tool, a hardware generator language (Chisel [1]), for designing customizable NOC. Various NOC configurations are generated using a concise Chisel code and their functionality and performance are tested on FPGA.
We also present a method for input driven NOC customizations in order to save energy. Focusing on a parallel accelerator architecture for K-means clustering algorithm, we leverage the idea of shrinking NOC resources whenever the performance is less sensitive to the resource. Our results show that input driven customization can save considerable NOC power for K-means accelerator traffic. The evaluation of proposed technique, with gate-level accuracy, was only possible because parameterization was a consideration from early stage of the design and also because Chisel facilitates such parameterization effectively.

## Slide 2: Problem/motivation
Goal: Flexible, App-specific NOC Generation
  Accuracy
    Performance
    Power
  Design space exploration
    Supports for parametric design
Available solutions
  C-based software simulation (e.g. Orion) inaccurate
  RTL too low-level
  Bluespec is not free
  Web-based solutions are closed source
This talk: Our experience building NOCs w/ CHISEL
Notes: We believe that customization can improve Network on Chip efficiency, by saving NOC power and/or improving its performance.
The customization can be done either for different applications or different inputs and execution phases within a single application.
Application-directed co-design presents a large design space to explore when changing both the hardware and algorithmic parameters.
To help us build energy-efficient NOCs, we need NOC modeling tools that accurately predict power and performance and can traverse the large design space.
There is a wide spectrum of tools that currently exist for NOC modeling. But, they have limitations making them cumbersome to use for our task.
On one end of the spectrum, we have high-level simulation tools like booksim or Orion. They may predict the performance trends correctly, but experiences showed that their absolute results for power estimation can be off by 5X.
The other end of the spectrum uses low-level hardware description languages that are hard to parameterize and extend.
Also, some researchers used new languages like Bluespec, with high-level constructs for generating hardware for NOC modeling. But Bluespec has costly license fee for industry.
Finally, there are a collection of closed-source options or web-based design tools that lack the API for rapid design space exploration.
We have turned to a new open-source, high level hardware description language called Chisel, which offers the right mix of features to enable our design space exploration.
This talk will provide highlights of our poster that shows (i)an NOC generator, (ii)the useful features of Chisel and (iii)the results we obtained using an FPGA platform for measuring the NoC power and performance. We also show a case for NOC customization for K-means clustering algorithm. We show that in this application there are power saving opportunities because K-means communication and computational requirements change based on the algorithm input.

## Slide 3: Chisel Workflow
Hardware in Chisel
Test-bench code in Scala
Chisel compiler
Verilog code
C++ simulation code
C++ simulation
Functional/Performance results
Synthesis flow
Developed @ UC Berkeley
Open-source
Built on top of Scala
  Object-oriented
  Functional
Verilog simulation
Tool
Input/output
Notes: Chisel is …
Chisel flow is …
Green boxes are tools
Blue boxes are inputs or outputs of the tools
C++ is good for faster simulation

## Slide 4: Network-on-Chip Generator
R
R
R
R
R
R
R
R
R
R
R
R
R
R
Big Router
Small Router
Big Router
Small Router
Customizable Features
  Topology (e.g., mesh, ring, torus)
  Buffer sizes
  Link widths
  Routing
Targeted for
  FPGA (evaluated)
  ASIC (future work)
Fully synthesizable
  Xilinx ISE 13+
Notes: What we mean by NOC generator
Our NOC generator is targeted for both FPGA and ASIC substrates.

## Slide 5: Parameterized Router
Input port
Switch
State
Stored Route
Route logic
RR Arbiter
RR Arbiter
Output port
Output port
Mediator
Mediator
State
State
State
Stored Route
Route logic
Input port
Notes: Blue colors indicates the parametric components which can be set by the user.
The router is a single cycle routing + switching + link traversal.
It is parametric with respect to the number of ports, buffer sizes, routing algorithm, and link width.
Currently the evaluation has been done only for FPGAs.

## Slide 6: 2D Mesh Example in Chisel
val routers =
Range(0, numRows, 1).map(i =>
new Range(0, numColumns, 1).map(j =>
new MyRouter(5, routerID(i, j), XYrouting)))
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
Notes: TODO: Some animation to high-light the part of the code you are talking about
2d Mesh example
Type inferring in both scala and chisel
Functional features.
Object oriented features including parametric classes. Routing function is a parameter.
Bulk connections.
Compile time execution that is why it is
hardware generator
The learning process for Chisel took 2 weeks.
And Router and NOC coding was done in 4 weeks.

## Slide 7: 2D Mesh Example in Chisel
for (i <- 0 until numRows) {
for (j <- 1 until numColumns) {
routers(i)(j).io.ins(south) <> routers(i)(j-1).io.outs(north)
routers(i)(j).io.outs(south) <> routers(i)(j-1).io.ins(north)}}
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
Notes: TODO: Some animation to high-light the part of the code you are talking about
2d Mesh example
Type inferring in both scala and chisel
Functional features.
Object oriented features including parametric classes. Routing function is a parameter.
Bulk connections.
Compile time execution that is why it is
hardware generator
The learning process for Chisel took 2 weeks.
And Router and NOC coding was done in 4 weeks.

## Slide 8: 2D Mesh Example in Chisel
for (j <- 0 until numRows) {
for (i <- 1 until numColumns) {
routers(i)(j).io.ins(west) <> routers(i-1)(j).io.outs(east)
routers(i)(j).io.outs(west) <> routers(i-1)(j).io.ins(east)}}
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
Notes: TODO: Some animation to high-light the part of the code you are talking about
2d Mesh example
Type inferring in both scala and chisel
Functional features.
Object oriented features including parametric classes. Routing function is a parameter.
Bulk connections.
Compile time execution that is why it is
hardware generator
The learning process for Chisel took 2 weeks.
And Router and NOC coding was done in 4 weeks.

## Slide 9: 2D Mesh Example in Chisel
for (i <- 0 until numRows) {
for (j <- 0 until numColumns) {
io.tap(routerID(i, j)).deq <> routers(i)(j).io.outs(cpu)
io.tap(routerID(i, j)).enq <> routers(i)(j).io.ins(cpu)}}
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
Notes: TODO: Some animation to high-light the part of the code you are talking about
2d Mesh example
Type inferring in both scala and chisel
Functional features.
Object oriented features including parametric classes. Routing function is a parameter.
Bulk connections.
Compile time execution that is why it is
hardware generator
The learning process for Chisel took 2 weeks.
And Router and NOC coding was done in 4 weeks.

## Slide 10: 2D Mesh Example in Chisel
val routers = Range(0, numRows, 1).map(i =>
new Range(0, numColumns, 1).map(j =>
new MyRouter(5, routerID(i, j), XYrouting)))
for (j <- 0 until numRows) {
for (i <- 1 until numColumns) {
routers(i)(j).io.ins(west) <> routers(i-1)(j).io.outs(east)
routers(i)(j).io.outs(west) <> routers(i-1)(j).io.ins(east)}}
for (i <- 0 until numRows) {
for (j <- 1 until numColumns) {
routers(i)(j).io.ins(south) <> routers(i)(j-1).io.outs(north)
routers(i)(j).io.outs(south) <> routers(i)(j-1).io.ins(north)}}
for (i <- 0 until numRows) {
for (j <- 0 until numColumns) {
io.tap(routerID(i, j)).deq <> routers(i)(j).io.outs(cpu)
io.tap(routerID(i, j)).enq <> routers(i)(j).io.ins(cpu)}}
Fits on 1 page!
Notes: TODO: Some animation to high-light the part of the code you are talking about
2d Mesh example
Type inferring in both scala and chisel
Functional features.
Object oriented features including parametric classes. Routing function is a parameter.
Bulk connections.
Compile time execution that is why it is
hardware generator
The learning process for Chisel took 2 weeks.
And Router and NOC coding was done in 4 weeks.

## Slide 11: Application Case Study: K-means
Cluster N points in D-dim space into C clusters
N = 12, C = 3, D = 2
Pick C initial centers
Assign N points to nearest center
Compute new centers
Max Iterations or Converge?
Done
Yes
No
Notes: Lets look at an example of using the parametric features of this NOC to design application-specific NOCs
K-means is an iterative data mining algorithm for clustering n points in d dimensional Euclidean space into k clusters.
As shown in figure in each iteration (i)each point is associated with the
closest centroid (ii)each new centroid is calculated by averaging the points associated to a particular centroid.
The new centroids are used as the input to next iteration of algorithm.
The algorithm finishes when association of points to centroids is not changed
across iterations, or the maximum number of iterations is reached.

## Slide 12: Parallel K-means accelerator
Customized Network-on-Chip
Reduction Core
Core (Nearest Distance)
Memory Banks
Streamer DMA
Core (Nearest Distance)
Core (Nearest Distance)
R
R
R
R
R
R
Notes: This figure shows the architecture of an accelerator that consists an streamer component, multiple K-means cores, and a reduction component. I don’t want to go to the details of algorithm but if you are interested come and see my poster.
This figure shows the architecture of an accelerator that consists an streamer component, multiple K-means cores, and a reduction component. I don’t want to go to the details of algorithm but if you are interested come and see my poster.

## Slide 13: Performance Sensitivity to NOC
Chart: K-means and Mesh Performance
| 8 | 16 | 32 | 8 | 16 | 32 | 8 | 16 | 32 | 8 | 16 | 32 | 2 | 6 | 16 | 32
1 | 0.48 | 0.9 | 0.95 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2 | 0.4 | 0.65 | 1.05 | 1.2 | 1.95 | 2 | 2 | 2 | 2 | 2 | 2 | 2
4 | 0.4 | 0.65 | 1.05 | 1.2 | 2 | 3 | 3 | 3.9 | 3.9 | 3.9 | 3.9 | 3.9
Number of Cores
Notes: One of the inputs to K-means is the number of centers. The more centers we have the algorithm is more compute intensive and less sensitive to NOC resources.
This figure shows the performance of K-means accelerator for 2, 6, 16, and 32 centers using one, two, and four cores.
We can see several configurations in which decreasing network width does not affect the performance while saving some power consumption.

## Slide 14: My experience - positives
Chisel (V.1.0) improves productivity
  Bulk interfaces
  Parameterized classes
  Type inference reduces errors
  Functional features
  Faster C++ based simulation
Open source (BSD license)
UCB support
Tested on large-scale UCB projects

## Slide 15: My experience - negatives
Compiler (V.1.0) not as robust as commercial tools
  Long compile time
  Memory leak
  Large circuits loading time
Single clock domain
Cannot mix synthesizable and behavioral code

## Slide 16: Thank you Please come and see my poster
Notes: Please come and see my poster if you are interested in more specific details on
Our experience with chisel or our customized NOC for K-means