## Slide 1
Mohamed Abdelfattah
Vaughn Betz
LYNX:
CAD for FPGA-based Networks-on-Chip

## Slide 2: System-level Interconnect
DDRx Controller
DDRx Controller
PCIe Transcievers
100G Ethernet Controller
A
B
Example Design
FPGA
C
D
Memory
From PCIe
To PCIe
System-Interconnection Tool e.g. Qsys
A
B
C
D
Soft Buses
Bus
module

## Slide 3: Embedded NoCs
Embedded NoC on FPGA
Implement System Communication
Ease Timing Closure (to IOs)
More Efficient than Soft Buses
DDRx Controller
DDRx Controller
PCIe Transcievers
100G Ethernet Controller
Routers
Links
Direct IOLinks
FabricPorts
Easy to Use?
FPGA
General-purpose system interconnect

## Slide 4: Embedded NoCs
Embedded NoC on FPGA
Implement System Communication
Ease Timing Closure (to IOs)
More Efficient than Soft Buses
DDRx Controller
DDRx Controller
PCIe Transcievers
100G Ethernet Controller
Routers
Links
Direct IOLinks
FabricPorts
Easy to Use?
FPGA
General-purpose system interconnect

## Slide 5: NoC Communication
DDRx Controller
DDRx Controller
PCIe Transcievers
100G Ethernet Controller
Easy to Use?
A
D
Example Design
Which Router?
FabricPort Mode?
Data
Packet
Data
FPGA
A
B
C
D
Memory
From PCIe
To PCIe
B
C
Packetize data
Manage traffic

## Slide 6: LYNX CAD Flow
NoC-based System
A
B
C
D
Design
NoC Architecture
Automatically connect design
Satisfy correctness constraints:
  ordering
Optimize performance:
  Throughput
  Latency

## Slide 7: Outline
1. LYNX CAD Flow
How can we automate the use of NoCs?
2. Transaction Communication
How to handle request – reply communication on NoC?
3. Comparison
LYNX + NoC compared to Qsys + Bus

## Slide 8: Outline
1. LYNX CAD Flow
How can we automate the use of NoCs?
2. Transaction Communication
How to handle request – reply communication on NoC?
3. Comparison
LYNX + NoC compared to Qsys + Bus

## Slide 9
CAD
Automatically connect application using NoC
Application’s communication description

## Slide 10
CAD
Classify connection into streaming or transaction

## Slide 11
CAD
Tarjan’s clustering algorithm
Cluster feedback loops to avoid stalls
Intra-cluster connected directly

## Slide 12
CAD
Map modules and clusters to suitable locations on the NoC
Simulated annealing
  Maximize throughput and minimize latency

## Slide 13: NoC Mapping
DDRx Controller
DDRx Controller
PCIe Transcievers
100G Ethernet Controller
FPGA
Width = 150
Routers = 16
VCs = 4
TDM = 4
FabricPort
Router
150 bits
600 bits
1.2 GHz
~ 300 Mhz

## Slide 14: NoC Mapping
DDRx Controller
DDRx Controller
PCIe Transcievers
100G Ethernet Controller
FPGA
Width = 150
Routers = 16
VCs = 4
TDM = 4
FabricPort
Router
150 bits
Module
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
600 bits
16 locations for a 600-bit module

## Slide 15: NoC Mapping
DDRx Controller
DDRx Controller
PCIe Transcievers
100G Ethernet Controller
FPGA
Width = 150
Routers = 16
VCs = 4
TDM = 4
FabricPort
Router
150 bits
1
4
4 x 150 bits
64 locations for a 150-bit module
3
2
1
2
3
4
5
6
7
8
9
10
11
12
14
15
16
13
18
19
20
17
22
23
24
21
26
27
28
25
30
31
32
29
34
35
36
33
38
39
40
37
42
43
44
41
46
47
48
45
50
51
52
49
54
55
56
53
58
59
60
57
62
63
64
61

## Slide 16
CAD
Map modules and clusters to suitable locations on the NoC
Simulated annealing
  Maximize throughput and minimize latency

## Slide 17
CAD
Soft logic wrappers between module and router
  Packetize data (simple)
  Manage traffic (complex)

## Slide 18
CAD
Analyze throughput and latency in NoC
Estimate frequency

## Slide 19
CAD
Java
Open-source
Available at:
eecg.utoronto.ca/~mohamed/lynx
Supports all features of commercial bus-based tools:
Streaming/transaction
E.g.: Uneven arbitration
Challenge: NoC is distributed

## Slide 20: Outline
1. LYNX CAD Flow
How can we automate the use of NoCs?
2. Transaction Communication
How to handle request – reply communication on NoC?
3. Comparison
LYNX + NoC compared to Qsys + Bus

## Slide 21: Streaming Communication
Streaming communication
Point-to-point
data
valid
ready
LYNX automatically generates translators
packet
ready
5
2
dest
vc

## Slide 22: Transaction Communication

## Slide 23: Transaction Communication
Return Address
Request
Reply
Response Unit
Simple FIFO
Buffers return address info.
  Return router
  Return VC

## Slide 24: Transaction Communication
Response Unit
Simple FIFO
Buffers return address info.
  Return router
  Return VC
Traffic Manager
Decides when requests can be issued
1. Traffic Build-Up in Multiple-Master Systems
2. Ordering in Multiple-Slave Systems

## Slide 25: Multiple-Master Systems
Master 1
Master 2
Master 3
Slave
E.g.: Memory

## Slide 26: Multiple-Master Systems
Master 1
Master 2
Master 3
Slave
Buffering
Switching

## Slide 27: Multiple-Master Systems
Master 1
Master 2
Master 3
Slave
Buffering
Switching

## Slide 28: Multiple-Master Systems
Requests accumulate in the interconnect
  Uses much of the buffering
Increases request-reply roundtrip latency
Catastrophic for NoCs – buffering is shared
Master 1
Master 2
Master 3
Slave
Traffic Build-Up

## Slide 29: Multiple-Master Systems
Requests accumulate in the interconnect
  Uses much of the buffering
Increases request-reply roundtrip latency
Catastrophic for NoCs – buffering is shared
Master 1
Master 2
Master 3
Slave
Traffic Build-Up
A
B

## Slide 30: Multiple-Master Systems
Credits Traffic Manager:
  Stalls new requests until reply comes back
  Number of requests = number of credits
  Prevents traffic build-up in NoC
Master 1
Master 2
Master 3
Slave
Credits Traffic Manager
Credits TM
Credits TM
Credits TM

## Slide 31: Credits Traffic Manager
Stalls new requests until reply comes back
Number of requests = number of credits
Prevents traffic build-up in NoC
3
2
1
0
stall

## Slide 32: Latency
Credits TM improves roundtrip latency (drastically)
… and reduces NoC contention
Chart: Number of Masters
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
LYNX NoC | 17.0396 | 17.8394 | 16.8436 | 21.8492 | 20.6808 | 18.0222 | 21.004 | 23.991 | 26.9831 | 18.1933 | 20.6724 | 22.0783 | 24.5712 | 26.5911
Without credits traffic manager
With credits traffic manager

## Slide 33: Ordering in Multiple-Slave Systems
Reply 2 arrives before reply 1
Data ordering hazard!
  Interconnect must guarantee correct ordering
Master
Slave 1
Slave 2
Request 1
Reply 1
Reply 2
Request 2

## Slide 34: 1. Stall Traffic Manager
Qsys uses “stall traffic manager”
  Stall requests to different slave until reply returns
Problem: latency increases / throughput drops
Master
Slave 1
Slave 2
Request 1
Reply 1
Reply 2
Request 2
Stall
TM
Stop request 2!
Allow request 2

## Slide 35: 2. VC Traffic Manager
Leverage VCs & reorder at master
  Increase throughput / reduce latency
  Use VC buffers in NoC  no added area
Throughput limited by number of VCs
Master
Slave 1
Slave 2
Request 1 (VC1)
Reply 1 (VC1)
Reply 2 (VC2)
Request 2 (VC2)
VC
TM
Allow reply 1
Allow reply 2
Buffer replies in NoC

## Slide 36: 3. ROB Traffic Manager
Reorder buffer (ROB) Traffic Manager
  Instantiate RAM in FPGA soft logic
  Reorder more replies than VC TM
    higher throughput
    … but more area
Master
Slave 1
Slave 2
ROB
TM
Buffer replies in RAM
BRAM

## Slide 37: Three Traffic Managers for Ordering
Performance
Chart: Number of Consecutive Requests to Each Slave
| 1 | 2 | 4 | 8 | 16
LYNX NoC (ROB) | 1 | 1 | 1 | 1 | 1
LYNX NoC (VC) | 0.21053 | 0.4 | 0.72727 | 1 | 1
LYNX NoC (Stall) | 0.052632 | 0.1 | 0.18182 | 0.30769 | 0.47059
Depending on traffic  VC or ROB TM

## Slide 38: Three Traffic Managers for Ordering
Performance
Chart: Number of Consecutive Requests to Each Slave
| 1 | 2 | 4 | 8 | 16
LYNX NoC (ROB) | 1 | 1 | 1 | 1 | 1
LYNX NoC (VC) | 0.21053 | 0.4 | 0.72727 | 1 | 1
Qsys Bus (Stall) | 0.11111 | 0.2 | 0.33333 | 0.5 | 0.66667
LYNX NoC (Stall) | 0.052632 | 0.1 | 0.18182 | 0.30769 | 0.47059
Depending on traffic  VC or ROB TM
Performance (much) better than Qsys
Qsys

## Slide 39: Outline
1. LYNX CAD Flow
How can we automate the use of NoCs?
2. Transaction Communication
How to handle request – reply communication on NoC?
3. Comparison
LYNX + NoC compared to Qsys + Bus

## Slide 40: Frequency
System Frequency ~1.5X higher with Embedded NoC
(150-bits)
LYNX NoC
Qsys Crossbar
Qsys Multi-Slave
Qsys Multi-Master

## Slide 41: Area
Chart: Number of Modules
| 2 | 4 | 8 | 16 | 32 | 64
FPGA large | 46480 | 46480 | 46480 | 46480 | 46480 | 46480
FPGA small | 11652 | 11652 | 11652 | 11652 | 11652 | 11652
Qsys (Crossbar - 2 clocks) | 258.93 | 812.73 | 2886.17 | 10789.67 | 62759.25
Qsys (Multiple Slaves - 2 clocks) | 168.67 | 324.43 | 632.54 | 1240.92 | 2468.89 | 4925.41
Qsys (Multiple Masters - 2 clocks) | 175.03 | 319.57 | 608.94 | 1174.05 | 2215.86
LYNX NoC (16-node, 150-bit, 4-VC) | 800 | 800 | 800 | 800 | 800 | 800
dummy | 0.021515 | 0.21515 | 0.21515 | 2.1515 | 21.5146 | 215.1463
32x32 Qsys crossbar larger than largest FPGA!
32x32 crossbar NoC = ~2% of FPGA area
(150-bits)
LYNX NoC
Qsys Crossbar
Qsys Multi-Slave
Qsys Multi-Master

## Slide 42: Summary
1. LYNX CAD Flow
2. Transaction Communication
3. Area/Frequency Comparison
Up to 78X less area
~1.5X higher system frequency
Traffic-build up in Multiple-master
Ordering in Multiple-slave
CAD flow steps to automatically connect Design to NoC

## Slide 43: Future Work
“Mimic” Benchmarking
  Standard way to compare interconnects
  Use graphs not complete apps
 | Ordering | Uneven Arbitration | Broadcast
LYNX |  |  | 
Hoplite |  |  | 
Qsys |  |  | 
 | Feed-forward Streaming | External Memory Transactions
LYNX | 100 GB/s | 10 GB/s
Hoplite | 75 GB/s | 12 GB/s
Qsys | 25 GB/s | 7 GB/s









A
B
C
D
Traffic generators instead of modules

## Slide 44
Thank You!

## Slide 45: Three Traffic Managers for Ordering
Chart: Number of Credits
| 4 | 8 | 12 | 16 | 20
ROB TM | 38.95 | 40.35 | 41.6 | 41.95 | 42.7
VC TM | 21.3 | 22.35 | 24.95 | 25.44 | 25.85
Stall TM | 23.1 | 23.35 | 23.7 | 23.75 | 23.8
ROB TM twice the area VC/Stall TMs
Area

## Slide 46: Future Work
“Mimic” Benchmarking
  Application graphs to evaluate and compare different interconnects
A
D
C
B
 | Transaction Ordering | Uneven Arbitration | Broadcast
LYNX |  |  | 
GENIE |  |  | 
Qsys |  |  | 
 | Feed-forward Streaming | External Memory Transactions
LYNX | 100 GB/s | 10 GB/s
GENIE | 75 GB/s | 12 GB/s
Qsys | 25 GB/s | 7 GB/s









NoC in context of tomorrow’s FPGAs
  High-level Synthesis
  Virtualization
  Partial Reconfiguration

## Slide 47: Latency
Chart: Number of Masters
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Qsys Bus (with clock crossing) | 10 | 14 | 18 | 22 | 26 | 30 | 34 | 38 | 42 | 46 | 50 | 54 | 58 | 62
Qsys Bus (no clock crossing) | 8 | 11 | 14 | 17 | 20 | 23 | 26 | 29 | 32 | 35 | 38 | 41 | 44 | 47
LYNX NoC | 17.0396 | 17.8394 | 16.8436 | 21.8492 | 20.6808 | 18.0222 | 21.004 | 23.991 | 26.9831 | 18.1933 | 20.6724 | 22.0783 | 24.5712 | 26.5911
LYNX NoC roundtrip latency lower than Altera Qsys Bus
~1.9x
~2.5x