## Slide 1: SDN Lecture
Layer VIII: Network Applications

## Slide 3
Network applications can be seen as the “network brains”. They implement the control-logic that will be translated into commands to be installed in the data plane, dictating the behavior of the forwarding devices. Take a simple application as routing as an example. The logic of this application is to define the path through which packets will flow from a point A to a point B. To achieve this goal a routing application has to, based on the topology input, decide on the path to use and instruct the controller to install the respective forwarding rules in all forwarding devices on the chosen path, from A to B.
Software-defined networks can be deployed on any tradi- tional network environment, from home and enterprise net- works to data centers and Internet exchange points. Such variety of environments has led to a wide array of network applications. Existing network applications perform traditional functionality such as routing, load balancing, and security policy enforcement, but also explore novel approaches, such as reducing power consumption. Other examples include fail-over and reliability functionalities to the data plane, end-to-end QoS enforcement, network virtualization, mobility management in wireless networks, among many others. The variety of network applications, combined with real use case deployments, is expected to be one of the major forces on fostering a broad adoption of SDN [268].

## Slide 4
Despite the wide variety of use cases, most SDN applications can be grouped in one of five categories: traffic engineering, mobility and wireless, measurement and moni- toring, security and dependability and data center networking. Tables IX and X summarize several applications categorized as such, stating their main purpose, controller where it was implemented/evaluated, and southbound API used.

## Slide 8: Traffic engineering
Several traffic engineering applications have been pro- posed, including ElasticTree [273], Hedera [275], OpenFlow- based server load balancing [336], Plug-n-Serve [284] and Aster*x [272], In-packet Bloom filter [276], SIM- PLE [290], QNOX [285], QoS framework [287], QoS for SDN [286], ALTO [269], ViAggre SDN [291], ProCel [281], FlowQoS [274], and Middlepipes [27]. In addition to these, recent proposals include optimization of rules placement [337], the use of MAC as an universal label for efficient routing in data centers [338], among other techniques for flow manage- ment, fault tolerance, topology update, and traffic characteri- zation [339]. The main goal of most applications is to engineer traffic with the aim of minimizing power consumption, maxi- mizing aggregate network utilization, providing optimized load balancing, and other generic traffic optimization techniques.
Load balancing was one of the first applications envisioned for SDN/OpenFlow. Different algorithms and techniques have been proposed for this purpose [336], [272], [284]. One partic- ular concern is the scalability of these solutions. A technique to allow this type of applications to scale is to use wildcard-based rules to perform proactive load balancing [336]. Wildcards can be utilized for aggregating clients requests based on the ranges of IP prefixes, for instance, allowing the distribution and directing of large groups of client requests without re-
quiring controller intervention for every new flow. In tandem, operation in reactive mode may still be used when traffic bursts are detected. The controller application needs to monitor the network traffic and use some sort of threshold in the flow counters to redistribute clients among the servers when bottlenecks are likely to happen.

## Slide 9: Traffic engineering
SDN load-balancing also simplifies the placement of net- work services in the network [284]. Every time a new server is installed, the load-balancing service can take the appropriate actions to seamlessly distribute the traffic among the available servers, taking into consideration both the network load and the available computing capacity of the respective servers. This simplifies network management and provides more flexibility to network operators.
Existing southbound interfaces can be used for actively monitoring the data plane load. This information can be lever- aged to optimize the energy consumption of the network [273]. By using specialized optimization algorithms and diversified configuration options, it is possible to meet the infrastruc- ture goals of latency, performance, and fault tolerance, for instance, while reducing power consumption. With the use of simple techniques, such as shutting down links and devices intelligently in response to traffic load dynamics, data center operators can save up to 50% of the network energy in normal traffic conditions [273].

## Slide 10: Traffic engineering
One of the important goals of data center networks is to avoid or mitigate the effect of network bottlenecks on the operation of the computing services offered. Linear bisection bandwidth is a technique that can be adopted for traffic patterns that stress the network by exploring path diversity in a data center topology. Such technique has been proposed in an SDN setting, allowing the maximization of aggregated network utilization with minimal scheduling overhead [275].
SDN can also be used to provide a fully automated system for controlling the configuration of routers. This can be partic- ularly useful in scenarios that apply virtual aggregation [340]. This technique allows network operators to reduce the data replicated on routing tables, which is one of the causes of routing tables’ growth [341]. A specialized routing applica- tion [291] can calculate, divide and configure the routing tables of the different routing devices through a southbound API such as OpenFlow.

## Slide 11: Traffic engineering
Traffic optimization is another interesting application for large scale service providers, where dynamic scale-out is required. For instance, the dynamic and scalable provisioning of VPNs in cloud infrastructures, using protocolols such as ALTO [271], can be simplified through an SDN-based approach [269]. Recent work has also shown that optimiz- ing rules placement can increase network efficiency [337]. Solutions such as ProCel [281], designed for cellular core networks, are capable of reducing the signaling traffic up to 70%, which represents a significant achievement.
Other applications that perform routing and traffic engi- neering include application-aware networking for video and data streaming [342], [343] and improved QoS by employing multiple packet schedulers [288] and other techniques [287], [285], [278], [344]. As traffic engineering is a crucial issue in all kinds of networks, upcoming methods, techniques and innovations can be expected in the context of SDNs.

## Slide 12: Mobility & wireless
The current distributed control plane of wireless networks is suboptimal for managing the limited spectrum, allocating radio resources, implementing handover mechanisms, man- aging interference, and performing efficient load-balancing between cells. SDN-based approaches represent an opportu- nity for making it easier to deploy and manage different types of wireless networks, such as WLANs and cellular networks [298], [300], [294], [235], [345], [346]. Traditionally hard-to-implement but desired features are indeed becoming a reality with the SDN-based wireless networks. These include seamless mobility through efficient hand-overs [298], [347], [345], load balancing [298], [235], creation of on-demand virtual access points (VAPs) [298], [295], downlink scheduling (e.g., an OpenFlow switch can do a rate shaping or time divi- sion) [295], dynamic spectrum usage [295], enhanced inter- cell interference coordination [295], [345], device to device of- floading (i.e., decide when and how LTE transmissions should be offloaded to users adopting the D2D paradigm [348]) [294], per client and/or base station resource block allocations (i.e., time and frequency slots in LTE/OFDMA networks, which are known as resource blocks) [235], [294], [346], control and assign transmission and power parameters in devices or in a group basis (e.g., algorithms to optimize the transmission and power parameters of WLAN devices, define and assign transmission power values to each resource block, at each base station, in LTE/OFDMA networks) [294], [235], sim- plified administration [298], [300], [235], easy management of heterogenous network technologies [300], [235], [349], in- teroperability between different networks [349], [346], shared wireless infrastructures [349], seamless subscriber mobility and cellular networks [345], QoS and access control policies made feasible and easier [345], [346], and easy deployment of new applications [298], [235], [349].

## Slide 13
One of the first steps towards realizing these features in wireless networks is to provide programmable and flexible stack layers for wireless networks [350], [235]. One of the first examples is OpenRadio [350], which proposes a soft- ware abstraction layer for decoupling the wireless protocol definition from the hardware, allowing shared MAC layers across different protocols using commodity multi-core plat- forms. OpenRadio can be seen as the “OpenFlow for wireless networks”. Similarly, SoftRAN [235] proposes to rethink the radio access layer of current LTE infrastructures. Its main goal is to allow operators to improve and optimize algorithms for better hand-overs, fine-grained control of transmit powers, resource block allocation, among other management tasks.

## Slide 14
Light virtual access points (LVAPs) is another interesting way of improving the management capabilities of wireless net- works, as proposed by the Odin [298] framework. In contrast to OpenRadio, it works with existing wireless hardware and does not impose any change to IEEE 802.11 standards. An LVAP is implemented as a unique BSSID associated with a specific client, which means that there is a one-to-one mapping between LVAPs and clients. This per-client access point (AP) abstraction simplifies the handling of client associations, au- thentication, handovers, and unified slicing of both the wired and wireless portions of the network. Odin achieves control logic isolation between slices, since LVAPs are the primitive type upon which applications make control decisions, and applications do not have visibility of LVAPs from outside their slice. This empowers infrastructure operators to provide ser- vices through Odin applications, such as a mobility manager, client-based load balancer, channel selection algorithm, and wireless troubleshooting application within different network slices. For instance, when a user moves from one AP to another, the network mobility management application can automatically and proactively act and move the client LVAP from one AP to the other. In this way, a wireless client will not even notice that it started to use a different AP because there is no perceptive hand-off delay, as it would be the case in traditional wireless networks.

## Slide 15
Very dense heterogeneous wireless networks have also been a target for SDN. These DenseNets have limitations due to constraints such as radio access network bottlenecks, control overhead, and high operational costs [294]. A dynamic two-tier SDN controller hierarchy can be adapted to address some of these constraints [294]. Local controllers can be used to take fast and fine-grained decisions, while regional (or “global”) controllers can have a broader, coarser-grained scope, i.e., that take slower but more global decisions. In such a way, designing a single integrated architecture that encompasses LTE (macro/pico/femto) and WiFi cells, while challenging, seems feasible.

## Slide 16: Measurement & monitoring
Measurement and monitoring solutions can be divided in two classes. First, applications that provide new functionality for other networking services. Second, proposals that target to improve features of OpenFlow-based SDNs, such as to reduce control plane overload due to the collection of statistics.
An example of the first class of applications is improving the visibility of broadband performance [351], [6]. An SDN-based broadband home connection can simplify the addition of new functions in measurement systems such as BISmark [351], al- lowing the system to react to changing conditions in the home network [6]. As an example, a home gateway can perform reactive traffic shaping considering the current measurement results of the home network.

## Slide 17: Measurement & monitoring
The second class of solutions typically involve different kinds of sampling and estimation techniques to be applied, in order to reduce the burden of the control plane with respect to the collection of data plane statistics. Different techniques have been applied to achieve this goal, such as stochastic and deterministic packet sampling techniques [352], traffic matrix estimation [260], fine-grained monitoring of wildcard rules [353], two-stage Bloom filters [354] to represent monitoring rules and provide high measurement accuracy without incurring in extra memory or control plane traffic overhead [302], and special monitoring functions (extensions to OpenFlow) in forwarding devices to reduce traffic and processing load on the control plane [355]. Point-to-point traffic matrix estimation, in particular, can help in network design and operational tasks such as load balancing, anomaly detection, capacity planning and network provisioning.

## Slide 18: Measurement & monitoring
With information on the set of active flows in the network, routing information (e.g., from the routing application), flow paths, and flow counters in the switches it is possible to construct a traffic matrix using diverse aggregation levels for sources and destinations [260].
Other initiatives of this second class propose a stronger de- coupling between basic primitives (e.g., matching and count- ing) and heavier traffic analysis functions such as the detection of anomaly conditions attacks [356]. A stronger separation favors portability and flexibility. For instance, a functionality to detect abnormal flows should not be constrained by the basic primitives or the specific hardware implementation. Put another way, developers should be empowered with streaming abstractions and higher level programming capabilities.

## Slide 19: Measurement & monitoring
In that vein, some data and control plane abstractions have been specifically designed for measurement purposes. OpenSketch [309] is a special-purpose southbound API de- signed to provide flexibility for network measurements. For instance, by allowing multiple measurement tasks to execute concurrently without impairing accuracy. The internal design of an OpenSketch switch can be thought of as a pipeline with three stages (hashing, classification, and counting). Input packets first pass through a hashing function. Then, they are classified according to a matching rule. Finally, the match rule identifies a counting index, which is used to calculate the counter location in the counting stage. While a TCAM with few entries is enough for the classification stage, the flexible counters are stored in SRAM. This makes the OpenSketch’s operation efficient (fast matching) and cost-effective (cheaper SRAMs to store counters).
Other monitoring frameworks, such as OpenSample [307] and PayLess [311], propose different mechanisms for deliv- ering real-time, low-latency and flexible monitoring capabil- ities to SDN without impairing the load and performance of the control plane. The proposed solutions take advantage of sampling technologies like sFlow [308] to monitor high- speed networks, and flexible collections of loosely coupled (plug-and-play) components to provide abstract network views yielding high-performance and efficient network monitoring approaches [307], [311], [353].

## Slide 20: Security & Dependability
An already diverse set of security and dependability proposals is emerging in the context of SDNs. Most take advantage of SDN for improving services required to secure systems and networks, such as policy enforcement (e.g., access control, firewalling, middleboxes as middlepipes [27]) [100], [326], [335], [324], [27], DoS attacks detection and mitigation [323], [334], random host mutation [324] (i.e., randomly and frequently mutate the IP addresses of end-hosts to break the attackers’ assumption about static IPs, which is the common case) [329], monitoring of cloud infrastructures for fine- grained security inspections (i.e., automatically analyze and detour suspected traffic to be further inspected by specialized network security appliances, such as deep packet inspection systems) [321], traffic anomaly detection [352], [323], [334], fine-grained flow-based network access control [325], fine-grained policy enforcement for personal mobile applications [327] and so forth [100], [326], [323], [329], [321], [324], [335], [352]. Others address OpenFlow-based networks issues, such as flow rule prioritization, security services composition, protection against traffic overload, and protection against malicious administrators [201], [258], [320], [328], [199].

## Slide 21
There are essentially two approaches, one involves using SDNs to improve network security, and another for improving the security of the SDN itself. The focus has been, thus far, in the latter.
Using SDN to improve the security of current networks. Prob- ably the first instance of SDN was an application for security policies enforcement [100]. An SDN allows the enforcement to be done on the first entry point to the network (e.g., the Eth- ernet switch to which the user is connected to). Alternatively, in a hybrid environment, security policy enforcement can be made on a wider network perimeter through programmable devices (without the need to migrate the entire infrastructure to OpenFlow) [326]. With either application, malicious actions are blocked before entering the critical regions of the network.

## Slide 22
SDN has been successfully applied for other purposes, namely for the detection (and reaction) against DDoS flooding attacks [323], and active security [319]. OpenFlow forwarding devices make it easier to collect a variety of information from the network, in a timely manner, which is very handy for algorithms specialized in detecting DDoS flooding attacks.
The capabilities offered by software-defined networks in increasing the ability to collect statistics data from the network and of allowing applications to actively program the forward- ing devices, are powerful for proactive and smart security pol- icy enforcement techniques such as Active security [319]. This novel security methodology proposes a novel feedback loop to improve the control of defense mechanisms of a networked infrastructure, and is centered around five core capabilities: protect, sense, adjust, collect, counter. In this perspective, active security provides a centralized programming interface that simplifies the integration of mechanisms for detecting attacks, by a) collecting data from different sources (to identify attacks), b) converging to a consistent configuration for the security appliances, and c) enforcing countermeasures to block or minimize the effect of attacks.

## Slide 23
Improving the security of SDN itself. There are already some research efforts on identifying the critical security threats of SDNs and in augmenting its security and dependability [201], [258], [357]. Early approaches try to apply simple techniques, such as classifying applications and using rule prioritization, to ensure that rules generated by security applications will not be overwritten by lower priority applications [201]. Other proposals try to go a step further by providing a framework for developing security-related applications in SDNs [258]. However, there is still a long way to go in the development of secure and dependable SDN infrastructures [357]. An in-deep overview of SDN security issues and challenges can be found in Section V-F.

## Slide 24: Data Center Networking
From small enterprises to large scale cloud providers, most of the existing IT systems and services are strongly dependent on highly scalable and efficient data centers. Yet, these infrastructures still pose significant challenges regarding computing, storage and networking. Concerning the latter, data centers should be designed and deployed in such a way as to offer high and flexible cross-section bandwidth and low- latency, QoS based on the application requirements, high levels of resilience, intelligent resource utilization to reduce energy consumption and improve overall efficiency, agility in provisioning network resources, for example by means of network virtualization and orchestration with computing and storage, and so forth [358], [359], [360]. Not surprisingly, many of these issues remain open due to the complexity and inflexibility of traditional network architectures.

## Slide 25
The emergence of SDN is expected to change the current state of affairs. Early research efforts have indeed showed that data center networking can significantly benefit from SDN in solving different problems such as live network migration [316], improved network management [316], [315], eminent failure avoidance [316], [315], rapid deployment from development to production networks [316], troubleshoot- ing [316], [317], optimization of network utilization [317], [312], [314], [315], dynamic and elastic provisioning of middleboxes-as-a-service [27], minimization of flow setup latency and reduction of controller operating costs [361]. SDN can also offer networking primitives for cloud appli- cations, solutions to predict network transfers of applica- tions [312], [314], mechanisms for fast reaction to operation problems, network-aware VM placement [317], [313], QoS support [317], [313], realtime network monitoring and prob- lem detection [317], [314], [315], security policy enforcement services and mechanisms [317], [313], and enable program- matic adaptation of transport protocols [312], [318].

## Slide 26
SDN can help infrastructure providers to expose more networking primitives to their customers, by allowing virtual network isolation, custom addressing, and the placement of middleboxes and virtual desktop cloud applications [313], [362]. To fully explore the potential of virtual networks in clouds, an essential feature is virtual network migration. Similarly to traditional virtual machine migration, a virtual network may need to be migrated when its virtual machines move from one place to another. Integrating live migration of virtual machines and virtual networks is one of the forefront challenges [316]. To achieve this goal it is necessary to dynam- ically reconfigure all affected networking devices (physical or virtual). This was shown to be possible with SDN platforms, such as NVP [112].

## Slide 27
Another potential application of SDN in data centers is in detecting abnormal behaviors in network operation [315]. By using different behavioral models and collecting the nec- essary information from elements involved in the operation of a data center (infrastructure, operators, applications), it is possible to continuously build signatures for applications by passively capturing control traffic. Then, the signature history can be used to identify differences in behavior. Every time a difference is detected, operators can reactively or proactively take corrective measures. This can help to isolate abnormal components and avoid further damage to the infrastructure.

## Slide 28: Towards SDN App Stores
As can be observed in Tables IX and X, most SDN applications rely on NOX and OpenFlow. NOX was the first controller available for general use, making it a natural choice for most use-cases so far. As indicated by the sheer number of security-related applications, security is probably one of the killer applications for SDNs. Curiously, while most use cases rely on OpenFlow, new solutions such as SoftRAN are considering different APIs, as is the case of the Femto API [252], [301]. This diversity of applications and APIs will most probably keep growing in SDN.
There are other kinds of network applications that do not easily fit in our taxonomy, such as Avior [363], OESS [364], and SDN App Store [365], [366]. Avior and OESS are graphical interfaces and sets of software tools that make it easier to configure and manage controllers (e.g., Floodlight) and OpenFlow-enabled switches, respectively. By leveraging their graphical functions it is possible to program OpenFlow enabled devices without coding in a particular programming language.

## Slide 29
The SDN App Store [365], [366], owned by HP, is probably the first SDN application market store. Customers using HP’s OpenFlow controller have access to the online SDN App Store and are able to select applications to be dynamically downloaded and installed in the controller. The idea is similar to the Android Market or the Apple Store, making it easier for developers to provide new applications and for customers to obtain them.