## Slide 1: HYDRO: A Hybrid Routing Protocol for Lossy and Low Power Networks draft-tavakoli-hydro-01
Stephen Dawson-Haggerty, Jonathan Hui, Arsalan Tavakoli

## Slide 2: Problem Statement
Needed: An IP-Based Routing Protocol for Lossy and Low Power Networks
Application Routing Requirements
  Concerns to be considered for a given application domain
 HYDRO (?)

## Slide 3: Hydro Properties
Combination of centralized and distributed mechanisms
  Distributed DAG formation
    Lots of literature about how to do this [MintRoute,CTP,4bitle,etc.]
  Centralized (but replicated) topology database
    Also well understood [TSMP,CentRoute, Ethane, etc.]
O(1) state used in L2N nodes when no traffic, collection
  But (optionally) optimizes active flows by using O(D) state
Border routers cache routes, connect to other networks (may allow transit)

## Slide 4: HYDRO Operation
process advertisement
next-hop: fe80::64
Node router
Border router
Installed link
solicit
source = fe80::1
dest = ff02::2
solicit
source = fe80::5
dest = ff02::2
advertise
source = fe80::64
dest = ff02::1
hop limit = 100
cost = 0
process advertisement
next-hop: fe80::64
fe80::1
fe80::5
fe80::2
fe80::6
fe80::a
fe80::7
fe80::8
Default route selection

## Slide 5: HYDRO Operation
Node router
Border router
Installed link
fe80::1
fe80::5
fe80::2
ping
source = 2001::6
dest = ipv6.google.com
hop-by-hop option topology
neighbor fe80::5 qual 1.1
neighbor fe80::8 qual 3.2
...
fe80::6
LSDB update
LSDB update
fe80::a
fe80::7
fe80::8
Default route selection
Topology Collection

## Slide 6: HYDRO Operation
Node router
Border router
Installed link
fe80::1
fe80::5
fe80::2
ping
source = 2001::6
dest = 2001::a
fe80::6
insert route
hop 0: fe80::5
hop 1: fe80::6
fe80::a
fe80::7
fe80::8
Default route selection
Topology Collection
Normal Forwarding

## Slide 7: HYDRO Operation
Node router
Border router
Installed link
fe80::1
fe80::5
fe80::2
send
nxt_hdr: tcp
source = 2001::6
dest = 2001::7
fe80::6
fe80::7
insert route
hop 0: fe80::2
hop 1: fe80::7
destination option install
flow destination: 2001::7
method: source
reverse?: no
hop 0: fe80::8
hop 1: fe80::6
fe80::8
store route
send
source = 2001::7
dest 2001::6
routing header
hop 0: fe80::8
hop 1: fe80::6
fe80::a
Default route selection
Topology Collection
Normal Forwarding
Route Install

## Slide 8: Topology and Workload
According to Routing Requirements, predominant traffic pattern is data collection, although unicast and multicast traffic is critical
  Hydro fundamentally optimizes data collection, and allows for optimization of active in-network flows
Each routing requirement highlights a hierarchical topology containing “Border Routers” that Hydro can utilize:
  Zone/Area controllers in Building-Automation, LBRs in Urban environments, Central controller in Home Automation
  When no such controller exists, size of network is small enough that an existing node can be tasked with Border Router responsibilities
Notes: Optimizes existing workload. Uses existing heirarchy.

## Slide 9: Beyond the Protocol Survey
Latency bounds
  Route convergence
  End-to-End transmission time
Flexible tradeoff between per-node state / control overhead and routing stretch
Priority-Based Routes and Quality of Service
  Traffic type can alter route selection
Multicast Traffic
Security Mechanisms

## Slide 10: Beyond the Protocol Survey
What are the real criteria that the protocol survey document excluded?
  Latency
  Stretch/optimality
Additional Extensions / Future Work
  Network Numbering: it’s a real question
  L3 interaction with L2.5 (6lowpan) compression
  Multicast Routing
  Priority Queue Forwarding

## Slide 11: Limitations of HYDRO
Source Routing
  Per-packet overhead and breaks down for deep paths.
Latency in reaction to installed path failures dependent on topology report rate.
  Need for Local Agility
Border Routers need backplane for reliable dissemination of topology

## Slide 12: End

## Slide 13: Backup Slides

## Slide 14: Multicast Forwarding
Use a combination of unicast and trickle-based dissemination
  Similar to Firecracker Protocol (Levis et. al)
Border Router identifies connected components multicast group subgraph
  Unicast multicast packet to small number of nodes in group
  Nodes in group forward packet within subgraph using Trickle-based mechanisms.
Degenerates cleanly
  Site-local all-nodes becomes a dissemination with trickle
  Small disconnected groups become a number of unicast messages

## Slide 15: Source Routing
Limitations
  Packet overhead per packet, dependent on size of route
  Large routes could dominate packet size, and require this state to be maintained at originating nodes
  Reduces local agility
Silver Lining / Solutions
  20-hops mentioned as max-depth in routing requirements docs
    Multiple border routers bounds maximum length of a path
  Hop-by-hop route install option can be used
  Use hybrid landmark routing:
    Source route broken up across a set of landmarks on a path

## Slide 16: ROLL Protocol-Survey Criteria
Node Cost
  Willingness metric and Node Attributes
Link Cost
  Link interface incorporates quality & confidence
Table scalability
  O(1) default route table, dynamic state is O(D)
Loss response
  Discovered when used, prompts update to controller
Control Overhead
  No periodic beacons, Topology reports tied to data rates

## Slide 17: Multiple Controllers
Mechanism for redundancy and scalability
Topology database replicated across all controllers
Controllers communicate using a backplane
Routes between in-network nodes can use backchannel paths between controllers

## Slide 18: Willingness and Node Attributes
Willingness: scalar value indicating desire/ability to carry traffic
  Used in default route formation: when choosing between “equivalent” default routes, more willing nodes are preferred
Node Attribute: an extensible type, for instance battery power remaining, processing capacity, or current load
  Used for centralized route computation