## Slide 1: 虛擬化技術 Virtualization Technique
System Virtualization
Case Study

## Slide 2: Agenda
VMware on x86
Xen on x86
KVM on x86
ARMvisor on ARM
  CPU virtualization
  Memory virtualization
  I/O virtualization

## Slide 3: vmware on x86

## Slide 4: VMware
Basic properties :
  Separate OS and hardware – break hardware dependencies
  OS and Application as single unit by encapsulation
  Strong fault and security isolation
  Standard, HW independent environments can be provisioned anywhere
  Flexibility to chose the right OS for the right application

## Slide 5: VMware Virtualization Stack

## Slide 6: VMware Major Products
VMware Server
  A free-of-charge virtualization-software server suite
  Run multiple servers on your server
  Hosted architecture
  Available for Linux hosts and Windows hosts
VMware ESX Server
  An enterprise-level computer virtualization product
  Quality of service
  High-performance I/O
  Host-less architecture ( bare-metal )

## Slide 7: VMware GSX Server Architecture

## Slide 8: VMware ESX Server Architecture

## Slide 9: XEN ON X86

## Slide 10: Xen
Basic properties :
  Para-virtualization
    Achieve high performance even on its host architecture (x86) which has a reputation for non-cooperation with traditional virtualization techniques.
  Hardware assisted virtualization
    Both Intel and AMD have contributed modifications to Xen to support their respective Intel VT-x and AMD-V architecture extensions.
  Live migration
    The LAN iteratively copies the memory of the virtual machine to the destination without stopping its execution.
Implement system:
  Novell's SUSE Linux Enterprise 10
  Red Hat's RHEL 5
  Sun Microsystems' Solaris

## Slide 11: Para-virtualization in Xen
Xen extensions to x86 arch
  Like x86, but Xen invoked for privileged instructions
  Avoids binary rewriting
  Minimize number of privilege transitions into Xen
  Modifications relatively simple and self-contained
Modify kernel to understand virtualized environment
  Wall-clock time vs. virtual processor time
    Desire both types of alarm timer
  Expose real resource availability
    Enables OS to optimize its own behaviour

## Slide 12: Original Xen Architecture

## Slide 13: Hardware Assistance in Xen
Hardware assistance :
  CPU provides VMExit for certain privileged instructions
  Extend page tables used to virtualize memory
Xen features :
  Enable Guest OS to be run without modification
    For example, legacy Linux and Windows
  Provide simple platform emulation
    BIOS, apic, iopaic, rtc, Net (pcnet32), IDE emulation
  Install para-virtualized drivers after booting for high-performance IO
  Possibility for CPU and memory para-virtualization
    Non-invasive hypervisor hints from OS

## Slide 14: New Xen Architecture

## Slide 15: KVM ON X86

## Slide 16: KVM
KVM ( Kernel-based Virtual Machine)
  Linux host OS
    The kernel component of KVM is included in mainline Linux, as of 2.6.20.
  Full-virtualization
    KVM is a full virtualization solution for Linux on x86 hardware containing virtualization extensions (Intel VT or AMD-V).
    Using KVM, one can run multiple virtual machines running unmodified Linux or Windows images.
  IO device model in KVM :
    KVM requires a modified QEMU for IO virtualization framework.
    Improve IO performance by virtio para-virtualization framework.

## Slide 17: KVM Full Virtualization
It consists of a loadable kernel module
  kvm.ko
    provides the core virtualization infrastructure
  kvm-intel.ko / kvm-amd.ko
    processor specific modules

## Slide 18: IO Device Model in KVM
Original approach with full-virtualization
  Guest hardware accesses are intercepted by KVM
  QEMU emulates hardware behavior of common devices
    RTL 8139
    PIIX4 IDE
    Cirrus Logic VGA

## Slide 19: IO Device Model in KVM
New approach with para-virtualization

## Slide 20: IO Device Model in KVM
virtio architecture

## Slide 21: ARMvisor ON ARM

## Slide 22: What is ARMvisor?
A KVM for ARM architecture
Technology:
  Para-virtualization
  Trap & Emulation
  Dynamic Memory Allocation
  virtio & IRQchip-in-kernel
Opensource under GNU GPLv2

## Slide 23: Who are developers?
@

## Slide 24: Overview of ARMvisor
CPU
MMU
I/O
Timer
Interrupt
Hardware
CPU Virtualization
MMU
Virtualization
I/O
Virtualization
VM 0
VM 1
Hypervisor
QEMU-ARM
KVM-ARM Linux

## Slide 25: Overview of ARMvisor
CPU Virtualization
MMU
Virtualization
I/O
Virtualization
Methodology: Trap and Emulation
Methodology: Shadow Paging
Methodology: Userspace I/O Emulation

## Slide 26: Software Stack of ARMvisor
Hardware: ARM Cortex-A8
Host OS: Linux 2.6.38
ARMvisor
Driver
QEMU 0.14
Device
Driver
Guest OS: Linux 2.6.35

## Slide 27
Kernel space
KVM
User space
QEMU
Guest Mode
Guest OS
2. Return to QEMU
1. VM initialization
3. Run VM
4. Enter Guest
5. Exit Guest
Enter Guest
Exit Guest
Return to QEMU
Run VM
Enter Guest
Lightweight trap
Heavyweight trap
Notes: In lightweight traps, the emulation is handled in internal functions of KVM which are implemented in the kernel space of Linux.
In contrast, heavyweight traps that include I/O accesses and parts of CPU functions will be handled in QEMU.
What’s more, QEMU is in Linux’s user space so context switches are required. Hence, the cost of a single heavyweight trap is relatively heavier than the lightweight one.

## Slide 28: ARMvisor ON ARM
CPU Virtualization
Memory Virtualization
I/O Virtualization

## Slide 29: CPU Virtualization
A classification of instructions of an ISA into 3 different groups:
  Privileged instructions
    Those that trap if the processor is in user mode and do not trap if it is in kernel mode
  Sensitive instructions
    Those that attempt to affect the resources in the system.
  Critical instructions
    Those are sensitive instructions but do not trap in user mode

## Slide 30: CPU Virtualization
Privileged
Instructions
Sensitive
Instructions
Critical
Instructions
We need to emulate sensitive instructions and
carefully handled critical instructions

## Slide 31: Sensitive Instruction Emulation
Classify sensitive, privilege and critical instructions for ARM ISA
Implement an sensitive instruction emulation engine
How to handle critical instructions?
  Lightweight Para-virtualization
    Pre-Insert swi #
    Few of guest kernel codes are patched

## Slide 32: ARM Instruction Classification
S | C | P | Instruction Type | Operation | Behavior | Emulation
 |  |  | Data-processing | ADCS, ADDS, ANDS, BICS, EORS, MOVS, MVNS, ORRS, RSBS, RSCS, SBCS, SUBS | CPSR  SPSR | Status Register Access
 |  |  | Status register access | MRS | GPR  CPSR/SPSR | 
 |  |  |  | MSR | CPSR/SPSR  GPR | 
 |  |  |  | CPS | CPSR  CPS (A¦I¦F¦Mode) | 
 |  |  | Extended | RFE | (CPSR, PC)  MEM | 
 |  |  |  | SRS | MEM  (SPSR, R14) | 
 |  |  | Load and Store Multiple | LDM(3) | CPSR  SPSR | 
 |  |  |  | LDM(2) | USR_REGS  MEM | Bank Register Access
 |  |  |  | STM(2) | MEM  USR_REGS | 
 |  |  | Load and Store | LDRT/LDRBT | GPR  MEM (User Permission) | User Permission Access
 |  |  |  | STRT/STRBT | MEM  GPR (User Permission) | 
 |  |  | Coprocessor | CDP/CDP2, LDC/LDC2, MCR/MCR2, MCRR/MRRC2, MRC/MRC2, MRRC/MRRC2, STC/STC2 | Call CORP COPR  MEM/GPR MEM/GPR  CORP | Coprocessor Access

## Slide 33: Patched Guest Kernel Codes
Patched Souse Code | LOC | Emulation
arch/arm/boot/compressed/head.S arch/arm/include/asm/assembler.h arch/arm/include/asm/irqflags.h arch/arm/include/asm/kvm-asm.h arch/arm/include/asm/kvmguest.h arch/arm/kernel/asm-offsets.c arch/arm/kernel/entry-armv.S arch/arm/kernel/entry-common.S arch/arm/kernel/head.S arch/arm/kernel/setup.c arch/arm/kernel/traps.c arch/arm/mm/abort-ev6.S arch/arm/mm/proc-macros.S arch/arm/mm/proc-v6.S | 6 71 99 154 20 12 74 20 4 6 14 5 4 6 | Status Register Access Bank Register Access Coprocessor Access
arch/arm/include/asm/futex.h arch/arm/include/asm/uaccess.h arch/arm/lib/clear_user.S arch/arm/lib/copy_from_user.S arch/arm/lib/copy_to_user.S arch/arm/lib/csumpartialcopyuser.S arch/arm/lib/getuser.S arch/arm/lib/putuser.S arch/arm/lib/strnlen_user.S arch/arm/lib/uaccess.S arch/arm/nwfpe/entry.S | 3 6 8 1 1 10 4 8 1 11 1 | User Permission Access
Total | 549 | 

## Slide 34: Para-virtualization
…
mov r0, r0
add sp, sp
movs pc, lr
…
Notes: Let’s see an example about the Para-virtualization implementation. On the screen is a partial assembly code in guest OS source code. The third line “movs pc lr”would update PC value so it’s obviously a sensitive instruction. Actually it’s a critical instruction so our goal is trying to make it trap to the VMM.

## Slide 35: Para-virtualization
…
mov r0, r0
add sp, sp
virt_svc_movs “movs pc, lr”
…
.macro virt_svc_movs, inst
SWI 0x190
\inst
.endm
We replace the instruction with a self-defined macro. The original instruction is the parameter of the macro. This macro would send a software interrupt to VMM. When receiving the SWI number 0x190, VMM has the knowledge that the next instruction is a instruction which should be emulated.
Notes: We replace the instruction with a self-defined macro. The original instruction is the parameter of the macro. This macro would send a software interrupt to VMM. When receiving the SWI number 0x190, VMM has the knowledge that the next instruction is a instruction which should be emulated.

## Slide 36
KVM Trap Entry
KVM/Guest
Context Switch
Unit
Host Trap Handler
Instruction Emulation
Exception/Interrupt Emulation
MMU Emulation
QEMU I/O
Emulation
KVM Trap Dispatcher
UND
ABORT
SWI
IRQ/FIQ

## Slide 37: Vector
oxffff0000
oxffff1000
Kernel Vector
0xffff001c
0x1C | FIQ
0x18 | IRQ
0x14 | (Reserved)
0x10 | Data Abort
0x0C | Prefetch Abort
0x08 | Supervisor Call
0x04 | Undef. Instr.
0x00 | Reset
Notes: 有一個exception vector table在一班的OS裡面，用來重新導向不同的trap到相對應的處理者

## Slide 38: KVM Vector
oxffff0000
oxffff1000
KVM
Vector
The KVM trap
Interface
0xffff001c
Notes: We imitate this mechanism. We design a KVM vector, and the KVM vector would re-direct traps to the KVM trap interface which is placed at address 0xffff1000 in another shared page. The exception trap to this vector would be re-direct to the interface for later handling.

## Slide 39: CPU Virtualization Overhead
CPU virtualization
  Frequent lightweight traps result in lots of context switch
Try to reduce…
  number of traps
  Overhead of emulation
Notes: In our measurement, parts of critical instructions only involve in virtual state and no hardware modification is needed.
As a result, instead of trapping such instructions, we have an idea that let these instructions execute in guest address space.
Other parts of sensitive instructions must be executed in privileged mode, that is, it must be trapped to host when emulation. The optimization policy of CPU virtualization is to reduce the number of traps and the overhead of emulation.

## Slide 40: Optimizations for CPU Virtualization
Dynamic View
  Which sensitive instructions are frequently used by the guest OS in the ARM architectures?
  What activities are these frequently-used sensitive instructions used in?
Optimizations
  Reduce instruction emulation overhead / traps
    Shadow register file
    Sensitive instruction grouping
    TLB/Cache trap overhead reduction

## Slide 41: CPU Optimization Methods
Operations that read the information in co-processor are replaced by SRFA (shadow register file access).
TLB operations and BTB flush in guest are replaced by NOP.
FIT (fast instruction trap) is applied to reduce costs of context switch.
Notes: 要解決的問題

## Slide 42: CPU Optimization
Shadow file register (SFR)
  Map VCPU’s shadow state of the register file into memory region that is both accessible for the VMM and guest with RW permission.
Notes: We proposed shadow register file which …… it’s a little bit hard to understand the literal meaning of this sentence. Here comes a figure.

## Slide 43: Shadow Register File Optimization
Sensitive Instruction
Emulation Engine
VCPU
Register
File
Guest
Sensitive
Instructions
Hypervisor
Guest
Trap
Shadow file register (SFR)
  Map VCPU’s shadow state of the register file into memory region that is both accessible for the VMM and guest with RW permission.

## Slide 44: Shadow Register File Optimization
Sensitive Instruction
Emulation Engine
VCPU
Register
File
Guest
Sensitive
Instructions
Hypervisor
Guest
Shadow
Register
File
Sync

## Slide 45: Sensitive Instruction Grouping Optimization
.macro vector_stub, name, mode, correction=0
  stmia sp, {r0, lr}
  mrs lr, spsr
  str lr, [sp, #8]
  mrs r0, cpsr
  eor r0, r0, #(\mode ^ SVC_MODE | PSR_ISETSTATE)
  msr spsr_cxsf, r0
  and lr, lr, #0x0f
  mov r0, sp
  movs pc, lr
Guest Kernel uses the vector_stub to handle interrupt/trap
Many sensitive instructions are used in the small code segment
Sensitive Instructions

## Slide 46: Sensitive Instruction Grouping Optimization
.macro vector_stub, name, mode, correction=0
  hypercall(vector_stub)
Grouping the small code segment by one hypercall

## Slide 47: TLB/Cache Trap Optimization
Sensitive Instruction
Emulation Engine
TLB and Cache
Instructions
Hypervisor
Guest
Trap
Enter System Mode
Context Switch
Handler
Dispatcher
TLB/Cache Instruction Emulation
Originally, the instruction emulation path is too long!
Assembly
Code
C

## Slide 48: TLB/Cache Trap Optimization
TLB and Cache
Instructions
Hypervisor
Guest
Trap
Enter System Mode
Fast Emulation
Engine
After optimization, the overhead of TLB/Cache trap is reduced
Assembly
Code

## Slide 49: CPU Optimization
Base
  Trap all sensitive instructions
VCPU v0.1 Model
  R Sharing: guest directly READ virtual registers
VCPU v1.0 Model
  R/W Sharing: guest directly R/W virtual registers
  Sensitive instruction grouping
  TLB/Cache trap overhead reduction

## Slide 50: Sensitive Instr. Trap Reduction
 | base version | CPU_OPT_V0.1 | CPU_OPT_V1.0
Guest sum_exits | 15536 | 8567 | 3788
Guest light_exits | 15318 | 8396 | 3555
Guest heavy_exits | 218 | 171 | 233
sensitive inst exits | 12679 | 5855 | 658
mls | 355 | 356 | 359
msr | 1567 | 1529 | 42
mrs | 1606 | 298 | 0
cps | 1842 | 1484 | 6
data | 317 | 318 | 167
copr | 6990 | 1868 | 84
ls | 286 | 171 | 402
LS (T or PT write) | 68 | 0 | 169
MMIO | 218 | 171 | 233
Total Instr Emulation | 12965 | 6026 | 1060
94.81%
100%
99.67%
98.80%
75.62%
76.79%

## Slide 51: ARMvisor ON ARM
CPU Virtualization
Memory Virtualization
I/O Virtualization

## Slide 52: Memory Virtualization on X86
Memory virtualization architecture

## Slide 53: Memory Virtualization on X86
The performance drop of memory access is usually unbearable. VMM needs further optimization.
VMM maintains shadow page tables :
  Direct virtual-to-physical address mapping
  Use hardware TLB for address translation

## Slide 54: MMU Virtualization on ARM
vCPU
MMU
Virtualization
vMMU
Guest Physical Memory
Host Physical Memory
Guest
GVA
GPA
HPA
Overview

## Slide 55: MMU Virtualization on ARM
Dynamic physical memory allocation to guest
Software MMU Virtualization
  Simulate a real ARMv6 ot v7 MMU
  Build up Shadow page table
  Synchronization between Guest page table and Shadow page table

## Slide 56: Dynamic Physical Memory Allocation to Guest
Guest
Physical
Memory
Host
Virtual
Memory
Host
Physical
Memory
Guest physical memory pages are allocated dynamically at runtime.

## Slide 57: Software MMU Virtualization (1)
MMU Virtualization will behave as a real MMU chip to build up page table.
2
1
Page Table
Real MMU Chip
3

## Slide 58: Software MMU Virtualization (2)
Guest
Page Table
Walker
Guest
Permission
Checker
Shadow Page Table
Mapping
Shadow Page Table
Update
MMIO
Access
Checker
PABT / DABT
Trap
True translation fault
True permission fault
MMIO emulation
Hidden translation fault
Software MMU Virtualization Processes
1
2
3
Initial
Synchronization
Real MMU Behavior
Shadow Table Behavior

## Slide 59: Step 1
While page fault is occured, Guest Page Table Walker will walk through guest page table to check if the fault is from guest.
Guest
Page Table
Walker
Guest
Permission
Checker
Shadow Page Table
Mapping
Shadow Page Table
Update
MMIO
Access
Checker
PABT / DABT
Trap
True translation fault
True permission fault
MMIO emulation
Hidden translation fault
1

## Slide 60: Step 2
Guest
Page Table
Walker
Guest
Permission
Checker
Shadow Page Table
Mapping
Shadow Page Table
Update
MMIO
Access
Checker
PABT / DABT
Trap
True translation fault
True permission fault
MMIO emulation
Hidden translation fault
2
Step 2 will check if guest access permission is not allowed.

## Slide 61: Step 3
Guest
Page Table
Walker
Guest
Permission
Checker
Shadow Page Table
Mapping
Shadow Page Table
Update
MMIO
Access
Checker
PABT / DABT
Trap
True translation fault
True permission fault
MMIO emulation
Hidden translation fault
3
Step 3 will check if the guest physical memory address used is located in the range of MMIO address.

## Slide 62: Steps 4 & 5
Guest
Page Table
Walker
Guest
Permission
Checker
Shadow Page Table
Mapping
Shadow Page Table
Update
MMIO
Access
Checker
PABT / DABT
Trap
True translation fault
True permission fault
MMIO emulation
Hidden translation fault
Step 4 and step 5 are used to build up shadow page tables and maintain their consistency between guest and shadow ones.
4
5

## Slide 63: Build Up Shadow Page Table
Process
Page Table
Shadow
Page Table
Process
Page Table
Shadow
Page Table
Virtual TTPR
Real TTPR
Guest OS
VMM
Corresponding mapping table
Context switch
Switch the pointer to new location
Process
Page Table
Shadow
Page Table
New process
Create new shadow page table mapping to new process
Access
Page fault !
Load !

## Slide 64: MMU Virtualization Optimization
Guest kernel space mapping sharing
Reduce guest page table synchronization overhead

## Slide 65: Guest kernel space mapping sharing
User space
Kernel space
User space
Kernel space
Guest Process 1
Guest Process 2
User space
Kernel space
Shadow table
Shadow table
Shadow table
The shadow tables of kernel space
are shared by all guest processes

## Slide 66: Reduce guest page table synchronization overhead
We use para-virtualization to inform hypervisor when guest would like to change guest page table
This method will eliminate from using write-protection for synchronization

## Slide 67: ARMvisor ON ARM
CPU Virtualization
Memory Virtualization
I/O Virtualization

## Slide 68: Emulate by QEMU

## Slide 69: I/O Virtualization Flow
KVM-ARM
ARM Architecture
QEMU-ARM
Guest OS
User Space
Kernel Space
R/W MMIO
Trap
Timer
Interrupt
UART
Storage
Network
I/O Request
I/O Access
I/O Response
I/O Result

## Slide 70: virtio

## Slide 71: What is virtio
Virtio is an idea from IBM to improve I/O virtualization.
An I/O abstraction layer
Provide a set of APIs and structures

## Slide 72: Why it fast
Guest share a memory space with QEMU, so that the data can be accessed by each sides.
Furthermore, the number of MMIOs can be reduced by using VirtQueue.

## Slide 73
Virtio AMBA Controller
Virtio Driver
Guest
Vring
Transport
Virtio AMBA Controller
Virtio Device
QEMU

## Slide 74: Devices & Drivers
Virtio supports Block, Network, Serial, and Ballon devices right now.
In addition, these drivers already built-in in Linux Kernel.

## Slide 75: irq_chip in kernel

## Slide 76: irq_chip in kernel

## Slide 77: irq_chip in kernel

## Slide 78: Why it useful
The MMIO request is no longer need to deliver to QEMU. That is to say, the type of trap is changed from heavy-wirght trap to light-weight trap.

## Slide 79: References
Web resources :
  Xen project http://www.xen.org
  KVM project http://www.linux-kvm.org/page/Main_Page
  IBM VirtIO survey https://www.ibm.com/developerworks/linux/library/l-virtio
  PCI-SIG IO virtualization specification http://www.pcisig.com/specifications/iov
Paper & thesis resources :
  Jiun-Hung Ding, Chang-Jung Lin, Ping-Hao Chang, Chieh-Hao Tsang, Wei-Chung Hsu, Yeh-Ching Chung, "ARMvisor: System Virtualization for ARM", Linux Symposium
  林長融，ARMvisor IO 效能最佳化及分析，以 Virtio 及 irqchip 為例，國立清華大學，碩士論文，2012
Other resources :
  Lecture slides of “Virtual Machine” course (5200) in NCTU
  Lecture slides of “Cloud Computing” course (CS5421) in NTHU
  Vmware Overview Openline presentation slides http://www.openline.nl
  Xen presentation http://www.cl.cam.ac.uk/research/srg/netos/papers/2006-xen-fosdem.ppt

## Slide 80: I/O Virtualization
Currently, ARM I/O Emulations are supported by QEMU-ARM

## Slide 81: Support ARMv6 & ARMv7 architecture
ARM v6 11mpcore
ARM v7 cortex-a8