## Slide 1: Opportunistic Routing in Mobile Ad-Hoc Networks
Pramita Mitra1 and Christian Poellabauer1
1Department of Computer Science and Engineering
University of Notre Dame, USA

## Slide 2: Introduction

## Slide 3
Opportunistic Networks (OPNETs)
  created out of mobile devices carried by people,
  no reliance on any preexisting infrastructure
  challenged by network irregularities such as frequent node disconnection, node mobility, changes in transmission power, etc.
Characteristics of OPNETs
  intermittent network connectivity – complete end-to-end paths from source to destinations may not be available
  variable link performance – links are unstable and may change or break quickly

## Slide 4
Mobile Ad-Hoc Networks (MANETs)
  Similarity to OPNETs -
    Neither network relies on a centralized entity, but are made out of autonomous and self-organizing mobile nodes.
    Nodes connect and disconnect as they move in and out of each other’s communications range, or are turned on or off unpredictably by power management algorithms.
  Difference with OPNETs -
    MANETs assume an end-to-end communications paradigm. In OPNETs, routes are formed online with the data message being forwarded one link at a time as the links in the route become available.
  OPNETs are, therefore, an extension of MANETs with the end-to-end communications paradigm relaxed or removed
    Hence this chapter refers to OPNETs as Opportunistic Mobile Ad-Hoc Networks (OPMANETs)

## Slide 5: An example of Exploiting Opportunistic Contacts for Communications
Bob’s Residence
Bob’s Phone
Car
Bluetooth
School Bus
Wi-Fi
Kid’s Phone
Bluetooth
3G
Bob wishes to send a message to his family but has no 2G/3G connectivity. He opportunistically forwards the message using the Bluetooth radio in his phone to another car driving in the same direction as his residence.
The car moves through the traffic in the city, and transfers the message using a Wi-Fi link to a school bus going in the same direction as Bob’s residence.
Next, the bus forwards the message using its Bluetooth radio to the cellphone of a kid who is disembarking at bus stop in the same area where Bob lives.
When the kid walks past Bob’s residence on his way to home, the message is finally delivered to its destination.

## Slide 6: Routing in OPMANETs

## Slide 7
Routing is one of the most compelling challenges in OPMANETs because no end-to-end path is available
  In fact the source and the destination(s) might never be connected to the same network at the same time
In order to make communications possible, routing protocols employ a “store-carry-forward” approach
  These devices take advantages of radio contacts with peers as and when they become available and cooperate in routing
    When a suitable relay node is not immediately found to forward the data to, the current node buffers the data and wait until a suitable forwarding opportunity is available.
  It may take multiple discontinuous wireless contacts or hops before the data is carried from the source to the destination(s) over a period of time.

## Slide 8: Challenges of Routing in OPMANETs
What | Why
Bad Forwarding Decisions | In OPMANETs, nodes connect and disconnect to and from the network frequently, which may lead to nodes making bad forwarding decisions, i.e., failure to forward data to the best relay node(s).
Connection Unpredictability | Data transfer to a relay node might be incomplete/unsuccessful due to highly unpredictable link quality and duration of contact.
Data Dissemination | It is not easy to provide reliable multi-hop, multi-destination communications between devices sharing physical resources and sensor data with each other in a spontaneous and ad-hoc fashion.

## Slide 9: Challenges of Routing in OPMANETs (Continued)
What | Why
Resource Constraints | In the “store-carry-forward” style routing, a node may have to buffer data for a long period of time before a suitable relay node could be found – thereby leading to drain on the local resources of the mobile devices.
Privacy and Security | Devices used in OPMANETs store personal data and interests. while participating in data forwarding, they become vulnerable to the danger of tracking and monitoring user behavior for constructing user profiles and compromising user anonymity in the network.
User Interaction | Although most of the OPMANET applications are pervasive, some of the received data may require some kind of instantaneous user reaction. However, it is not easy to design a general user interaction model for such systems.

## Slide 10: Analysis of OPMANET Routing Approaches

## Slide 11: Analysis Framework
Routing in OPMANETs
Discovery and Dissemination
Resource Usage
Applications

## Slide 12: Questions Asked in this Chapter
Discovery and Dissemination –
  How does the protocol discover and exploit the intermittent communication opportunities in a mobile environment?
  How does the protocol provide reliable multi-hop, multi-destinations data delivery, which is a common data dissemination pattern in OPMANETs?
Resource Usage –
  What impact does the protocol have on the battery power, CPU usage and memory of the local device?
Applications –
  What kind of real-world applications are enabled by the routing protocol?
  What are their Quality of Service requirements?

## Slide 13: Taxonomy of Routing Protocols in OPMANETs
Routing Approaches in OPMANETs
Forwarding-based
Flooding-based
Hybrid
Social
Behavior-based
Direct Transmission
Context-based
History
Location
Mobility
Epidemic
History
Network Coding
Location
Link Asymmetry

## Slide 14: Forwarding-based Approaches
Forwarding-based approaches select only one relay node for forwarding data messages
Two types
  Direct transmission-based approaches – these protocols limit the number of hops traveled by a data message, i.e.,
    they either directly transmit to the destination(s) when they are in communications range with them, or,
    a fixed number of relay nodes are used.
  Context-based approaches – these protocols exploit the context in which the nodes are operating to decide
    which node to forward the data message to, and
    whether it should transmit the message immediately or hold the message until it meets a better node.

## Slide 15: Context-based Approaches: (1) History/Estimation-based
These approaches allow a node to make better forwarding decision by making an estimation of the forwarding probability of its neighbors based on historical data.
Protocols differ in the parameters they use for making estimation. Commonly used parameters are:
  previous connection/disconnection time between nodes
  residual battery level
  rate of mobility or change of connectivity
  number of messages forwarded by a neighbor in the past
  number of encounters with the destination(s)

## Slide 16: Context-based Approaches: (2) Location-based
Nodes choose the neighbor which moves the data message closest to the destination(s).
Some kind of future location prediction techniques are used by location-based approaches to select the relay node. Typical parameters being used for location prediction are:
  Last-known location
  Velocity
  Direction of movement
  Past vicinity to other nodes
Nodes incur additional overhead while obtaining location updates of their own and neighboring nodes.

## Slide 17: Context-based Approaches: (3) Mobility-based
The mobile devices in OPMANETs often follow certain known patterns such as walking along a street or driving down the highway.
Such regular motion patterns help the intermediate nodes to make accurate estimation of which nodes move toward the destination with higher probability.
  Useful for urban applications where users exhibit certain patterns of mobility

## Slide 18: Context-based Approaches: (4) Link Asymmetry-based
These approaches exploit asymmetric communication opportunities arising in heterogeneous OPMANETs for increased data transmission success and lower latency.
Cost of discovering asymmetric links in the network is non-negligible. Common techniques used in asymmetric link discovery are:
  Using mutual third-party set of proxy nodes
  Exchanging neighbor lists
  Making one-way link quality estimates

## Slide 19: Flooding-based Approaches
Multicast is a common delivery semantic in OPMANETs when the data message is intended to be delivered to all members in the same multicast group.
Multicasting is often realized by flooding - the heuristic used by flooding-based algorithms is that data should be diffused all over the network because no knowledge about an appropriate next-hop node is available.
  Flooding-based techniques work well in highly mobile networks with many spontaneous communication opportunities between nodes.
  They result in shorter message delivery delay, only at the expense of high resource consumption, contention and network congestion due to large number of data transmissions associated with flooding.
Flooding-based approaches employ a variety of policies to limit flooding, e.g., imposing a maximum number of hops to each data message, or by limiting the total number of message copies present in the network at the same time.

## Slide 20: Flooding-based Approaches: (1) Epidemic Routing
These approaches are the most primitive form of flooding.
As suggested by the term “epidemic”, these routing approaches diffuse data in the network in a fashion similar to diseases or viruses (i.e., by means of pair-wise contacts between nodes).
  A node is susceptible to infection when it has not yet received the data message.
  A susceptible node becomes infected when it comes into contact with an infected node and receives the message from it. After catching the infection, the infected node stores the message locally.
  An infected node is healed when (if at all) it delivers the message to the destination node(s).
  A healed node also becomes immune to the same disease and does not provide relaying of the same message.

## Slide 21: Flooding-based Approaches: (2) Location-based
Geocasting protocols send messages from a source to all hosts located in a specific geographical region.
  When a node inside the geocasting region receives the message, it shares the messages with other group members inside the geocasting region using flooding.
  Group membership changes whenever a mobile node moves in or out of the geocasting region.

## Slide 22: Flooding-based Approaches: (3) History-Based
Improves upon epidemic routing by using a history-based method to choose messages to forward to a new contact
  When two nodes meet, they use their history of past encounters to make delivery probability prediction.
  Delivery probability depends on
    Frequency of encounters - If they meet very often, they have high delivery probability to each other. On the other hand, two nodes which haven’t met each other in a while are not good forwarders of messages to each other.
    Visits of nodes to other geographic regions – A node that frequently visits the area where the destinations are located, has a high delivery probability.
    Time since last encounter – Delivery probability values must age with time.

## Slide 23: Flooding-based Approaches: (4) Network Coding-based
Network-coding based protocols take an original approach to limit message flooding.
  Data delivery is made with fewer number of messages injected into the network.
Just to give a classical example, assume A, B, and C are the only three nodes of a small network. Let us assume that node A generates the data message “a” and node C generates the data message “c.” In order to distribute their data to all other nodes, nodes A and C send their messages to node B. Instead of sending two separate data messages for “a” and “c,” respectively, node B broadcasts a single message containing “a” XOR “c.” Once “a” XOR “c” is received, both nodes A and C can finally infer the data messages sent by the other source (i.e., node A can infer “c” and node C can infer “a”).

## Slide 24: Hybrid Approaches
Flooding-based approaches result in shorter delay but generate high overhead, network congestion and contention. Forwarding-based approaches minimize overhead but suffer from long delays.
Hybrid approaches combine features from forwarding-based approaches with flooding-based approaches to achieve low data dissemination latency while limiting the network overheads.
  A forwarding-based approach is used to get the data message as close to the destinations as possible.
  Once the data message gets close to the destinations, flooding-based approaches are used to disseminate the data in the surrounding.

## Slide 25: Social Behavior-based Approaches
Social behavior-based approaches use social-based metrics derived from contacts between devices to make opportunistic forwarding decisions with low overhead.
  Many approaches implicitly assess the strength of “social” ties between nodes, using metrics such as time of last encounters between nodes, or frequency of contacts as a hint of similarity.
  However, these simple metrics may only capture one facet of the underlying mobility patterns, which can in turn hinder good contact predictions.
    Complex network analysis is a further generic and powerful tool to formulate and solve the problem of future contact prediction.

## Slide 26: OPMANET Applications

## Slide 27
Traditional applications are not suitable for OPMANETs because they normally assume an end-to-end connection from the source to the destination(s).
The applications that are suitable for OPMANETs are typically asynchronous in nature and tolerant of long delay and high error rates.
  Typical application scenarios are urban pocket switched networks, advertisements, wildlife/environmental monitoring, providing Internet connectivity in developing areas, etc.

## Slide 28: Urban Environments
Haggle[1] measures and models pair-wise contacts between devices in a Pocket Switched Networks (PSNs) using the following two parameters:
  Duration of contact - the total time that two tagged mobile devices are within reach of each other. It directly influences the capacity of OPNETs because it limits the amount of data that can be transferred between nodes.
  Inter-contact times - the time in between two contact opportunities between the same two tagged devices. It influences the feasibility of OPNETs and the delay associated with them.
Various sets of traces from real-world environments were collected and analyzed
The Haggle architecture enables a social and context-aware content sharing service that exploits a context definition designed for OPNMAETs.
  The service uses the users’ social behavior patterns to identify content that might be relevant to the communities a user interacts with.
  These interaction patterns allow the system to improve forwarding decisions by probabilistically predicting future user contacts.

## Slide 29: Urban Environments
adPASS[2] disseminates advertisements among interested users in an urban environment, using a word-of-mouth recommendation style approach.
  Data dissemination relies solely on one-hop communications and uses a node’s profile to carry out its task. When two nodes detect a match in their node profiles, they exchange data. The physical movement of nodes is utilized to distribute the data.
adPASS also makes use of Information Sprinklers for implementing time-shifted information pass, i.e., users who are at the same place but at a different time are able to share information with one another.

## Slide 30: Wildlife Monitoring
ZebraNet[3] tracks and monitors zebras wearing special collars in the vast savanna area of central Kenya.
  The base station consists of a mobile vehicle for the researchers, which periodically moves around in the savanna and collects data from the zebras encountered.
Two alternative protocols for data collection
  Flooding-based - each collar sends all its data to each encountered neighbor until the data eventually reaches the base station.
  History-based - each node selects only one of its neighbors as relay for its data, the selected node is the one with the highest probability to eventually encounter the base station.
    Each node is thus assigned a hierarchy level (initially zero) that increases each time it encounters the base station, and conversely decreases after not having seen the base station for a certain amount of time. When sending data to a relay node, the neighbor to be selected is the one with the highest hierarchy level.

## Slide 31: Environmental Monitoring
Delay-insensitive underwater sensor networks[4]
  Such networks consist of sensors and vehicles deployed to perform collaborative monitoring tasks over a given underwater region.
  Serves a variety of applications. e.g., oceanographic data collection, pollution monitoring, offshore exploration, disaster prevention, assisted navigation, tactical surveillance, mine reconnaissance, etc.
Each node is allowed to select its best next hop node, the transmission power and the forward error correction code rate for each packet.
The routing protocol exploits those links that guarantee a low packet error rate, in order to maximize the probability that the packet is correctly decoded at the receiver.

## Slide 32: Connecting Developing Areas
DakNet Project[5] aims at realizing a very low-cost asynchronous ICT infrastructure to provide connectivity to rural India.
  Kiosks are built up in villages and equipped with digital storage and short-range wireless communications .
  Periodically, Mobile Access Points (MAPs) mounted on buses, motorcycles, or even bicycles pass by the village kiosks and exchange data with them wirelessly.
  MAPs can download data stored at the kiosks, and upload them to the Internet when passing by an access point (AP) in a nearby town. Similarly, MAPs may download, from the Internet, the requested data and bring it to villages.
DakNet has the potential to support a number of applications, e.g., messaging (e.g., email, audio/video messaging, and mobile e-commerce), data distribution (e.g., public health announcements, community bulletin boards, news, and music), and collection (e.g., environmental sensing, voting, health records, and census).

## Slide 33: Connecting Developing Areas
Saami Network Connectivity (SNC) [6] provides network connectivity to the nomadic Saami population of the reindeer herders in Sweden, Norway, and Finland.
Network connectivity
  enables the Saami to achieve economic growth through distance education, work and Internet-based business.
  gives the Saami more visibility, and allows them to have more influence in the political and economic affairs of their country.
In its initial stage, the SNC project has only focused on providing email, file transfer, and cached web services to the Saami people.
  Reindeer herd telemetry is also going to be provided to support the herding activity itself.

## Slide 34: Discussion and Conclusion

## Slide 35
This chapter provides an overview of a few key routing approaches in OPMANETs by characterizing them in terms of three aspects, i.e.,
  data dissemination
  resource usage
  applications
Based on the existing research efforts and the unique characteristics of OPMANETs, this chapter found that there are still a few research issues that are far from being adequately addressed. These issues are listed as follows:

## Slide 36
Advanced personal mobile devices should be used for increasing network capacity
  The rapid proliferation of sophisticated mobile devices (e.g., smartphones and tablets) equipped with powerful processors, abundant memory and an ever-increasing number of sensors presents the potential of building large-scale dynamic OPMANET applications.
Use of heterogeneous devices and radio technologies should be encouraged for increasing the number of communication opportunities in the network
  The number of devices with diverse radio communications technologies is increasing (e.g., smartphones and tablets are equipped with multiple radio technologies such as Wi-Fi, Bluetooth, and RFID) and one should exploit such heterogeneous communication opportunities for increased data delivery success in OPMANETs.
Privacy and Security
  Future research efforts should focus on developing new privacy and security techniques because the personal mobile devices used in OPMANETs store personal data and interests, and thus become vulnerable to the danger of compromising user anonymity and data integrity while participating in data forwarding.

## Slide 37
Applications should be able to specify their Quality of Service (QoS) requirements
  Future research approaches should aim at enabling the applications to specify their own QoS requirements (e.g., data persistence, reliable delivery, etc.) to the routing protocol.
Node location and velocity should be used by routing approaches
  Forwarding approaches should leverage node location and velocity with simple and accurate link availability estimation algorithms for making intelligent forwarding decisions.
Social behavior-driven traces should be used for deriving realistic mobility models
  Since OPMANETs exploit users’ mobility to bridge disconnections and partitions in the network, it is of high importance to identify realistic mobility models using real users’ mobility traces, in order to drive the protocols’ design and to provide sensible performance results.

## Slide 38
Hybrid routing protocols should be further investigated for increasing data dissemination efficiency in OPMANETs
  Future research efforts should focus on developing hybrid approaches that can dynamically mix-and-match approaches from the set of forwarding-based approaches with the ones from the set of flooding-based approaches, as the multicast group size and resources capabilities of the nodes vary in the network.
Communication opportunities can be artificially created
  Message ferry-based routing protocols artificially create communication opportunities in a sensor network by opportunistically employing additional mobile nodes to offer a message relaying service, and they can be further investigated to draw insights to be used in other application scenarios in OPMANETs.
Multi-tier routing protocols can increase network connectivity at scale
  Future routing approaches should investigate the feasibility of building multi-tier OPNETs in which upper tier nodes will be used to enable connection among various groups of disconnected lower tier nodes in a sparse/partitioned network.

## Slide 39
User participation should be rewarded to increase message forwarding
  With the increasing use of personal mobile devices for implementing OPMANET applications, the assumption of an altruistic resource sharing environment is no longer feasible. Since battery, storage, and processing power are limited and precious resources on such personal user devices, OPMANET applications should provide means to reward participating users that help in forwarding the data messages.

## Slide 40: References
A. Heinemann, “Collaboration in Opportunistic Networks”, PhD Dissertation, Technical University of Darmstadt, 2007.
http://www.haggleproject.org
P. Juang, H. Oki, and Y. Wang, “Energy-Efficient Computing for Wildlife Tracking: Design Trade-Offs and Early Experiences with ZebraNet”, ACM SIGPLAN Notices, Volume 37, 2002.
D. Pompili, T. Melodia, and I. F. Akyildiz, “Routing Algorithms for Delay-insensitive and Delay-sensitive Applications in Underwater Sensor Networks”, In Proceedings of ACM MOBICOM, 2006.
A. Pentland, R. Fletcher, and A. Hasson, “DakNet: Rethinking Connectivity in Developing Nations”, IEEE Computer, Volume 37, Number 1, 2004.
A. Doria, M. Uden, and D. P. Pandey, “Providing Connectivity to the Saami Nomadic Community,” In Proceedings of the 2nd International Conference on Open Collaborative Design for Sustainable Innovation, 2002.