## Slide 1: Mesh networks (for public safety) – a taxonomy
Henning Schulzrinne
FCC & Columbia University

## Slide 2: Overview
A taxonomy of nodes, relationships and devices
Efficiency and capacity
Technical background
Alternatives for public safety

## Slide 3: Mesh components
Wireless routers
Gateways
Printers, servers
Mobile clients
Stationary clients
Intra-mesh wireless links
Stationary client access
Mobile client access
Internet access links
Node Types
Link Types
Mihail L. Sichitiu, NCSU
Notes: Mihail L. Sichitiu, NCSU, 2005/2006

## Slide 4: Mesh requirements
Need symmetric radio links
  802.11 in “ad-hoc” mode
  LTE does not currently support direct mode
    without eNodeB
Stand-alone operation  more than just links
  no HSS
  no remote authentication (HSS, RADIUS/DIAMETER server)
  built-in support infrastructure
    DNS
    DHCP
    SIP proxy
    service discovery
Notes: http://urgentcomm.com/networks_and_systems/news/direct-mode-lte-study-20110928/

## Slide 5: Store-forward vs. Store-carry-forward
store packet for < 100 ms
~stationary while transmitting
store data
& move
mesh networks
store-carry-forward
disruption tolerant
delay tolerant
disk

## Slide 6: Taxonomy
Wireless
Networking
Multi-hop
Infrastructure-less
(ad-hoc)
Infrastructure-based
(Hybrid)
Infrastructure-less
(MANET)
Single
Hop
Cellular
Networks
Wireless Sensor
Networks
Wireless Mesh
Networks
Car-to-car
Networks
(VANETs)
Infrastructure-based
(hub&spoke)
802.11
802.16
Bluetooth
802.11
Mihail L. Sichitiu, NCSU

## Slide 7: Taxonomy, cont’d.
Mesh
infrastucture
in-home (Zigbee)
backup (netBlazr)
temporary
local area (1-2 hops)
wide area (3+ hops)
access (municipial)

## Slide 8: Relationships: Local mesh vs. funnel
GW
Internet

## Slide 9: Mobility
Mobility
Nomadic
(discontinuous)
Vehicular
stationary
dense urban, pedestrian
relative speed
extent of mobility

## Slide 10: Three kinds of mesh nodes
 | Mobile handset | ad-hoc | infrastructure
Radio | 1 (802.11) | 1-2 | 2-4
Antenna | omni | omni | directional
Power | battery | utility | utility, solar, …
Range | 100’ | 100’-200’ | 100’ … 40 miles

## Slide 11: Mesh network capacity
Does adding nodes add per-node capacity?
Depends strongly on assumptions:
  locality of traffic (local vs. funnel to Internet)
  interference  power control, directional antennas
  node distribution
  traffic distribution (uniform vs. hot spot)
Simplified assumptions
per-user throughput < c2W/√(n log n) for link rate W and n nodes
can be as low as W/n
Notes: Plextek 2006: Final Report - Study of Efficient Mobile Mesh Networks
http://stakeholders.ofcom.org.uk/binaries/research/technology-research/mesh.pdf

## Slide 12: Example alternative: Inmarsat BGAN
Examples for illustration only

## Slide 13: Example alternative: Viasat (Exede)
26”
“up to 12 Mb/s upstream -
up to 3 Mb/s downstream”
15 GB for $80/month

## Slide 14: Example: AT&T remote mobility zone
coverage: ½ mile radius
Notes: http://www.wireless.att.com/businesscenter/business-programs/mid-large/remote-mobility-zone.jsp

## Slide 15: Example: Amateur radio
HF & VHF
low bandwidth

## Slide 16: Conclusion
There is no single “mesh” network
What are the requirements?
  instantaneous setup (auto-configuration) by non-techies
  capacity?
  resiliency?
  low cost