## Slide 1: E-MOSFET
The E-MOSFET or enhancement MOSFET can operate in only the enhancement mode. With a positive voltage above a threshold value on the gate, an induced channel of thin layer of –ve charges is created.
The conductivity of channel is enhanced by increase VGS and thus pulling more electrons into channel area.
Notes: Fig 7-32 n channel EMOSFET
Fig 7-33 EMOSFET schem. symbols

## Slide 2: E-MOSFET Characteristics and Parameters
The E-MOSFET for all practical purposes does not conduct until VGS reaches the threshold voltage (VGS(th)). [ID=0 when VGS<VGS(th) ]
ID when conducting can be determined by the formulas below.
K = ID(on) /(VGS - VGS(th))2
ID = K (VGS - VGS(th))2
Notes: Fig 7-40 a n channel curve

## Slide 3: MOSFET Biasing- voltage divider bias
For E-MOSFETs zero biasing cannot be used. Voltage-divider bias must be used to set the VGS greater than the threshold voltage (VGS(th)). ID can be determined as follows. To determine VGS, normal voltage divider methods can be used. The following formula can be applied.
VGS = (R2 / (R1+R2))VDD
VDS = VDD - IDRD
K = ID(on)/(VGS - VGS(th))2
ID = K(VGS -VGS(th))2
VDS can be determined by application of Ohm’s law and Kirchhoff’s voltage law to the drain circuit.
Notes: Fig 7-44a Voltage-divider EMOSFET

## Slide 4: Example 7-16
Determine VGS and VDS for E-MOSFET circuit below. Assume MOSFET has minimum values of ID(on) =200mA at VGS=4V and VGS(th)=2V.

## Slide 5: MOSFET Biasing- drain feedback bias
With drain-feedback bias there is no voltage drop across RG making VGS = VDS. With VGS given determining ID can be accomplished by the formula below.
ID = (VDD – VDS)/RD
Notes: Fig 7-44b drain-feedback