## Slide 1: Wind Energy
Chemical Engineering Seminar
By: Jacqueline Milkovich

## Slide 2: Why Wind Energy?
The current estimate of wind energy potential is 10x the amount of electricity consumption for the entire United States
Low cost and low risk option for electricity consumers and utility companies
Reduced carbon dioxide emission
Notes: Wind energy is a domestic, renewable source of energy that generates no pollution and has little environment impact up to 95% of land used for wind farms can also be used for other profitable activities including ranching, farming, and forestry
The current estimate of wind energy potential is 10x the amount of electricity consumption for the entire US
The US currently get 4.1% of its energy from wind

## Slide 3: Cost and Risk
Notes: Low cost and low risk option for electricity consumers and utilities
Primary drivers that determines the cost of electricity from wind energy: capital cost, capacity factor, and operating cost
With improving technology and techniques wind energy is increasingly becoming one of the most affordable forms of electricity today
When assessing new sources of electricity generation, utilities consider risk of fuel price risk, future environmental regulation as well as cost
Since wind energy doesn’t have fuel cost, contracts called power purchase agreements are signed that last about 20-30 years

## Slide 4: Wind Energy and Carbon Dioxide
Notes: The US burns around 5.4 billion metric ton of carbon dioxide each year, the power sector is the biggest source of carbon dioxide emissions, contributing to 38% of carbon dioxide emissions in the US
In 2013 168 million mega-watts per hour was generated by wind energy, which avoided over 96 million metric ton of carbon dioxide being emitted into the atmosphere, this reduced the power-sector carbon dioxide emission by 4.4%, and is equivalent to taking 16 million cars off the road
On average a single average size wind turbine will avoid over 3,500 metric tons of CO2 annually, equivalent to taking 600 cars off the road

## Slide 5: Wind Basics
Wind turbines are highly evolved windmills
Energy ultimately comes from the sun
Need good winds: >4 m/s at 10 meters
Wind turbines harness wind’s kinetic energy and convert it into electricity
Blades capture energy -> rotation of blades->internal shaft to spin, which is connected to gearbox -> increase speed of rotation -> connected to generator -> produces energy
Notes: Wind turbines are basically highly evolved version of windmills
Wind comes from solar heating of earth’s surface
The earth receives 1.74 x 10^17 watts of power an hour from the sun, 2% of this energy is concerted to wind energy
Modern wind turbines harness wind’s kinetic energy and convert it into electricity
How Wind Energy Works: blades capture energy and rotate, this triggers an internal shaft to spin which is connected to a gear box increasing the speed of rotation, the gear box is connected to a generator that ultimately produces the energy

## Slide 6: Energy and Efficiency
Energy = Power * Time
  Time: Estimate from annual average wind speed
  Power =.5(p)(A)(V^3)
Maximum theoretical power conversion efficiency: Betz Limit = 59%
Practical conversion efficiency: 10% - 30%
Typical commercial turbine: 35%
Notes: Energy
Time: estimate assuming an annual average wind speed and a statistical distribution of wind speeds over time
Power of a mass of air moving through a hoop at velocity v
Density of air = 1.239 kg/m^3
A = area which through the wind is passing, through the wind turbine rotor
V = wind velocity
Betz Limit = 59%
Thus maximum mechanical power extracted from wind blowing through a hoop at a certain rate would be .59*(.5)pAV^3
Higher the wind speed, higher the efficiency

## Slide 7: Aerodynamics of Wind Turbines
Drag Force- component that is in line with the direction of the air stream
Lift Force- the component that is at right angles to the direction of the air stream
  Principle force that drives modern wind turbine rotor
Airfoil Design- one surface of the blade is somewhat rounded, while the other is relatively flat
  Maximizes lift and minimizes drag
  Lift results from pressure difference between the upper and lower surfaces
Notes: Modern wind turbines use aerodynamic principles to capture wind’s energy most efficiently
An object in an air stream experiences a force that is imparted from the air stream to that object, this force is equivalent to two component forces acting in perpendicular directions known as the drag and lift force, the magnitude of these forces depend on the shape of the object, its orientation to the direction of air the air stream, and the velocity of the air stream
Drag Force- component that is in line with the direction of the air stream
Acts parallel to wind flow
Lift Force- the component that is at right angles to the direction of the air stream, principle force that drives modern wind turbine rotor and thus allows it to produce power
Acts perpendicular to the wind flow
Modern wind turbines make use of the aerodynamic forces generated by aerofoils in order to extract power from the wind but each harness these forces in different ways

## Slide 8: Horizontal vs. Vertical Turbines
Horizontal
Most common type
Controls turn rotor into wind
Self-starting
Vertical
Don’t need to be pointed into the wind
Difficult to manufacture due to curved blades
Low efficiency
Non-self-starting
Notes: Horizontal
Equipped with wind assessment equipment that will automatically rotate into the face of the wind and angle its blades to optimize energy capture
Usually has 2-3 blades
Produce high torque at low rotor speed
Vertical
Use wind from any direction without need for position device
Besides this up side they have found little commercial success due to issues with power quality, cyclic loads in the tower systems and the lower efficiency of some of them
Not economically competitive with horizontal design
Not able to self-start since they are unable to produce sufficient aerodynamic starting torque , most need some type of mechanism to start

## Slide 9: Wind Speed in US
Notes: Thinner planetary boundary layer means that stronger winds blow closer to the ground, boundary layer gets thinner where surface obstruction such as trees a d topography are minimal -> US Flat Plains
North Dakota has enough available wind resources to supply energy to 36% of the US
Wind speed can change from day-day, day-month, day-year
A small change in wind velocity has a big impact on power and energy (since velocity is cubed)
Wind speeds also varies at different times in different locations (example might be higher in California in the afternoon and higher in the morning in Minnesota)
Wisconsin
Currently has 417 wind turbines, ranks 22nd out of 43 for number of utility scaled wind turbines
Ranks 17 in wind energy potential, currently Wisconsin’s wind potential is 4x the state’s current electricity needs
Wisconsin enacted a renewable portfolio standard in 1999 and increased its requirement in 2006, which requires 10% of Wisconsin’s utilities to be generated by renewable resources

## Slide 10: Types of Wind Energy
Utility Scale Wind
  Turbines > 100 KW
  Electricity delivered to power grid
  Less than 1% of the electricity generated in US
Distributed/Small Winds
  Turbines < 100 KW
  Electricity delivered directly to home/farm
  More expensive than utility scale
Offshore Winds
  Turbines placed in water bodies
Notes: Utility: wind turbines are larger than 100 kw, are developed with electricity delivered to the power grid and distributed to the end user by electric utilities or power system operator
Turbines on wind farms are connected so the electricity can travel from the wind farm to the power grid, once there power operators will direct it to where its needed
Wind farms are located on private land where the developer of the farm leases the land from the original land owner providing lease payments
Wind accounts for less than 1% of the electricity generated in the US, but installed capacity have been expanding at an annual average rate of 25%
Distributed/Small Winds: turbines of 100 kw or smaller to directly power a home, farm, or small business
More expensive than utility scale due to no being connected to the grid, needs expensive battery
Offshore Wind: turbines placed in bodies of water around the world, not currently in US though

## Slide 11: On-Shore vs. Off-Shore
Off-shore capacity factor: 38%
Off-shore energy is a higher investment but has greater energy returns
  Higher capital costs
  Higher wind speeds
US currently does not have off-shore wind farms
  Cape Cod Wind Project
Notes: Capital cost higher then onshore wind
Off-shore wind speeds are generally higher and steadier allowing greater energy production, the farther off shore you go the higher the wind speeds
Off-shore turbines kept within 30 meter deep due to high developmental cost and 5 km in distance away from the grid, this leads to sight issues
Current onshore wind potential can produce energy for 10 US, offshore potential could product energy for 13 US
Currently no off-shore wind farms in US, but cape cod wind was signed off to happen in 2010 after much debate and will be the first US wind farm

## Slide 12: Environmental Impacts
Positives
Reduction of air pollution for energy production
Requires no water for waste heat removal
Reduced carbon dioxide emissions
95% of land used for wind farms can also be used for other profitable activities (farming, ranching, ect.)
Negatives
Noise
Electromagnetic Interference
Visual
Birds
Notes: Noise: the sources of the noise come from mechanical noise from the gearbox and generator, and aerodynamic noise which comes from the interaction of the air flow with the blades, most commercial wind turbines undergo noise measurement tests, most wind farms are far away from human habitat to eliminate noise complaints
Electromagnetic Interference: when a turbine is positioned between a radio or television transmitter and receiver it can reflect some of the electromagnetic radiation in such a way that the reflected wave interferes with the original signal as it arrives at the receiver, this causes the received signal to be distorted, the extent depends on the material to make the blades, metal blades cause the biggest problem, laminated timber blades absorb rather than reflect radio waves so do not present a problem
Birds: every turbine kills 1-2 birds per year (100,000-400,000 birds a year), the major cause of birds death is building and windows which kill 100 million to 1 billion, as wind farms become increasingly popular project sites need to be conscious of bird sensitive areas
Visual appearance of landscape, resistant to changes in appearance of landscapes, opinions often change once structures have been around for a while

## Slide 13: Future of Wind
A strong national renewable electricity standard
Research and Design
  Aerodynamics and extreme winds
  Integration to the grid
  Minimizing environmental impacts
  Public attitudes to development
Notes: Renewable Portfolio Standards- set targets for renewable energy in the near and long term future, currently 29 states have renewable portfolio standards, but this does not occur at a federal level
Deploying wind energy at a larger level than it is today requires the US to upgrade and expand our nation’s transmission grid, and use the current grid more efficiently