## Slide 1: DC/DC Converter

## Slide 2: Stabilize control voltages in 24 V DC systems Compact and powerful DC/DC converters for an everlasting supply
Innovative products for industrial automation

## Slide 3
The compact DC/DC converters feature protection class III.
They are suitable for applications in floating systems,
e.g. emergency backup systems in ships.
The extraordinary performance:
High efficiency up to 94%
High shock and vibration immunity
Narrow housing
Galvanic isolation: Protection Class III
Super boost with more than 600% * IN for 16 ms
Integrated status relay and active switching outputs
Comprehensive international approvals : TUV, UL, Class I, Div2, ATEX, GL, DNV, ABS, BV, RINA, LR
All these make the converter an all-rounder in all 24 V DC supply systems!

## Slide 4: Target industries and customers
Machinery
Process
Energy
Transportation
Device
Manufacturer
Machine Tools
Automotive
Elevators & Escalators
Oil & Gas
Renewables
Traditional
Transmission & Distribution
Drive Controls & Power Electronics
I/O control devices
Chemical / Pharma
Water Treatment
Food & Beverage
Infrastructure
Ship Building
Railway
Interface Electronics
Conveying Systems

## Slide 5: Product Utility / Attribute
All-purpose use
International approvals like cULus, Class1.Div2 ,ATEX as well as GL ,DNV,BV ensure the world-wide use in different applications.
Space saving
The compact design saves up to 30% space in the cabinet.
Preventive function monitoring
The integrated alarm outputs provide the status supervision for PLC or DCS systems.
Applicable for use in floating systems
DC/DC converter for protection class III. Typical applications are emergency battery banks in buffer mode.
Super boost with more than 600% * IN for 16 ms
Fast and reliable tripping of circuit breakers
Robust and reliable
Reliable operation in a wide temperature range of -25…+70°C (Start-Up:– 40 °C) and MTBF value > 1.000.000 Hours
A galvanic isolated DC/DC converter avoids critical earth loops and regenerates a stable output voltage out of an unregulated or distorted input voltage.

## Slide 6: Key Benefits against competitors
Rapid status diagnosis
LED indicators and integrated status
relay and transistor outputs facilitate status and rapid error analysis
Space saving
perfectly suitable for all standard control
cabinets and the compact design
can saves up to 30% space in the cabinet.
Space saving
Up to 30%
Comprehensive applications around the world
They can be used reliably in different regions and industries
because of the international approvals
(UL, Cl1.Div2, GL, DNV and ATEX)
High Efficiency
Up to 94%
Energy saving
High efficiency up to 94% and low idling power losses ensure low energy consumption and long product life time
Robust and reliable
Reliable operation throughout a wide temperature range of – 25 °C …+70 °C
High MTBF value of > 1.000.000 hours

## Slide 7: Application: Power supply system with DC/DC converter
DC
DC
Control box
Voltage drop
fluctuations due
to load currents
stable
voltage
230VAC
AC
DC
Control cabinet
24VDC
24VDC
230VAC
AC
DC
+24VDC
-24VDC
DC
DC
Control box
24VDC
PE1
PE2
-24VDC
Udiff <> 0
Galvanic isolation required due to different potential
Reconditioning of the 24V DC
due to voltage drops
Control cabinet
Principle diagram 1

## Slide 8: Application: Principle power supply system in shipbuilding industry
3x400VAC
generator 1
AC
DC
Control cabinet
24VDC
Power Good: A
Power Good: B
DC
DC
24VDC
charger
3x400VAC
generator 2
Emergency power distribution
Central
Battery bank
10A PROmax
10A DC/DC
CP M DM20
Principle diagram 2

## Slide 9: Selection chart
Type | Order code | Input /Output voltage | Output current
PRO DCDC 120W 24V 5A | 2001800000 | 24 V DC | 5 A
PRO DCDC 240W 24V 10A | 2001810000 | 24 V DC | 10 A
PRO DCDC 480W 24V 20A | 2001820000 | 24 V DC | 20 A
DC/DC Converter
Accessories modules for different applications
Type | Order code | Application note
CP DM 10 | 8710620000 | Diode module 10A for redundancy power
CP M DM20 | 1222210000 | Diode module 20A for redundancy power
CP DC UPS 24V 20A/10A | 1370050010 | DC UPS for 10A/20A
CP DC UPS 24V 40A | 1370040010 | DC UPS for 40A

## Slide 10
Competitive Analysis
– we are Best in class !
Technical feature |  |  | 
Variants | 5 A | 5, 10, 20 A | 5, 10, 20 A
Input Voltage DC | 14,4…32,4 V | 14…32 V | 14…32 V
Dimension | 32*124*102 (5A) | 48*130*120 | 43*130*120
[W*H*D (mm)] |  |  | 
[10A Version] |  |  | 
MTBF | > 800.000 Hours | > 750.000 Hours | > 1.250.000 Hours
Efficiency | 90% | 92% | 93%
Operating Temperature | -25°C … +70°C | -25°C … +70°C | -25°C …+70°C
 |  |  | (Start-up: - 40 °C)
Power boost | Not applicable | 600% x IN for 12ms | 600% x IN for 16 ms
 |  |  | Weidmüller Patent
Hold up time | 6 ms | 12 ms | 14 ms
Terminals input | NON Pluggable | Pluggable | Pluggable
Status indication | Uin < 19.2 V DC OK: Green | Boost: Yellow Uin < 19.2 V DC OK: Green | DC OK:Green >90%In: Yellow Fault: Red Low Uin: Yellow
Approvals | cURus; cULus; ATEX; GL | cURus; cULus; GL,DNV,BV, ABS,RINA,LR | TÜV; cULus;
 |  |  | Cl1,Div.2; ATEX;
 |  |  | GL,DNV,BV, ABS, RINA, LR;

## Slide 11: DC/DC converter Point of difference
Feature | Customer benefit | Competition
Status signaling with integrated status relay, transistor outputs and triple-color LED |  Remote monitoring through status relay and transistor outputs for PLC, DCS  Easy handling during the setting up of new machinery and system Time saving during trouble shooting | No competitor can offer such combined status signaling with different methods. Triple-LED is true USP from Weidmüller
Narrow housing 5A: 32 x 120 x 130 mm (W x D x H) 10A: 43 x 120 x 130 mm (W x D x H) 20A: 75 x 120 x 130 mm (W x D x H) |  up to 30% space saving | Phoenix Contact: 32 mm (5A) 48 mm (10A) 82 mm (20A)
High efficiency up to 94% & minimal no-load losses |  Cost saving due to low energy consumption | Phoenix Contact: 92% efficiency
Super boost of > 600% * In for minimal 14 ms (Dynamic Current Limiting: Weidmüller Patent) | Tripping of circuit breaker reliably and quickly in case of short circuits Reliable starting up of high capacitive load: e.g. Motor | Weidmüller-Technology has higher performance than SFB technology from Phoenix Contact.
Full set of approvals for shipbuilding and heavy process segments | Suitable for both marine applications and Ex applications in hazardous areas | Only Phoenix contact

## Slide 12
Weidmüller Order Code | Puls Order Code | Phoenix Contact Order Code
2001800000 | CD5.241 /CD5.241-L1 | 2320034 / 2320542
2001810000 | Not available | 2320092 / 2320555
2001820000 | Not available | 2320102 / 2320568
Cross-Reference List

## Slide 13: Thank you
DC/DC Converter