## Slide 1: Digital Control Systems
INTRODUCTION

## Slide 2: Introduction
What is a control system?
Objective:
To make the system OUTPUT and the desired REFERENCE as close as possible, i.e., to make the ERROR as
small as possible.
Key Issues:
1) How to describe the system to be controlled? (Modeling)
2) How to design the controller? (Control)

## Slide 3: Introduction
What is important in a control system?
Stability
• (Transient) response speed
• Accuracy
  dynamic overshooting and oscillation duration
  Steady state error
• Robustness
  errors in models (uncertainties and nonlinearities)
  effects of disturbances
  effects of noises

## Slide 4: Introduction
Modeling of dynamic systems
Model: A representation of a system.
Types of Models:
• Physical models (prototypes)
• Mathematical models (e.g., input-output relationships)
Analytical models (using physical laws)
Computer (numerical) models
Experimental models (using input/output experimental data)
Models for physical dynamic systems:
Lumped-parameter models
Continuous-parameter models. Example: Spring element (flexibility, inertia, damping)

## Slide 5: Introduction
Signal categories for identifying control system types
Continuous-time signal & quantized signal
Continuous-time signal is defined continuously in the time domain. Figure on the left shows a continuous-time signal, represented by x(t).
Quantized signal is a signal whose amplitudes are discrete and limited. Figure on the right shows a quantized signal.
Analog signal or continuous signal is continuous in time and in amplitude. The real word consists of analog signals.

## Slide 6: Introduction
Discrete-time signal & sampled-data signal
Discrete time signal sampled data signal
Discrete-time signal is defined only at certain time instants. For a discrete-time signal, the amplitude between two consecutive time instants is just not defined. Figure on theleft shows a discrete-time signal, represented by y(kh), or simply y(k), where k is an integer and h is the time interval.
Sampled-data signal is a discrete-time signal resulting by sampling a continuous-time signal. Figure on the right shows a sampled-data signal deriving from the continuous-time signal, shown in the figure at the center, by a sampling process. It isrepresented by x∗(t).

## Slide 7: Introduction
Digital signal or binary coded data signal
Digital signal is a sequence of binary numbers. In or out from a microprocessor, a semiconductor memory, or a shift register.
In practice, a digital signal, as shown in the figures at the bottom, is derived by two processes: sampling and then quantizing.
Digital signal

## Slide 8: Introduction
Control System Types

## Slide 9: Introduction
Mathematical comparison between analog and digital control systems

## Slide 10: Introduction
Digital Control systems
Digital controls are used for achieving optimal performance-for example, in the form of maximum productivity, maximum profit, minimum cost, or minimum energy use.

## Slide 11: Introduction
Digital Control systems
Digital controls are used for achieving optimal performance-for example, in the form of maximum productivity, maximum profit, minimum cost, or minimum energy use.

## Slide 12: Introduction
Advantages of digital computers:
Reduced cost,
Flexibility in response to design changes,
Noise immunity
Digital control systems are more suitable for Modern control systems.
Disadvantages of digital computers:
From the tracking performance side, the analog control system exhibits good performances than digital control system.
Digital control system will introduce a delay in the loop.

## Slide 13: Introduction
The loop (forward and feedback) contains both analog and digital signals must provide a means for conversion from one form to other to be used by each subsystem.
Analog-to-Digital Converter(ADC)
A device that converts analog signal to digital signal is called Analog-to-Digital Converter.
Digital Analog Converter(DAC)
A device that converts digital signals to analog signals is called a Digital Analog Converter.

## Slide 14: Introduction
Digital-To-Analog Conversion
From the binary number each bit is properly
weighted voltages and are summed together
to yield analogue output.

## Slide 15: Introduction
Analog-To-Digital Conversion
ADC is not instantaneous and needs two-step process.
There is a delay between the analog input voltage and the output digital word.
In ADC, the analog signal is first converted to a sampled signal and then converted to a sequence of binary numbers, the digital signal.

## Slide 16: Introduction
Controller Design in Digital Control Systems

## Slide 17: Introduction
Controller design in digital control systems - Design in S-domain
Digitization (DIG) or discrete control design
The above design works very well if sampling period T is sufficiently small.

## Slide 18: Introduction
How to design a Controller:
For the approximation methods, used to convert the continuous controller to digital controller, are: Euler method, Trapezoidal method …etc and we can use forward or backward approximation.
forward approximation
backward approximation
Afterwards, the differential equation of the controller can be transformed to difference equation where this difference equation can be easily programmed as a control algorithm.
Note that the sampling time T should be close to zero.

## Slide 19: Introduction
Controller design in digital control systems -Design in Z domain
Direct (DIR) control design

## Slide 20: Introduction
Controller design in digital control systems -Des,gn in Z domain