## Slide 1: Optical Amplifiers
By: Ryan Galloway

## Slide 2: The Goal
Amplify a signal.
Generate extremely high peak powers in ultrashort pulses
Amplify weak signals before photo detection to reduce noise
Regenerate signals in long distance optical communication

## Slide 3: General Types
Doped fiber amplifiers
  EDFA, TDFA, YDFA, PDFA
Semiconductor Optical Amplifiers (SOA)
  Tapered Amplifiers
    BoosTA
  Vertical Cavity SOA
Raman Amplifier
Chirped Pulse Amplification

## Slide 4: Parameters to keep in mind
Maximum gain in dB
Gain Saturation
Saturation power and gain efficiency
Power efficiency
Upper state lifetime
Gain bandwidth
Noise
Sensitivity to back reflections

## Slide 5: Doped Fiber Background Info
Driven by the Telecom Industry

## Slide 6: Erbium Doped Fiber Amplifier
Erbium is pumped with 980nm(for low noise) or 1.45um (higher power)
  Gain in the 1550nm region
Stimulated emission of erbium ions, at signal wavelength
~30nm gain spectrum due to broadening mechanisms
Pump beam and signal must be at different wavelengths
Optical isolators are used at the output, the EDFA is a high gain amplifier

## Slide 7: Other Rare Earth Amplifiers
Same principle as EDFA
Thulium doped fluoride fiber amplifiers (TDFA)
  Pumped at 1047 or 1400nm
  1460-1530nm or 1800-2000nm range
Praseodymium doped amplifiers
  1300nm range
Ytterbium doped amplifiers
  1um range
  Used for industrial processing with very high output power

## Slide 8: Design Issues with Doped Fibers
Nonlinear effects:
  Kerr Effect:
    Change in effective index of refraction from high intensity light
  Raman gain via Stokes wave generation
  Stimulated Brillouin scattering
Losses when no pump beam is present
Doping concentration and quenching

## Slide 9: Semiconductor Amplifiers
Specs:
  wavelength range: 633 to 1480 nm
  input power: 10 to 50 mW
  output power: up to 3 Watt ~30dB gain
  Tunable +/- 20nm
  ~nanosecond upper state lifetime
    Fast response to pump
Typically from group III-V
Advantages:
  Smaller and Less expensive than EDFA
  Electrically pumped
High optical Nonlinearity
  Attractive for signal processing
  Can create all four nonlinear operations
    cross gain modulation
    cross phase modulation
    wavelength conversion
    four wave mixing

## Slide 10: Raman Amplifiers
Most of the time photons scatter elastically (Rayliegh Scattering)
Some photons will scatter inelastically and lose energy
Working Principles:
  Nonlinear process: Stimulated Raman Scattering
  Incident photon excites electron to virtual state
  Electron de-excites down to the vibrational state
Advantages
  Any single mode fiber can be used
  Lower cross talk between signals
  Very broadband operation
Disadvantages
  High optical pump power
  Low Gain ~ 10 dB
  Long length of fiber required

## Slide 11: Chirped Pulse Amplification
How does one make extremely intense ultrashort pulses without any nonlinear distortion or damage to equipment?
  Make a short pulse, spread it out, amplify it, compress it.

## Slide 12: National Ignition Facility
192 beams with .4 meter diameter focused in an attempt to create fusion.
https://www.youtube.com/watch?v=4Cb7iqaN91c

## Slide 13: Bibliography
Ultra-intense lasers: Beyond a petawatt, http://www.nature.com/nphys/journal/v7/n1/full/nphys1897.html
http://www.ecse.rpi.edu/~schubert/Light-Emitting-Diodes-dot-org/chap22/chap22.htm
R. Paschotta, article on 'fiber amplifiers' in the Encyclopedia of Laser Physics and Technology, accessed on 2015-10-08
R. Paschotta, article on 'Raman scattering' in the Encyclopedia of Laser Physics and Technology, accessed on 2015-10-08
https://en.wikipedia.org/wiki/Chirped_pulse_amplification
https://en.wikipedia.org/wiki/Optical_amplifier#Laser_amplifiers
http://www.fiber-optic-tutorial.com/comparison-of-different-optical-amplifiers.html
https://lasers.llnl.gov/about/how-nif-works/beamline/amplifiers
http://www.hanel-photonics.com/tapered_amplifier.html
R. Paschotta, article on 'amplifiers' in the Encyclopedia of Laser Physics and Technology, 1. edition October 2008, Wiley-VCH, ISBN 978-3-527-40828-3