## Slide 1: Transducers
PHYS3360/AEP3630
Lecture 33

## Slide 2: Terminology
Transducers convert one form of energy into another
Sensors/Actuators are input/output transducers
Sensors can be passive (e.g. change in resistance) or active (output is a voltage or current level)
Sensors can be analog (e.g. thermocouples) or digital (e.g. digital tachometer)
Sensor
Actuator
Notes: Energy form conversion: electrical signals, movement, radiant energy, thermal, or magnetic energy, etc.
Sensors/Actuators – both are transducer types
Analog-sensor-produced signals can be digitized

## Slide 3: Transducer types
Quantity being Measured | Input Device (Sensor) | Output Device (Actuator)
Light Level | Light Dependant Resistor (LDR), Photodiode, Phototransistor, Solar Cell | Lights & Lamps, LED's & Displays, Fiber Optics
Temperature | Thermocouple, Thermistor, Thermostat, Resistive temperature detectors (RTD) | Heater, Fan, Peltier Elements
Force/Pressure | Strain Gauge, Pressure Switch, Load Cells | Lifts & Jacks, Electromagnetic, Vibration
Position | Potentiometer, Encoders, Reflective/Slotted Opto-switch, LVDT | Motor, Solenoid, Panel Meters
Speed | Tacho-generator, Reflective/Slotted Opto-coupler, Doppler Effect Sensors | AC and DC Motors, Stepper Motor, Brake
Sound | Carbon Microphone, Piezo-electric Crystal | Bell, Buzzer, Loudspeaker

## Slide 4: Positional Sensors: potentiometer
Processing circuit
Can be Linear or Rotational
Notes: Can be Linear or Rotational

## Slide 5: Positional Sensors: LVDT
Linear Variable Differential Transformer

## Slide 6: Positional Sensors: Inductive Proximity Switch
Detects the presence of metallic objects (non-contact) via changing inductance
Sensor has 4 main parts: field producing Oscillator via a Coil; Detection Circuit which detects change in the field; and Output Circuit generating a signal (NO or NC)
Used in traffic lights (inductive loop buried under the road). Sense objects in dirty environment.
Does not work for non-metallic objects. Omni-directional.
Notes: Used in traffic lights (inductive loop buried under the road). Sense objects in dirty environment.
Does not work for non-metallic objects. Omni-directional.

## Slide 7: Positional Sensors: Rotary Encoders
Incremental and absolute types
Incremental encoder needs a counter, loses absolute position between power glitches, must be re-homed
Absolute encoders common in CD/DVD drives

## Slide 8: Temperature Sensors
Bimetallic switch (electro-mechanical) – used in thermostats. Can be “creep” or “snap” action.
Thermistors (thermally sensitive resistors); Platinum Resistance Thermometer (PRT), very high accuracy.
Creep-action: coil or spiral that unwinds or coils with changing temperature
Notes: Creep-action: coil or spiral that unwinds or coils with changing temperature

## Slide 9: Thermocouples
Two dissimilar metals induce voltage difference (few mV per 10K) – electro-thermal or Seebeck effect
Use op-amp to process/amplify the voltage
Absolute accuracy of 1K is difficult

## Slide 11: Light sensors: photoconductive cells
Light dependent resistor (LDR) cell

## Slide 12: Light level sensitive switch

## Slide 13: Photojunction devices
photodiode
phototransistor

## Slide 14: Photovoltaic Solar Cells
Can convert about 20% of light power into electricity
Voltage is low (diode drop, ~0.6V)
Solar power is 1.4kW/m^2
Notes: Solar power is 1.4kW/m^2

## Slide 15: Photomultiplier tubes (PMT)
Most sensitive of light sensors (can detect individual photons)
Acts as a current source
electrons

## Slide 16: Motion sensors/transducers
Switches, solenoids, relays, motors, etc.
Motors
  DC
    Brushed/brushless
    Servo
    Stepper motors
  AC
Stepper motor
Brushed motor – permanent magnets on armature, rotor acts as electromagnet
Brushless motor – permanent magnet on the rotor, electromagnets on armature are switched
Notes: Brushed motor – permanent magnets on armature, rotor acts as electromagnet
Brushless motor – permanent magnet on the rotor, electromagnets on armature are switched

## Slide 17: Sound transducers
microphone
speaker
Note: voice coil can also be used to generate fast motion

## Slide 18: Piezo transducers
Detect motion (high and low frequency)
Sound (lab this week), pressure, fast motion
Cheap, reliable but has a very limited range of motion

## Slide 19: Summary
We’ve only briefly touched on most basic types
Many other transducers are used/common, almost for any physical quantity one can think of
Processing electronics is often essential: output of many sensors is not linear, needs impedance transform, filtering, etc.
For additional references see
  http://www.electronics-tutorials.ws/io/io_1.html
  Handbook of Transducers by H.N. Norton
  http://www.sparkfun.com