## Slide 1: Portland Cement and Concrete

## Slide 2: How Cement Works
Water mixes with Portland cement and starts a chemical reaction – Hydration
Setting Heat Shrinking
Faster setting = higher heat = shrinkage cracking
(in general)
Cement particles bond to each other over time. The longer they are kept moist, the stronger the bond.

## Slide 3: Cement Types
Type I – normal or standard
Type II – Modified, slight sulfate resistance
Type III – High Early Strength, high heat, quick setting
Type IV – Low heat , slow setting
Type V – Sulfate Resistant

## Slide 4: Air Entraining
  Forms tiny bubbles in the mix
  Resists freeze/thaw effects
  It is often added at cement plant
    IA, IIA, IIIA

## Slide 5: Aggregate
Blend of varying sizes – grading important for economy of mix
Strength, durability, wear resistance critical
Chemical compatibility with cement and reinforcing steel

## Slide 6: Water
Potable or drinkable

## Slide 7: Admixtures
  Accelerators
  Retarders
  Water reducers
  Plasticizers
  Never use admixtures unless they have been called for by the engineer!

## Slide 8: Concrete Mixes
  Sometimes specified by “sack”
  One sack of Portland cement = 94 #
  5 sack mix would have 470 # of cement
  More precise method is by pounds of each ingredient
  Cement
  Water
  Fine aggregate
  Coarse aggregate

## Slide 9: Major Tests for Concrete
  Slump test – workability of the mix
  Air test – determines the amount of air entraining in the mix
  Temperature – may be critical in extreme conditions
  Cylinder test – to determine the design strength at 3,7,&28 days
  Core test – drilled cores from set concrete to test strength

## Slide 10: Reinforcing (Rebar)
Reinforcing bars – provide tensile strength for the composite piece
Welded wire fabric – not considered reinforcing if made of light gage wire-reduces cracking and excess shrinkage in slabs

## Slide 11: Rebar Sizes
Number Diameter #3 3/8” #4 1/2”
#5 5/8”
#6 3/4”
Number is over 8.

## Slide 12: Welded Wire Fabric
6x8 W1.4xW2.0
Longitudinal spacing Transverse wire size
Transverse spacing Longitudinal wire size

## Slide 13: Formwork
  Huge hydrostatic loads (150 pcf approx)
  Bracing critical
  Wall forms require ties through forms
  Column forms
  Release agent

## Slide 14: Weight of Concrete
Consider concrete to weigh about 150 pounds per cubic foot
27 C.F. = about 4000 pounds/ CY
Trucks carry 10 yards = 40,000 #
Trucks weigh about 26,000 #
Total weigh = 66,000 #

## Slide 15: Ready Mix Vs. Site Mix
  Quality control is main concern
  Access to site is a consideration
  Small jobs may us sacked concrete @ 80# per sack (about ½ C.F.)

## Slide 16: Placing Concrete
  Forms braced and leveled. Clean of debris
  Move concrete from truck to placing site
    Chute, buggy, pump, bucket, conveyor belt
  Consolidate (beware of segregation)
  Screed (slab)
  Float (slab)
  Trowel (slab)
  Finish (slab)
  Cure

## Slide 17: Precast Concrete
Precast
Pre-stressed
  Pre-tensioned
  Post-tensioned