## Slide 1: Coal

## Slide 2: What is coal?
Most abundant fossil fuel in the world
Enough coal reserves to last 200 years
Dark sedimentary or metamorphic combustible rock made from swamp plants that died millions of years ago and were transformed by intense heat and pressure

## Slide 3: What is the coal used for?
heating
Burned to turn water into steam, which turns blades of a turbine to generate electricity
Steel production

## Slide 4: HOW IS COAL MADE ???

## Slide 5: Types of Coal
Grades of Coal
  Peat
  Lignite
  Sub‐bituminous
  Bituminous
  Anthracite

## Slide 6: Where is coal?

## Slide 7: Peat
Lowest grade; newest deposit, not true coal
Found in wetlands
Least amount of heating value
Concern: destroying wetlands

## Slide 8: Lignite
Sedimentary rock
Brownish-black coal
High moisture content
“soft”
Used for generating electricity
Carbon content: 20-25%

## Slide 9: Sub-bituminous Coal
Sedimentary rock
Dull black
Harder than lignite, higher energy value
Used for electricity
Carbon content: 30-45%

## Slide 10: Bituminous Coal
Sedimentary rock
Most common type; 50% of US coal reserves
Harder than sub-bituminous coal, more energy
Used for heating and electricity
Carbon content: 45-80%

## Slide 11: Anthracite
Metamorphic rock
“hard” coal, black and shiny
High
highest energy content
Only 1.5% of US coal reserve base (rare)
Carbon content: 80-96%

## Slide 12: Coke
Almost pure carbon
Coal heated with out air to remove any water

## Slide 13: Coal Key
Peat-Brown
Lignite-Yellow
Sub-bituminous-Red
Bituminous-Green
Anthracite-Blue
Coke

## Slide 14: Coal Mining

## Slide 15: Mine Reclamation
Mine reclamation is the process of restoring land that has been mined to a natural or economically usable purpose

## Slide 16: Surface Mining Control and Reclamation Act, 1977
Requires that coal-mining sites be restored to natural areas or productive land

## Slide 17: Cookie Mining