## Slide 1: Bearing Use in Design

## Slide 2: Bearing Terminology
Bearing
Raceway
Rolling Elements
Cage
Lubricant
Seal
=

## Slide 3: Bearing Arrangement Terminology
Cylindrical roller bearing
Four-point contact ball bearing
Housing
Shaft
Shaft abutment shoulder
Shaft diameter
Locking plate
Radial shaft seal
Distance ring
Housing bore diameter
Housing bore
Housing cover
Snap ring

## Slide 4: Radial Bearing Types
Angular Contact
Deep Groove
Self Aligning
Cylindrical Roller
Full Complement
Cylindrical Roller
Needle Roller
Tapered Roller

## Slide 5: Thrust Bearing Types
Cylindrical Roller
Needle Roller
Tapered Roller
Thrust Ball Bearing
Single Direction
Thrust Ball Bearing
Double Direction
Angular Contact

## Slide 6: Bearing Selection – Space
Limited Radial Space
  Choose bearing with low cross-sectional height
  EX. Needle roller and cage assemblies
Limited Axial Space
  Choose bearings that can handle combined loads
  EX. Cylindrical roller, deep groove, needle roller

## Slide 7: Bearing Selection – Loads
Magnitude
  Roller bearings support heavier loads than similar sized ball bearings
  Full complement roller bearings support heavier loads than corresponding caged bearings
Radial
  Some cylindrical roller and all needle roller

## Slide 8: Bearing Selection – Loads
Axial
  Thrust ball bearing and four-point contact ball
  Angular contact thrust ball bearings

## Slide 9: Bearing Selection – Loads
Combined
  Greater the angle of contact, greater ability to handle axial loads

## Slide 10: Bearing Selection – Loads
Moment
  Eccentric loads resulting in tilting moment
  Best: paired single row angular contact bearings or tapered roller bearings

## Slide 11: Bearing Selection – Misalignment
Rigid Bearings
  Deep groove and cylindrical roller
    Cannot accommodate misalignments well
Accommodating Bearings
  Self-aligning ball bearings, spherical roller (radial and thrust)

## Slide 12: Bearing Selection – Speed
Highest Speeds
  Purely Radial Loads
    Deep Groove Ball Bearings
    Self Aligning Ball Bearings
  Combined Loads
    Angular Contact
Thrust bearings cannot accommodate as high speeds as radial

## Slide 13: Seals
Purpose
  Keep contaminants out, and lubricant in the bearing cavity
Types
  Seals in contact with stationary surfaces (static) / sliding surfaces (dynamic)
  Non-contact seals
  Bellows and membranes

## Slide 14: Bearing Arrangement
Locating and Non-locating
  Stiff
    Deep groove ball bearing with cylindrical roller bearing
  Self-Aligning
    Self-aligning ball bearing with toroidal roller bearing

## Slide 15: Selection of Fit
The heavier the load, particularly if it is a shock load, the greater the interference fit
Elements will heat up differently causing expansion
Tolerances on shaft and housing
http://www.skf.com/group/products/bearings-units-housings/ball-bearings/principles/application-of-bearings/radial-location-of-bearings/selection-of-fit/recommended-fits/index.html

## Slide 16: Methods of Location
Locking Washer
  Washer engages keyway in shaft
  Tab is bent over into slot on circumference of nut
Locking Screw
  Prevents nut from turning

## Slide 17: Bearing Load
Dynamic
  Load to failure after 1,000,000 revolutions (ISO 281:1990)
  Shows metal fatigue (flaking, spalling) on rings or rolling elements
Static
  Rotate at slow speeds (< 10 RPM)
  Perform very slow oscillating movements
  Stationary under load for certain extended periods

## Slide 18: Service Life Factors
Contamination
Wear
Misalignment
Corrosion
Cage Failure
Lubrication
Seal

## Slide 19: Designing For Disassembly
Add threaded holes to use screws to ‘jack’ bearings out of housings
Add porting and grooves to use high pressure oil to dismount bearings

## Slide 20: Introducing Pre-Load
Enhance stiffness
Quiet running
Accurate shaft guidance
Compensates for wear and settling
Longer service life

## Slide 21: Bearing Example

## Slide 22: Designing Shafts for Bearings