## Slide 1: Domain-Specific Embedded Systems
Carlos Padilla

## Slide 2: Overview
Automobile Industry
Network Applications

## Slide 3: History
Growth of Electronics in Cars
Programming Languages
  C
  Some C++ but not using all of C++ functionality

## Slide 4: Automotive Segments
Body
Chassis and Safety
Driver Assistance
Powertrain and transmission
Infotainment and Telematics

## Slide 5: Body
Responsible for
  Comfort
  Safety and Networking
    CAN
    MOST
    LIN
    FlexRay
    Ethernet
  Windows
  Doors
  HVAC

## Slide 6: Chassis and Safety
This area is generally concerned with driver Safety
Examples
  Anti-lock Braking System
    Reducing crashes by 30% in regular vehicles, 60% in SUVs
  Tire Pressure Monitoring System

## Slide 7: Driver Assistance
Advanced Driver Assistance System (ADAS)
Adaptive Cruise Control
Radar system
  Blind spot detection
  Crash Detection
High/Low beam detection
360 degree camera support
Map based ADAS support
http://adasis.ertico.com/wp-content/uploads/sites/13/2014/09/ADASIS_Brochure.pdf

## Slide 8: Powertrain and Transmission
Emphasis on improving fuel efficiency
  High pressure injection systems
Meet CO2 emission standards
Hybrid Engines

## Slide 9: Infotainment and Telematics
Multimedia support
  Media player
  Phone Integration
  Bluetooth Support
  3G/4G suppport
  High definition screens
Telematics support
  GPS
  Navigation System

## Slide 10: Automotive quality
Safety is important in automotive systems and hence the quality of the software is very important. Engineers must design and implement their system with the following in mind
  Planning for Murphy’s law
    Plan for unlikely failure
  Fault-tolerant communications
    ACK/NACK, parity, recovery
  Fault-tolerant software
    Ensure system does not fall apart
    Different components may have contradictory information
  Zero-defect software
    Test early and often to avoid defects from being caught too late

## Slide 11: Automotive quality
Risk management and failure modes
  Identify high risk, create plans, and set priorities to deal with them
  ISO 31000
Failure modes and effects analysis (FMEA)
  Occurrence, Severity, Detection
  Multiply these to get Risk Priority Number (RPN)
  High RPN should be dealt with first

## Slide 12: Development
Subsystem interoperability
  Modularity
Software specifications
  SRS document, emphasis on safety
  ISO 830 SRS standard
Software architecture
  Model of how system is organized, hierarchy, relationships
Modeling
  Help engineers understand functional, non functional, and quality requirements for system
Autocoding and drivers
  Converting Diagrams to code, code templates. Drivers to interact with low level hardware

## Slide 13: Testing and Diagnostics
Bench testing
  Code coverage: regression testing, unit testing, etc
Trace and debug
  Ability to find and fix failures in software
Final-phase testing
  Testing in the car, hardware in the loop
Calibration
  Fine-tuning system to maximize performance
Maintenance/ product lifetime support
  Support system for 15 years
Diagnostics
  MIL Data logger, OBD II , DTC

## Slide 14: Automotive Standards
Standards allow engineers to follow similar guidelines
  Allows integration with third party sources
  Promote safety standards
MISRA
  The Motor Industry Software Reliability Association
  MISRA C
AUTOSAR
AEC
  Automobile Electronics Council

## Slide 15: AUTOSAR
Stands for Automotive Open Software Architecture
Purpose is to standardize interfaces, structures, and communication across car manufactures and third party providers
Component based architecture
Issues with AUTOSAR
  Lacks information on timing requirements
  Additional computation and memory needed

## Slide 16: Paper: AUTOSAR Test Automation
Purpose of paper is to develop test automation using AUTOSAR
Car manufactures continue to provide most safety and comfort features
  The addition of these features increases the number of electronics in the car
As number of embedded systems in a car increases so does the cost
  Due to the software needed and testing required
Test automation offers a robust and efficient way of testing the ever increasing number of embedded components

## Slide 17: Client Server Model
A client server design pattern with AUTOSAR was used
AUTOSAR Components
  Client
  Server
Server provides services to the clients
Clients use services provided by server
N >= 0 Clients to 1 Server

## Slide 18: HVAC System
1 Server
  ECU
5 Clients (Control units)
  Blower unit
  Compressor
  Apt sensor
  Expansion valve
  Temperature sensor
Serial Communication (RS232)
  Blower unit, Compressor
CAN Communication
  Apt Sensor, Expansion Valve, Temperature Sensor

## Slide 19: HVAC System: Clients
Blower unit
  Cool down temp of Air-conditioner gas.
  Fan speed depends on gas temperature
Compressor
  Power from Engine
  Transfers AC gas to Evaporator after compressing to low temperature low pressure gas
Apt sensor
  Monitors AC line pressure to avoid accidents
Expansion valve
  Controls force of cool down
Temperature sensor
  Monitors inside and outside temperature
  Transfers temperature difference to ECU (Server) based on user input

## Slide 20: HVAC Control Model

## Slide 21: Test for HVAC

## Slide 22: Strengths of Paper
Make strong case for increased test automation
Through this method ECU and control units could be tested without having to assemble the entire system
Changing out parameters for Engine speed and Compressor torque is easier than attempting to achieve these values manually
Allows for testing a variety of scenario by simply changing a few parameter values
Good Structure
  Outlines purpose, provides background info, explains experiment, good diagrams

## Slide 23: Weaknesses of Paper
Weak Conclusion
  Short, more of summary
Does not address some weakness of AUTOSAR
  Timing requirements
  Extra memory and computational processing
Very short test case list
Some translation issues

## Slide 24: Relevance
As cars system become more complex and filled with additional embedded systems efficient ways of testing must be found to keep costs down

## Slide 25: Safety and Security
Automotive safety
  ISO 26262
  ASIL
Automotive security
  Past: Car alarms etc.
  Present: Hacking
  Future: Counterfeiting (modules)

## Slide 26: Future
Improved Performance
Multicore in vehicle
Mobile connectivity
Self driving cars

## Slide 27: Network Devices
System Architecture
  Networking in Offices and Schools
  Security: Firewalls
Network Planes
  Data, Control, Service, Management
Data Plane
  First component to get data from IO (Ethernet)
  L3 routing, IPsec, firewall
Service Plane
  Handles exception packets
Control Plane
  Protocols to interact with peer networks.
Management Plane
  HMI for network

## Slide 28: Multicore System on Chip (SoCs)
Contain multiple general purpose cores and multiple peripheral controllers
Reduces cost by integrating multiple cores and IOs into one board
Parser
  ARM, MIPS
OS
  Linux, BSD

## Slide 29: Packet engine hardware (PEH) Block
Purpose is to distribute data to multiple cores
  On top of Ethernet layer
Parts that make up PEH block
  Parser
  Distribution
  Classification
  Scheduler, queues and channels
  Accelerators

## Slide 30: PEH Block: Parser
Parse the messages from the Ethernet data block
Check validity of message
If valid extracts fields from data packet
Capable of reassembling fragments

## Slide 31: PEH Block: Distribution and Classification
Distribution
  Extract data from fields to put place packet in queue
  CRC-32 and CRC-64 used to hash packets
Classification
  Allows software to assign specific queues for types of packets
  Extracts value from packet
  Certain packets like GUI may be of higher priority and shouldn’t be left to hash

## Slide 32: PEH Block: Scheduler
Queues
  Packets placed her by Distribution and Classification
  Also used by cores to send out packets or access hardware acceleration engines
Channels
  Bundles set of Queues
  Cores can access data from one or more channels

## Slide 33: PEH Block: Accelerators
Used to handle computationally intensive algorithmic tasks away from cores
Examples
  Cryptography
  Pattern matching
  Compression/decompression
  De-duplication
  Time management
Ingress Acceleration
  Incoming packets
Engress Acceleration
  Outgoing packets to interfaces

## Slide 34: PEH Block: Buffer Manager
Handles allocation and deallocation of memory
Pools of memory
Avoid software worrying about this memory management

## Slide 35: Pipeline programming model
Different Functions processed by different multiple cores
Used often when migrating from single core to multi core to avoid concurrency issues
High Complexity
  Throughput is based on functions that demand the most cores, losing efficiency on functions that need less cores
  Higher latency of packets (queuing tasks to other functions)
  Breaking up functions into multiple packets may be difficult

## Slide 36: Run-to-completion programming
All cores process all functions
Focus here is in how the work flow is distributed to each flow
Requirements needed to consider
  Important packets maintain order within flow
  Performance scaling expected to be linear
  Latency from ingress and egress should be low

## Slide 37: Data-plane infrastructure (DP-Infra)
Used to improve modularity
Many forwarding engines (FE)
Separate common functionality among Fes into modules
  Allows reuse
  Maintainability
  Portability
Used by FEs to interact with Acceleration Engines (AEs)

## Slide 38: Forward Engine (FE)Structure
First, parses packet headers to extract desired field data.
Next, uses extracted data to match flow context in flow database
  Exception packets do not match
Then, process packet based on state of information
  Packet may be modified
Lastly, send out updated packet to next FE
  Uses DP-Infra

## Slide 39: Network application programming Techniques
Hash tables are a common data structure used in network programming
  Searching for Packet should be fast to maintain good performance
Avoid locks
  Important for packet processing to avoid lock state as much as possible
  If cores are made to spin no performance improvement is achieved
  Locks are still important for maintaining data integrity
Avoid reference counting
  Read-Copy-Update (keep read side unlock, but write side is still locked)
  Reference counting used to avoid flow context while being used
  Should be avoided because locks are required
  Prone to errors, if count is not kept properly

## Slide 40: Network application programming Techniques (cont)
Safe reference mechanism
  A safe way to access data from a neighboring node
  API functions used to allow neighbors to access data
  Avoid use of pointers
  Removes need for reference counting
Flow parallelization
  One data flow processed by one core at a time
  Different flows processed across multiple cores

## Slide 41: Statistics
Reducing cache thrashing is important
  Flow statistics
  Global statistics
  Keeping data in cache is important to avoid stalls from core
  Each core can have its’ own statistics and own cache lines
Statistics acceleration
  Multicore SoC with this feature make the previous techniques unnecessary

## Slide 42: General performance techniques
Keep relevant data in cache to avoid stalls
  Cycles in which the core is just waiting
Software-directed prefetching
  Software used to move data in DDR memory into L1 cache
Compiler Built-ins for likely/unlikely
  Cores typically expect instructions to be right next to each other
  Branching can cause instructions to be DDR instead of cache
  This compiler built in setting is used to determine code that is mostly likely to operate together
Keeping important data in cache
  Avoid data moving into DDR when it will be used often
  Need to be careful when locking data into cache because it minimizes cache available to CPU

## Slide 43: General coding guidelines
Avoid initialized variables until necessary not when declared
  Reduced unnecessary time spent by core cycles if that data is not needed
Define inline macros
Avoid buffer copies, string comparisons and allocations
Use hardware acceleration when possible

## Slide 44: Linux operating system
Popular operating system for network devices
Execution spaces
  Kernel
  User space
Kernel space used for data and service plane programming
User space is now also being looked at for data plane programming
Translation lookaside buffer (TLB) misses associated with user-space programming
Access to hardware peripherals and hardware accelerators
Deterministic performance

## Slide 45: Translation lookaside buffer (TLB)
User space programs use virtual addresses
Virtual addresses do not have one to one correspondence with physical addresses
TLB is used to get physical address from virtual address
Problem
  When address is not found TLB a fault is generated and the kernel space must now resolve it
  This decreased performance greatly if there are many misses
Solutions
  Using Huge pages (hugetlbfs) can reduce misses
  Some multicore SoC come with hardware page walk, to avoid performance hits when page is missed

## Slide 46: Access to hardware
Problem
  Hardware peripherals and hardware accelerators is obtained through physical memory
  Accessing hardware through User space involves context switch and buffer copying
Solution
  Linux provides memory mapping so hardware registers can be accessed directly by user space
  Multicore SoC with IOMMU can convert virtual memory to physical memory

## Slide 47: Deterministic performance
Problem
  Linux General Purpose OS which causes cores to be share across multiple tasks
  Cores are not dedicated and hence cannot be deterministic
Solution
  Threads can be created with an affinity to a particular core
  Cores can be dedicated to threads and Linux will not assign other processes or threads to these cores

## Slide 48: Questions?

## Slide 49: Sources
(2013-04-01). Software Engineering for Embedded Systems: Methods, Practical Techniques, and Applications (Expert Guide) (Kindle Location 19943). Elsevier Science. Kindle Edition.
H. Moon, G. Kim, Y. Kim, S. Shin. Automation Test Method for Automotive Embedded Software Based on AUTOSAR, Fourth International Conference on Software Engineering Advances, 2009. ICSEA '09, September 2009
The ADAS Horizon Concept http://adasis.ertico.com/wp-content/uploads/sites/13/2014/09/ADASIS_Brochure.pdf