## Slide 1: Acoustic Features for Speech Recognition: From Mel-Frequency Cepstrum Coefficients (MFCC) to BottleNeck Features(BNF)
F01921031 鍾承道

## Slide 2: Outline
Mel-Frequency Cepstrum Coefficients
  DFT
  Mel Filter Bank
  DCT
From human knowledge to data driven methods
  Supervised objective
  Machine Learning
  DNN
  Bottle Neck Feature

## Slide 3: What are acoustic features?
Features used to describe characteristics of speech signal at every time instant.
Automatic Speech Recognition (ASR) systems take these features as input and apply machine learning model to map them into a sequence of words . (for more info, take Prof. Lee’s Course)

## Slide 4: What are acoustic features?
Consists of two dimensions :
  Features space
  Time
For Example:
  Fourier transform coefficients, Spectrogram, MFCC, Filter bank output, BNF…
Desired properties of acoustic features for ASR:
  Noise Robustness
  Speaker Invariance
From the Machine Learning point of view, the design of the feature has to be considered with the learning method applied.

## Slide 5: Mel-Frequency Cepstrum Coefficients(MFCC)
The most popular speech feature in from 1990 to the early 2000s
It is the result of countless trial and errors optimized to overcome noise and speaker variation issues under the HMM-GMM framework for ASR.

## Slide 6: MFCC (from wiki)
Take the Fourier transform of (a windowed excerpt of) a signal.
Map the powers of the spectrum obtained above onto the mel scale, using triangular overlapping windows.
Take the logs of the powers at each of the mel frequencies.
Take the discrete cosine transform of the list of mel log powers, as if it were a signal.
The MFCCs are the amplitudes of the resulting spectrum.

## Slide 7: MFCC
Discrete Fourier Transform
Mel Filter bank
Discrete Cosine Transform
Hamming
Window
Time Domain Signal
MFCC

## Slide 8
 Hamming Window
Hamming window
: some operator
w : window shape

## Slide 9: MFCC
Discrete Fourier Transform
Mel Filter bank
Discrete Cosine Transform
Hamming
Window
Time Domain Signal
MFCC
window size = 32ms
hop size 10 ms
For wav encoded at 16k Hz, 0.032 * 1600 = 512 sample points
512
Short time Fourier transform
Dimension: 512

## Slide 10: Mel-Filter Bank Outputs
The design is based on human perception:
wider bands for higher frequencies (less sensitive)
narrower bands for lower frequencies (more sensitive)
The response of the spectrogram is recorded as the feature

## Slide 11: MFCC
Discrete Fourier Transform
Mel Filter bank
Discrete Cosine Transform
Hamming
Window
Time Domain Signal
MFCC
512
40
Response of spectrogram
Mel filter banks:
Triangular band-pass filters are selected

## Slide 12: Cepstral Coeffiencents
Time -> DFT -> frequency
  “Spectral” domain
Frequency -> DCT -> ??(like time)
  “Cepstral” domain
Main reason is for data compression
It also suppresses noise: white noise can spread over entire spectrum (like a bias term), taking dct of the spectrogram reduces the damage to only 1 dimension (dc term) in cepstral domain

## Slide 13: MFCC
Discrete Fourier Transform
Mel Filter bank
Discrete Cosine Transform
Hamming
Window
Time Domain Signal
MFCC
512
40
DCT compression:
40 spectral coefficients
into
12 cesptral coefficients
12

## Slide 14: The final step
We get a 12 dimension feature for every 10 milliseconds of voice signal
Energy Coefficient(13th ):
  The log of the energy of the signal
Delta Coefficient(14~26th ):
  the difference between the neighboring features
  Measures the change of features through time
Double Delta Coefficient(27~39th ):
  the difference between the neighboring delta features
  Measures the change of delta through time

## Slide 15: MFCC
Discrete Fourier Transform
Triangular Filter bank
Discrete Cosine Transform
Hamming
Window
Time Domain Signal
Add delta, double delta
MFCC
512
40
12
39

## Slide 16: The MFCC framework
The action of applying DFT, mel-Filter bank, and DCT can be viewed as multiplying the input feature by a matrix with predefined weights.
These weights are designed by “human heuristics”

## Slide 17: MFCC
Discrete Fourier Transform
Triangular Filter bank
Discrete Cosine Transform
Hamming
Window
Time Domain Signal
Add delta, double delta
MFCC
512
40
12
39
Matrix
Scaling
Function

## Slide 18: Improvement of the MFCC framework
Weight matrix 1
Why not let the data decide what the values of the matrix should be?
Human Knowledge -> Data Driven
Time Domain Signal
Activation Function 1
Weight matrix 2
Activation Function 2
…
Weight matrix L
Activation Function L
Feature

## Slide 19: How do we let the data drive the coefficients?
Weight matrix 1
This depends on your objective: What do you want to map the information to?
  For speech recognition it is usually words or phones.
Input Signal
Activation Function 1
Weight matrix 2
Activation Function 2
…
Weight matrix L
Activation Function L
Feature
Output, objective

## Slide 20: Data driven transformations
Weight matrix 1
The task for ASR:
  .
Input Signal
Activation Function 1
Weight matrix 2
Activation Function 2
…
Weight matrix L
Activation Function L
Feature
Output, objective
Input speech features
model parameter
sequence of words

## Slide 21: Machine Learning
This is done in two phases:
In the learning phase, we learn the model parameters on training data, which are (, ) pairs.
In the testing phase, we fix the weights and apply the transformation on to get
Input speech features
model parameter
sequence of words

## Slide 22: The Deep Neural Network
Weight matrix 1
This is the exact formulation for a machine learning technique called the deep neural network
Input Signal
Activation Function 1
Weight matrix 2
Activation Function 2
…
Weight matrix L
Activation Function L
Feature
Output, objective

## Slide 23: The Deep Neural Network
Bigger/Deeper network -> better performance
  Requires more data, more computers to train
All the big players: Apple, Google, Microsoft,… meet these requirements
This is why the technique is so popular
Weight matrix 1
Input Features
Activation Function 1
Weight matrix 2
Activation Function 2
…
Weight matrix L
Activation Function L
Feature
Output, objective

## Slide 24: BottleNeck Features(BNF)
Features extracted at the final layer right before the output are called bottleneck features
They usually outperform conventional features on their specific task.
Weight matrix 1
Input Feature
Activation Function 1
Weight matrix 2
Activation Function 2
…
Weight matrix L
Activation Function L
BNF
Feature
Output, objective

## Slide 25: BottleNeck Features(BNF)
Often BNFs are used as the input to another DNN. The recursion goes on and on.
It is not a far stretch to say that the MFCC technique is obsolete by today’s standard.
Weight matrix 1
Input Feature
Activation Function 1
Weight matrix 2
Activation Function 2
…
Weight matrix L
Activation Function L
BNF
Feature
Output, objective

## Slide 26: References
Xu, Min, et al. "HMM-based audio keyword generation." Advances in Multimedia Information Processing-PCM 2004. Springer Berlin Heidelberg, 2005. 566-574.
Zheng, Fang, Guoliang Zhang, and Zhanjiang Song. "Comparison of different implementations of MFCC." Journal of Computer Science and Technology 16.6 (2001): 582-589.
Hinton, Geoffrey, et al. "Deep neural networks for acoustic modeling in speech recognition: The shared views of four research groups." Signal Processing Magazine, IEEE 29.6 (2012): 82-97.
http://en.wikipedia.org/wiki/Mel-frequency_cepstrum
Professor Lin-Shan Lee’s slides
Evermann, Gunnar, et al. The HTK book. Vol. 2. Cambridge: Entropic Cambridge Research Laboratory, 1997.