## Slide 1: Sensors
EE 5351
Lecture 7

## Slide 2: Sensors Are…
Extremely sensitive to some aspect of the local environment (temp, sound level, motion, etc.)
Extremely insensitive to all other factors
Able to create a linear response to measured changes in that environmental variable
Able to transduce the measurements into a useable signal

## Slide 3: A few sensors…
www.societyofrobots.com

## Slide 4: Types of Sensors:
Position/Orientation: GPS, Accelerometer, digital compass, Shaft Encoder
Temperature: Bi-metallic, Thermistor, Infra-Red
Sound: Microphone
Object Location: IR, Accoustic (SONAR), Laser Range Finder
Force/Pressure: Piezo-Resistive, Metallic
Magnetic Field: Hall Effect

## Slide 5: Piezoelectric Effect
Wikipedia.org
In certain Crystals and special ceramics, the crystaline structure deforms under pressure to produce a measurable voltage
Excellent Force
Transducer
Reversible: V F or F  V

## Slide 6: Draw Your Own Strain Gauge!?!?
Paper in NATURE by Cheng-Wei Lin, Zhibo Zhao, Jaemyung Kim & Jiaxing Huang
“Pencil Drawn Strain Gauges and Chemiresistors on Paper”

## Slide 7: Hall Effect

## Slide 8: Output From Transducers (Sensors)
Analog or Digital
Wired or Wireless
Passive/Active

## Slide 9: Analog Signals
0-5 Vdc
-5 to +5 Vdc
4-20 mA Current
Pulsed (Pulse frequency proportional to measured amplitude)

## Slide 10: ADC (Analog to Digital Converter)
Periodically sample an Analog Sensor signal and convert it to a digital word
ADC has finite precision, usually +/- ½ bit
Leads to Quantization Error
Accuracy also limited by linearity of measurement process, bandwidth and sampling frequency, aliasing error, etc.
Accuracy usually summarized by Effective Number of Bits (ENOB)

## Slide 11: QUANTIZATION:
Quantization is determined by:
  - The resolution (R) of the ADC (No. of Bits)
  - The full-scale voltage range (span)of the input
Q = Span/(2R-1)
Example: 8-bit ADC with span of -5 to +5 volts: Q = 10/255 = 39.2 mV per bit

## Slide 12: Example:
Let’s Look at applying a temperature sensor, AD590 to an ATMEGA328 ADC port:
ATMEGA: 10-Bit resolution, +/- ½ bits, Span = 0-5 Volts
Analog Devices AD 590: Output: 1 uA per Kelvin, terminated by a 10 k-ohm resistor