## Slide 1: Distributed Control: Echelon’s view of the Internet of Things
Bob Dolin’s position paper
Fred Baker’s presentation

## Slide 2: Distributed control in the “Internet of Things”
Types of “real time” in communications
  Normal Internet communications
    Moving files, exchanging text, in a static network
    Human time scales, nobody dies if something is late
  Space: Command/Telemetry
    Constant feedback, occasional configuration changes
    Remote object time scales, nobody dies if something is late
  Distributed Control – machine to machine
    Continuously changing variables to control the behavior of an application
    In some applications, people die, or are annoyed, or the purpose is not served if time scales of interest are not observed
Notes: Distributed control is characterized by a network of machines that interact and cooperate to achieve a system purpose. This cooperation has real time constraints according to the application being implemented. Violating these constraints makes the application not work with consequences ranging from annoyance all the way to loss of property or even of life.

## Slide 3: Example of distributed control: ANSI/CEA 709.1, EN-14908-1, GB/Z 20177.1
Bellagio Fountain
  http://www.5min.com/Video/Learn-About-the-Bellagio-Fountains-278834664
Numerous control points
  Sometimes addressed as a group
  Sometimes addressed individually
Paradigm:
  Central controller sets variables
  Actions are published as status
  Status changes published on a node affect the actions of the nodes that are subscribed to the status change
NACKs
  May be appropriate for scaling when moving large amounts of data
Positive Acknowledgement
  Need for commands
  Retransmission within loss variance
Notes: http://www.5min.com/Video/Learn-About-the-Bellagio-Fountains-278834664 is a video of the Bellagio fountains. Things to note – differences in delta velocity (they might cut in or out, or add pressure or drop it over a period of time), angular momentum (straight up, twirling in circles, etc), and sequence (a group all at once, or a group in sequence).
Consider the implications of a three second RTO (one spray does something different and it’s obvious), a missed command (maybe something keeps spraying or fails to spray?), etc.
Application to industrial control – the robot keeps turning and injures someone/something or doesn’t turn and fails to do its job.
Consider the implications for Fukushima reactors: are the rods really in?

## Slide 4: Network stack requirements (assumptions made by application) #1
Retransmission:
  Network recovers from packet loss or informs application
  Recovery is timely: on the order of RTTs, not seconds
Network engineering meets application requirements
Network independent of MAC/PHY
Scale
  Thousands of nodes
  Multiple link speeds
Multicast
  Throughout network
  Reliable (positive Ack)
Duplicate suppression
Notes: To meet the response time requirements of larger networks, routers are used to segment traffic and compression is used to increase link bandwidth – but, since packets can cross routers compression of the L3 header is very desireable.

## Slide 5: Network stack requirements (assumptions made by application) #2
Emergency messages
  Routed and/or queued around other traffic
  Other traffic slushed as delivered
Routine traffic delivered in sequence
Separate timers by peer/message
Polling of nodes
  Sequential
  Independent of responses
Paradigm supports peer-to-peer
  Not everything is client/server

## Slide 6: Network stack requirements (assumptions made by application) #3
Capabilities:
  Discover nodes
  Discover node capabilities
  Deliver multi-segment records (files)
Exchange of multi-segment records
Network and application versioning
Simple Publish/Subscribe parsers
Security
  Strong encryption,
  Mutual authentication,
  Protection against record/playback attacks
  Suite B ciphers