## Slide 1: Integrating concurrency control and energy management in device drivers
Presented By
Ahmed Elnably and Andrew Sedlmayr
ELEC 518
Rice University

## Slide 2: Sensor Networks
Where can we find them?
  Simple answer: Everywhere!!
Industrial applications:
  Petroleum
  Radiation detection (Japan)
  Global warming
  Weather forecasting (Sometimes they get it right!!!)

## Slide 3: Challenges
Ease of use
Withstand Harsh environmental conditions
Mobile
Light weight
Low power
  Small battery
  Energy Harvesting
Communication failures
Dynamic network topology
Must run unattended from days to years
Notes: The main characteristics of a sensor network include:
Power consumption constrains for nodes using batteries or energy harvesting
Ability to cope with node failures
Mobility of nodes
Dynamic network topology
Communication failures
Heterogeneity of nodes
Scalability to large scale of deployment
Ability to withstand harsh environmental conditions
Easy of use
Unattended operation.

## Slide 4: Kevin Klues
U of Washington for masters
UC Berkeley for PhD

## Slide 5: Chenyang Lu
Kevin’s masters adviser
Research topics includes sensor networks and real time systems
Has 4 papers cited more than 50 times, 3 about sensor networks

## Slide 6: Vlado Handziski
Researcher at Technische Universität Berlin in the Telecommunication Networks Group (TKN)
Research interests Wireless sensor networks

## Slide 7: Adam Wolisz
Prof in Technische Universität Berlin, he founded the TKN
One of his research interests are sensor networks

## Slide 8: David Culler
Chair of CS department at UC Berekely
One of the inventors of TinyOS, the most famous sensor networks’ OS
37 50+ citation papers! Most of them in sensor networks

## Slide 9: David Gay
Was a programming language research in Intel research labs, currently in Google
Helped invent TinyOs

## Slide 10: Philip Levis
Assistant professor at Stanford
His top 8 cited papers (40+ citations) are about sensor networks
Research interest includes sensor networks

## Slide 11: Motivation
Traditional Embedded Operating Systems
  VxWorks – Multicore, preemptive, blocking
  QNX – Multicore, Microkernel architecture, POSIX
  eCos – One process, preemptive, multiple threads
  TinyOS – Single Thread/Stack, non-blocking
Difficult to manage energy in traditional Operating Systems
  Hard to tell the OS about future application workloads
  All energy management logic pushed out to the application
  Optimal energy savings at cost of application complexity
Notes: eCos (embedded configurable operating system) is an open source, real-time operating system intended for embedded systems and applications which need only one process with multiple threads. It is designed to be customizable to precise application requirements of run-time performance and hardware needs. Essentially, this enables eCos developers to create their own application-specific operating system
VXWorks
The key features of the current OS are:
Multitasking kernel with preemptive and round-robin scheduling and fast interrupt response
User-mode applications ("Real-Time Processes", or RTP) isolated from other user-mode applications as well as the kernel via memory protection mechanisms.
SMP and AMP support
Fast, flexible inter-process communication including TIPC
Error handling framework
Binary, counting, and mutual exclusion semaphores with priority inheritance
Local and distributed message queues
POSIX PSE52 certified conformance in user-mode execution environment[13]
File systems: High Reliability File System (HRFS), FAT-based file system (DOSFS), Network File System (NFS)
IPv6 networking stack
VxSim simulator
QNX
As a microkernel-based OS, QNX is based on the idea of running most of the OS in the form of a number of small tasks, known as servers. This differs from the more traditional monolithic kernel, in which the operating system is a single very large program composed of a huge number of "parts" with special abilities. In the case of QNX, the use of a microkernel allows users (developers) to turn off any functionality they do not require without having to change the OS itself; instead, those servers are simply not run. With the QNX microkernel, kernel operations are relatively few and of short duration. This minimal locking approach improves the performance of the rest of the system because neither BKL or fine grained locking approaches are necessary.
TinyOS
TinyOS is a free and open source component-based operating system and platform targeting wireless sensor networks (WSNs). TinyOS is an embedded operating system written in the nesC programming language as a set of cooperating tasks and processes. It is intended to be incorporated into smartdust. TinyOS started as a collaboration between the University of California, Berkeley in co-operation with Intel Research and Crossbow Technology, and has since grown to be an international consortium, the TinyOS Alliance.
Because sensornets have limited resources and different use cases than traditional timesharing systems they tend to run small, customizable OSs with flexible abstraction layers. In practice sensornet operating systems (TinyOS, Contiki, MOS) like their embedded siblines, provide minimal energy management support. eCOS and VxWorks have interfaces for processor power control but peripheral device control is left to the application. TinyOS has power control interfaces that the application must explicily invoke.

## Slide 12: Existing OS Approaches
Dynamic CPU Voltage Scaling
  Vertigo – Application workload classes
  Grace OS – Explicit realtime deadlines
Disk Spin Down
  Coop-IO – Application specified timeouts
Energy Allocation
  Cinder Operating System – Reserves and Taps
  ECOSystem – Currentcy
ACPI
  OS directed configuration, power and thermal management of computing platforms
Notes: Vertigo
Power management extensions for linux. Automatically classifies machine utilization into different types of episodes and automatically assigning deadlines to them. Deadline and classification information is derived from communication patterns between the executing tasks based on observations in the OS kernel.
Vertigo showed that having a process tell the OS its workload class greatly outpreforms simple hardware heuristics and fixed-interval averaging.
GRACE-OS integrates dynamic voltage scaling into soft real-time scheduling and decides how fast to execute applications in addition to when and how long to execute them. GRACE-OS makes such scheduling decisions based on the probability distribution of application cycle demands, and obtains the demand distribution via online profiling and estimation.
Demonstrates that receiving explicit real-time deadlines from applications allows an OS to reduce energy further.
Coop-I/O
Applications can declare open, read and write operations as deferrable and even abortable by specifing a time-out and a cancel flag. This information enables the operating system to delay and batch requests so that the number of power mode switches is reduced and the device can be kept longer in a low-power mode.
Cinder Operating System
Reserves and Taps – Isolation, Delegation, and Subdivision.
A reserve describes a right to use a given quantity of a resource, such as energy. When an application consumes a resource the Cinder kernel reduces the values in the corresponding reserve. The kernel prevents threads from performing actions for which their reserves do not have sufficient resources.
A tap transfers a fixed quantity of resources between two reserves per unit time, which controls the maximum rate at which a resource can be consumed.
Isolation – Isolate energy consumption (Same as CPU, Disk, Memory).
Delegation – Loan any of its available energy to another principal.
Subdivision – Partition available energy.
ECOSystem
Currentcy – Gives an application the ability to spend a certain amount of energy, up to a fixed cap. Works great for simple large applications but falls short when confronted with the complex multiple principle applications of today’s mobile systems. Ie, Web browsers run active code as well as plugins.
ACPI
ACPI establishes industry-standard interfaces enabling OS-directed configuration, power management, and thermal management of mobile, desktop, and server platforms. Defines platform-independent interfaces for hardware discovery, configuration, power management and monitoring. The specification is central to Operating System-directed configuration and Power Management (OSPM); which therefore removes device management responsibilities from legacy firmware interfaces. ACPI’s logic requires dedicated peripheral hardware support that the simple, low-power chips common to embedded systems do not have.
Despite all of these advances most modern operating systems still use very simplistic energy management policies. Behind all of the advanced libraries applications still use APIs which were designed before energy constraints were a major concern.

## Slide 13: Device power management
Device Drivers Power Management
  Mac OS X
  Linux 2.6
  Windows
ACPI
  Platform Independent Specification
  Hardware Support
    Function Fixed Hardware Interface relies on AML
  ACPI Component Architecture
  Global States: G0-G3, (G0)S0, (G1)S1-S4, (G2)S5
  Processor States: C0-C3
  Device States: D0-D3
  Performance States: P0-Pn (C0, D0)
Notes: ACPI Advanced Configuration and Power Interface
Bytecode from an external source must be run by the system with full privileges
Function Fixed Hardware interfaces are platform-specific features, provided by platform manufacturers for the purposes of performance and failure recovery
The complexity of the ACPI specification leads to a lengthy and difficult implementation in OS software. The purpose of the ACPI Component Architecture is to simplify ACPI implementations for operating system vendors (OSVs) by providing major portions of an ACPI implementation in OS-independent ACPI modules that can be easily integrated into any OS.
Global states
G0 (S0): Working
G1, Sleeping subdivides into the four states S1 through S4:
S1: All processor caches are flushed, and the CPU(s) stop executing instructions. Power to the CPU(s) and RAM is maintained; devices that do not indicate they must remain on may be powered down.
S2: CPU powered off
S3: Commonly referred to as Standby, Sleep, or Suspend to RAM. RAM remains powered
S4: Hibernation or Suspend to Disk. All content of main memory is saved to non-volatile memory such as a hard drive, and is powered down.
G2 (S5), Soft Off: G2 is almost the same as G3 Mechanical Off, but some components remain powered so the computer can "wake" from input from the keyboard, clock, modem, LAN, or USB device.
G3, Mechanical Off: The computer's power consumption approaches close to zero, to the point that the power cord can be removed and the system is safe for dis-assembly (typically, only the real-time clock is running off its own small battery).
Device states
D0 Fully On is the operating state.
D1 and D2 are intermediate power-states whose definition varies by device.
D3 Off has the device powered off and unresponsive to its bus.
The CPU power states
C0 is the operating state.
C1 (Halt) is a state where the processor is not executing instructions, but can return to an executing state essentially instantaneously. All ACPI-conformant processors must support this power state. Some processors, such as the Pentium 4, also support an Enhanced C1 state (C1E or Enhanced Halt State) for lower power consumption.
C2 (Stop-Clock) is a state where the processor maintains all software-visible state, but may take longer to wake up. This processor state is optional.
C3 (Sleep) is a state where the processor does not need to keep its cache coherent, but maintains other state. Some processors have variations on the C3 state (Deep Sleep, Deeper Sleep, etc.) that differ in how long it takes to wake the processor. This processor state is optional.
Performance states
These states are implementation-dependent, but P0 is always the highest-performance state, with P1 to Pn being successively lower-performance states, up to an implementation-specific limit of n no greater than 16.
P-states
P0 max power and frequency
P1 less than P0, voltage/frequency scaled
Pn less than P(n-1), voltage/frequency scaled

## Slide 14: Case Study
Mac OS X
  Device Drivers live in the kernel space (KEXTs)
    Directly access hardware devices
    Use primary interrupts
  I/O Kit
    Device interface - user space library through which the application communicates with a device.
    User client – in-kernel object that provides a connection between the device driver and application in user space
  POSIX
  Device Drivers live in the kernel space (KEXTs)
    Directly access hardware devices
    Use primary interrupts
Notes: The I/O Kit also provides services, accessible through a procedural interface, for obtaining device information and accessing devices from non-kernel code. By using this interface, you can obtain the hardware support your application needs without taking on the complexity of writing kernel-resident code.
A user client is an in-kernel object that inherits from IOService and provides a connection between an in-kernel device driver or device nub and an application or process in user space. Some documentation uses the term “user client” to refer to the combination of the user-space device interface and the in-kernel user client object, but for this discussion, “user client” refers to the in-kernel object alone.
The I/O Registry is a dynamic database that describes a collection of ”live” objects, each of which represents an I/O Kit entity (such as a driver, family, or nub). You can think of the I/O Registry as a tree with a nub representing the computer’s main logic board at the root, and various device drivers and nubs as the leaves. In response to the addition or removal of hardware or other changes in the system, the I/O Registry automatically updates to reflect the current hardware configuration.
A driver personality is a dictionary of key-value pairs that specify device property values, such as family type, vendor name, or product name. A driver is suitable for any device whose properties match one of the driver’s personalities. In its Info.plist file, a driver stores its personalities as values of the IOKitPersonalities key.
Driver matching is the process the I/O Kit performs at boot time (and whenever the system’s hardware configuration changes) to find in-kernel device drivers for all devices currently attached to the system. When it finds the driver personality that is most suitable for a particular device, the I/O Kit instantiates that personality, places a copy of its personality dictionary in the I/O Registry, and (in most cases) starts the driver.
A matching dictionary is a dictionary of key-value pairs that describe the properties of a device or other service. You create a matching dictionary to specify the types of devices your application needs to access. The I/O Kit provides several general keys you can use in your matching dictionary and many device families define specific keys and matching protocols. During device matching (described next) the values in a matching dictionary are compared against nub properties in the I/O Registry.
Device matching is the process of searching the I/O Registry for objects representing a specific device or device type in the current system. For example, an application or other code running in Mac OS X can initiate a search for all USB storage devices. In device matching, the I/O Kit compares the keys and values in the matching dictionary an application supplies with a device nub’s properties stored in the I/O Registry.
A device file is a special file the I/O Kit creates in the /dev folder for each serial and storage device it discovers. If your application needs to access such a device, you use I/O Kit functions to get the path to the device and use the POSIX API to communicate with it.

## Slide 15: Case Study
Mac OS X
  Power Events
    Sleep – All drivers must respond
    Wake – All drivers must respond
    Shutdown – Drivers do not need to respond
  The Power Plane: A Hierarchy of Power Dependencies
  Devices and Power States
    Off and On required
    Power State Attributes
      The capability of the device while in a given state
      The device’s power requirements of its power parent
      The power characteristics the device can provide to its power children
      The version of the power-state structure the device uses to store its power-state information
  Two Types of Drivers
    Passive – Responds to system power events
    Active – Performs tasks such as deciding when the device should become idle and changing the device’s power state
Notes: Mac OS X tracks all power-managed devices in a tree-like structure, called the power plane, that captures the power dependencies among devices. A device, usually a leaf object in the power plane, generally receives power from its ancestors and may provide power to its children. For example, because a PCI card depends for power on the PCI bus to which it’s attached, the PCI card is considered to be a power child of the PCI bus. Likewise, the PCI bus is considered to be the power parent of the devices attached to it.
An example of a passive driver is the AppleSmartBatteryManager driver present in most Macintosh laptop computers. The AppleSmartBatteryManager driver provides battery-status information to the battery-status menu bar item; when the system is about to sleep, the driver simply stops polling the battery for status information. A good example of an active driver is the built-in audio chip driver, because it performs its own idleness determination to allow the audio hardware to power off when it is not in use. If there is no sound coming out of a laptop's or desktop's internal speakers, the audio hardware will drop into a low power mode until it is needed.

## Slide 16: Embedded OS
QNX
  Why not use APM or its successor ACPI?
  Application-driven framework
    Power manager – Process that implements the system power management policy
    Power-managed objects – Hardware components that can be independently power managed
    Power-aware application – User applications that interact with the power manager
    Persistent storage service – Preserves hardware and software configuration details during low power modes
    BSP support – Board specific initial program loader
Notes: Many assumptions that are made about devices in a “normal” machine cannot be made in embedded machines, and the hardware and firmware of embedded machines generally provides much less assistance to the kernel for device discovery. Often, many of an embedded machine’s peripherals are connected via an unconventional bus which provides no facilities for systematic scanning or probing of devices.
When the device depends on other devices being enabled, the situation is a little more complex. However the driver will generally know what the other devices are and their drivers, so it is usually quite simple to create an ad-hoc interface whereby one driver can ask the other to enable the device it requires.
The two main industry standards for PM -- APM and its successor ACPI -- deal with PCs, not embedded systems. The older APM standard was BIOS-oriented (how many embedded systems even have a BIOS?). The newer ACPI is more OS-focused and therefore more sophisticated, but the standard expressly concerns itself with desktops, laptops, and servers. An OS can never anticipate the application-specific scenarios of embedded systems and make appropriate power policy decisions.
The QNX PM framework is precisely that -- a framework or set of mechanisms that developers can use to control and manage power in their embedded systems. The OS doesn't impose a power policy. Instead, you create your own policy based on the specific needs of your application.
Power manager
A process that implements the system's PM policy. This policy is user-written -- the system designer creates a custom policy for the embedded system, and has full control over device power modes for the various operational modes of the system.
Power-managed objects
These represent hardware or software components that can be independently power-managed. Device drivers for power-managed devices interact with the power manager to control device power modes according to the system's PM policy.
Power-aware applications
These are user-written applications that interact with the power manager. They provide functionality specific to the embedded system (e.g. monitoring environmental conditions that could affect the desired operational mode of the system).
Persistent storage services
These allow device drivers to preserve hardware and software configuration details when the system is placed in a standby mode. The developer can customize the physical storage location of this persistent data for the embedded system.
BSP support
Code within the board-specific IPL and startup programs implements the board- and CPU-specific support for sleep/standby modes.

## Slide 17: More Challenges
Device Control
  Future application workload
    When do you power down a device?
  Traditional I/O Handling
    Control returns to application after I/O is complete
Application
Kernel
Device

## Slide 18: Overview
Concurrency Control
  Concurrency of I/O operations alone, not of threads in general
  Synchronous vs. Asynchronous I/O
    Asynchronous I/O can improve energy efficiency by allowing the OS to schedule it
Energy Management
  Power state of device needed to perform I/O operations
  Determined by pending I/O requests using Asynchronous I/O
Notes: An OS can improve energy by putting peripherals into low power modes and dropping the processor to a sleep states when idle. The challenge lies in deciding when and how to do so. To manage energy well an OS must infer future application behavior.
Why concurrency?
Statement: The more workload information an application can give the OS, the more energy it can save when scheduling that workload.

## Slide 19: Integrated Concurrency and Energy Management (ICEM)
Device driver architecture that manages energy
  Implemented in TinyOS 2.0
  Three driver classes: virtualized, shared, dedicated
  Power Locks: synchronization primitives which couple energy, configuration, and concurrency management.
  Component library: arbiters, power managers, and configurators.
Advantages of ICEM
  Energy Efficient: within 1.6% of hand tuned implementation
  Reduces code complexity: 400 vs 68 lines (nesC)

## Slide 20: Hardware Platform
CPU
  MSP430
    8Mhz, 16-bit
    I2C, SPI, ADC
    10kB Ram
Radio
  CC2420
    250kbps, 802.15.4
Flash
  ST M25P80
    2Mb External
Total Solar
  TSR Photodiode
Photo Active
  PAR Photodiode
Temperature and Humidity
  SHT11
Notes: 802.15.4
low-rate wireless personal area networks (LR-WPANs)
Data rates of 250 kbps, 40 kbps, and 20 kbps
It is the basis for the ZigBee,[1] WirelessHART, and MiWi specification
Fully Active: 30mA
Deepest Sleep State: 7-9uA

## Slide 21: Hardware Platform
Six Major I/O Devices
Possible Concurrency
  I2C, SPI, ADC
Energy Management
  Power on peripherals only when needed

## Slide 22: Example Application
Requirements
  Every 5 Minutes
    Sample all the sensors and log the readings to flash
  Every 12 Hours
    Retrieve new readings from flash and send to central collection unit
Pseudocode

## Slide 23: Example Application – Work Flow

## Slide 24: Example Application – Work Flow

## Slide 25: Example Application – Work Flow

## Slide 26: Example Application – Work Flow

## Slide 27: Example Application – Work Flow

## Slide 28: Example Application – Work Flow

## Slide 29: Example Application – Work Flow

## Slide 30: Example Application
Energy efficient application Pseudocode

## Slide 31: Example Application
Energy efficient application Pseudocode
Device Power Control

## Slide 32: Example Application
Energy efficient application Pseudocode
Device Wait Times

## Slide 33: Example Application
ICEM Application – Look familiar?
  Removed device control from application

## Slide 34: ICEM Attributes
Three classes of drivers
  Virtualized – Functional Interface
  Dedicated – Functional and Power Interfaces
  Shared – Functional and Lock Interfaces

## Slide 35: Virtualized Device Driver
Provides a Functional interface
Assumes multiple users
Implemented for higher-level users that can tolerate longer latencies
Concurrency Control
  Implicit control through buffering requests
Energy Management
  Implicit management based on pending requests

## Slide 36: Dedicated Device Driver
Provides a Functional and Power Control interface
Assumes one user
Implemented for lowest-level hardware independent abstractions
Concurrency Control
  None
Energy Management
  Explicit management through power control interface
Notes: Complete control over the hardware

## Slide 37: Shared Device Driver
Provides Functional and Lock interfaces
Assumes multiple users
Implemented for lower-level users that require stringent timing requirements
Concurrency Control
  Explicit control through Lock requests
Energy Management
  Implicit management base on pending requests

## Slide 38: ICEM Attributes
Three classes of drivers
  Virtualized – Functional Interface
  Dedicated – Functional and Power Interfaces
  Shared – Functional and Lock Interfaces
Power Locks – Split phase locks with integrated energy and configuration management
Notes: The split-phase operations TinyOS provides are similar to traditional asynchronous I/O with one important difference: they know
when an application is aware that an I/O operation has completed.
In a threaded system, a device driver will resume threads blocked on select (or a similar function), but the scheduler may not run the device thread immediately. In contrast, an application making split-phase I/O requests receives explicit notification from a device driver upon its completion through a direct upcall. This subtle but important difference allows a device driver to know exactly when an application has been notified about the completion of an I/O event. ICEM leverages this knowledge, using application I/O requests to precisely control a device’s power state.

## Slide 39: Power Locks
Used to synchronize access to drivers between software components
Idle Lock  Turn off device
Client could specify device configuration
Client request a lock, provide a callback function when it is given the lock
Deadlock problems could arise
Notes: Traditionally, locks such as mutexes and semaphores are blocking constructs that protect critical sections or shared data structures.
However, as TinyOS does not have blocking calls, its locks must be split-phase.
As power lock requests are non-blocking, a component can request several locks in parallel and proceed when they are all granted.
This of course raises deadlock concerns!! – Open area for future work!

## Slide 40: Power Locks
Notes: Traditionally, locks such as mutexes and semaphores are blocking constructs that protect critical sections or shared data structures.
However, as TinyOS does not have blocking calls, its locks must be split-phase.

## Slide 41: ICEM Attributes
Three classes of drivers
  Virtualized – Functional Interface
  Dedicated – Functional and Power Interfaces
  Shared – Functional and Lock Interfaces
Power Locks – Split phase locks with integrated energy and configuration management
Component Library
  Arbiters – manages I/O concurrency
  Configurators – provides device specific configurations
  Power Managers – provides energy management policy
Notes: Arbiters:
The component library has two arbiter policies, round robin and first come first served
Power Managers:
At boot, all power managers have control over a lock and all devices are powered down. When a power manager receives a callback from its arbiter that the lock has been requested, it takes this as a signal that the device needs to be used and must be powered up. Conversely, when a power manager receives the lock from its arbiter, it takes this as a signal that the device is idle and may be powered down again.
The component library has two power manager policies, immediate and deferred. The former powers off a driver as soon as the lock falls idle, while the latter waits for a timeout.
Configurator:
Configurators are part of a lock granting path. They implement the Configuration interface that arbiters use. Configurators are for when power lock clients have a code preamble which should execute before they perform any operations. Configurators allow clients to incorporate this logic into an arbiter. This is useful when many clients have the same code preamble: one implementation can serve them all.

## Slide 42: Component Library
Used to implement Power lock
Notes: Arbiters:
The component library has two arbiter policies, round robin and first come first served
Power Managers:
At boot, all power managers have control over a lock and all devices are powered down. When a power manager receives a callback from its arbiter that the lock has been requested, it takes this as a signal that the device needs to be used and must be powered up. Conversely, when a power manager receives the lock from its arbiter, it takes this as a signal that the device is idle and may be powered down again.
The component library has two power manager policies, immediate and deferred. The former powers off a driver as soon as the lock falls idle, while the latter waits for a timeout.
Configurator:
Configurators are part of a lock granting path. They implement the Configuration interface that arbiters use. Configurators are for when power lock clients have a code preamble which should execute before they perform any operations. Configurators allow clients to incorporate this logic into an arbiter. This is useful when many clients have the same code preamble: one implementation can serve them all.

## Slide 43: Component Library
Lock interface for concurrency control (FCFS, Round-Robin
ArbiterConfigure interface for automatic hardware configuration
DefaultOwner interface for automatic power management
Notes: Arbiters:
The component library has two arbiter policies, round robin and first come first served

## Slide 44: Component Library
Implement ArbiterConfigure Interface
Call hardware specific configuration from dedicated driver
Notes: Configurator
Configurators are part of a lock granting path. They implement the Configuration interface that arbiters use. Configurators are for when power lock clients have a code preamble which should execute before they perform any operations. Configurators allow clients to incorporate this logic into an arbiter. This is useful when many clients have the same code preamble: one implementation can serve them all.

## Slide 45: Component Library
Implement DefaultOwner interface
Power down device when device falls idle
Power up device when lock request is received
Provides Immediate and Deferred policies
Notes: Power Manager
At boot, all power managers have control over a lock and all devices are powered down. When a power manager receives a callback from its arbiter that the lock has been requested, it takes this as a signal that the device needs to be used and must be powered up. Conversely, when a power manager receives the lock from its arbiter, it takes this as a signal that the device is idle and may be powered down again.
The component library has two power manager policies, immediate and deferred. The former powers off a driver as soon as the lock falls idle, while the latter waits for a timeout.

## Slide 46: Shared Example Driver
MSP430 USART0
  Three modes of operation - SPI, I2C, UART

## Slide 47: Shared Example Driver
MSP430 USART0
  Three modes of operation - SPI, I2C, UART

## Slide 48: Shared Example Driver
MSP430 USART0
  Three modes of operation - SPI, I2C, UART

## Slide 49: Shared Example Driver
MSP430 USART0
  Three modes of operation - SPI, I2C, UART
POWER LOCK
Notes: Notice that each user is supplied a functional and lock interface characteristic of a SHARED driver

## Slide 50: Drawbacks
ICEM Overhead
  RAM and ROM – Library components require additional code space and memory.
  CPU cycles – calls utilizing shared drivers must go through arbiters, power managers.

## Slide 51: Arbiter Overhead
Arbiter Overhead (RAM)
  350 – 550 bytes Initial overhead
  Increases linearly with the number of clients
Notes: Explain RR and FCFS
+ denotes a complete arbiter. A simple arbiter doesn’t support power management (has no default client)
For n clients
FCFS arbiter uses 6+n bytes of RAM (Array based queue)
RR arbiter uses 8 + [n/8] (Bitmask of pending requests)

## Slide 52: Arbiter Overhead
Arbiter Overhead (CPU)
Notes: The bars are the additional cycles of a default client (to support power management).
The most expensive arbiter operation is the complete request-grant cycle which take 300-350 cycles.

## Slide 53: Arbiter Overhead
Arbiter Overhead (CPU)

## Slide 54: Arbiter Overhead
Arbiter Overhead (CPU)
Notes: The most expensive arbiter operation is the complete request-grant cycle which take 300-350 cycles (@ 4Mhz 75-87uS). Full arbiters take longer because they must tell the default client to release the lock

## Slide 55: Power Manager Overhead
Power manager library components
  RAM and ROM overhead
  Cycle count overhead
Notes: + Denotes a deferred power manager. (Immediate power manager, lack of plus).
Adding power management can add up to an additional 400 cycles of overhead (@ 4Mhz 100uS).
They use immediate power managers for the bus and ADC and deferred power manager for the voltage reference (because of the 17ms wakeup time).

## Slide 56: Drawbacks
ICEM Overhead
  RAM and ROM – Library components require additional code space and memory.
  CPU cycles – calls utilizing shared drivers must go through arbiters.
What does this overhead mean to power consumption?

## Slide 57: Energy Overhead
Hand Tuned – Most energy efficient
ICEM – All concurrent operations
Serial+ – Optimal serial ordering
Serial- – Worst Case serial ordering
Notes: Serial+ and Serial- are single threaded versions with blocking I/O calls that differ in their sensor sampling order which effect how often deferred drivers are powered on and off.

## Slide 58: Energy Overhead
Application Energy per Day
  5 Minute sampling interval
  12 hour send cycle
Notes: The serial+ implementation and the ICEM version have the same energy consumption during the sampling period. Serial- wastes more energy and the Hand tuned application uses less. Expected? Yes.
Notice that ICEM and the energy efficient hand tuned application have the same energy consumption (per day) during the send cycles.
Why is this important?

## Slide 59: Energy Overhead
Average energy consumption
Notes: The radio send function uses the most energy therefore the implementations with the more optimal send cycles will have greater lifetimes.

## Slide 60: Energy Overhead
Overhead of ICEM vs Energy Efficient implementation
  ADC Timeout + Power Lock Overhead
Overhead (Assume 288 samples per day)
  2.9mAs/day ~= 1029 mAs/year
  5.60% of total sampling energy
  0.03% of total application energy
Notes: Write Prior Samples – Log write and timeout times
Sample Photo active and sample total solar – Voltage reference warmup, analog samples, and voltage reference timeout
Sample Temperature and sample humidity – Humidity sample, temperature sample, and digital sensor timeout.
It is clear that the digital sensor readings dominate execution time and must be serialized (see hardware)

## Slide 61: Hand-Tuned Node Lifetime
Assume 2 AA batteries ~= 2700mAh
2.93 Years with 5 minute sample interval

## Slide 62: Node Lifetime Comparison

## Slide 63: Conclusions
ICEM: Integrated Concurrency and Energy Management
  Device driver architecture for ultra-low power device
  Applications operate within 1.6% of hand-tuned optimal energy implementation (based on representative application)
  Simplifies application and driver development
  Based on the hypothesis that the most useful power management information an application can provide an OS is the potential concurrency of its I/O operations.
    Application level concurrency allows the OS to save energy by efficiently scheduling I/O operations
  Questions the assumption that sensornet applications must be responsible for all energy management and cannot use a standardized OS with a simple API.

## Slide 64: Paper Analysis
What is new (2007)
  OS power management support in a RTOS
  Implemented in TinyOS – Split Phase
  Using a traditionally passive mechanism to implement an active power policy
  Idea that concurrency is the most important power information you can pass to the OS
What isn’t so new
  The idea of abstracting power management controls from the application to the OS (OSPM)
Notes: OSPM – Operating system directed power managment

## Slide 65: Paper Quality
Pros
  Major Conference (SOSP ‘07)
  Credible Authors
  Application using ICEM is within 1.6% energy consumption of the ideal implementation
  Low overhead (Memory and Computational)
  Reduces application complexity
  Unique Solution
Notes: Is the simple application really representative of most sensornet systems.
Implemented in TinyOS 2.0, Is this a pro or con? I would argue both.
Pro: Implementation proves it is viable
Cons: TinyOS is a small footprint OS that is single threaded (stack), non-blocking and has completion callback/upcall to eliminate polling. Would this concept scale?
Scalability

## Slide 66: Paper Quality
Cons
  Small number of citations (11 in 3.5 years)
  Increases initial development time
  All conclusions based on a “representative” simple application and hardware platform
    Low Duty Cycle
    All sensors sampled at same frequency
  Solution based on assumption that the most important information an application can provide the OS is the potential concurrency of its I/O operations.
  Potential for Deadlock
  Scalability
Notes: Is the simple application really representative of most sensornet systems.
Implemented in TinyOS 2.0, Is this a pro or con? I would argue both.
Pro: Implementation is viable.
Cons: TinyOS is a small footprint OS that is single threaded (stack), non-blocking and has completion callback/upcall to eliminate polling.
Is it scalable, portable, useable?

## Slide 67: Questions?
Notes: SOSP - Symposium of Operating Systems Principles
Is the simple application really representative of most sensornet systems
Implemented in TinyOS 2.0, Is this a pro or con?

## Slide 68: System Power
Notes: The processor values are reported for each power state and include leakage currents of platform peripherals such as sensors, USB, and flash. The peripheral values do not include the processor current draw; instead, they show the lowest power state the processor can enter while that peripheral is in use. This is LPM3 for the radio because the SPI bus is off except for a few hundred microseconds of radio commands. It is
LPM1 for the flash because logging operations keep the SPI bus on. It is also LPM1 for the analog sensors because the ADC requires a clock source, while it is LPM3 for the two I2C sensors because the bus is in software on GPIO pins. Finally, the voltage reference requires a 17ms warmup time before it can be used.

## Slide 69: Virtualized Example Driver
Flash Storage

## Slide 70: Example CC2420 Stack
3 Shared Drivers
  SPI
2 Dedicated Drivers
  GPIO
  Timer
2 Virtualized Drivers
  Send
  Receive

## Slide 71: Other Papers
V. Venkatachalam and M. Franz. “Power Reduction Techniques For Microprocessor Systems” ACM Computing Surveys, 37(3):195-237, 2005
Dutta, P., Culler, D., and Shenker, S. “Procrastination might lead to a longer and more useful life”. HotNets-VI (2007).

## Slide 72: Device Driver Links
QNX Developer Support "http://www.qnx.com/developers/docs/6.3.0SP3/neutrino/sys_arch/power.html”
Linux Device Drivers “http://lwn.net/images/pdf/LDD3/”
Mac Os X Developers Library “http://developer.apple.com/library/mac/#documentation/DeviceDrivers/Conceptual/IOKitFundamentals/PowerMgmt/PowerMgmt.html”
The Windows 2000 device driver book “http://books.google.com/books?id=nZu3E_IZS34C&pg=PA187&lpg=PA187&dq=device+drivers+that+manage+power&source=bl&ots=dwTefjhD67&sig=WjjWzBABUZC53vbtjnYq4OZGso4&hl=en&ei=ONOcTe7FBYKftwe0ofnVBw&sa=X&oi=book_result&ct=result&resnum=6&ved=0CEIQ6AEwBQ#v=onepage&q=device%20drivers%20that%20manage%20power&f=false”