## Slide 1: CMOS image sensors
Presenter: Alireza eyvazzadeh

## Slide 2
Complementary metal–oxide–semiconductor
a technology for constructing integrated circuits
CMOS technology is used in
Microprocessors
Microcontrollers
static RAM
other digital logic circuits
CMOS technology is also used for several analog circuits such as
image sensors
data converters

## Slide 3
Two most common types of sensors used in digital cameras:
CCD - Charge Coupled Device
CMOS - Complementary Metal Oxide Semiconductor
With the CMOS imager both the 'Photon-to-Electron' conversion and the 'Electron-to-Voltage' conversion is done within the pixel
CMOS image sensors
All CCD and CMOS image sensors operate by exploiting the photoelectric effect to convert light into electricity

## Slide 4
Some drawbacks of CCDs
complex clocking requirements
high power consumption
difficulty of on-chip integration of circuitry
limited frame rate
CMOS image sensors address these drawbacks by using the same technology as microprocessors and memory chips

## Slide 5
Advantages and drawbacks of the CMOS image sensors
Low Power Consumption
Also they are still too noisy and less sensitive than CCDs
one-third to more than 100 times less than that of CCDs
Lower cost compared to CCD’s technology
On chip functionality
A sensor can integrate various signal and image processing blocks such as ampliﬁers, ADCs, circuits for color processing and data compression, etc. on the same chip
Miniaturization
Random access of image data
Selective read-out mechanism
High-speed imaging

## Slide 6
internet camera
digital still camera
machine vision
Automotive
children’s toy
medicine and dentistry
fingerprint ID
surveillance
aerospace
motion analysis
industrial inspection
quality control
process control
target tracking
spectroscopy
present applications of CMOS image sensors

## Slide 7
Overall architecture
CMOS imagers architecture can be divided into four main blocks:
1. Pixel Array
2. Analog Signal Processors
3. Row and Column Selector
4. Timing and Control

## Slide 8
Each pixel contains a photodetector and some transistors. This area is the heart of an image sensor and the imaging quality is largely determined by the performance of this area.
active pixels (APS)
passive pixels (PPS)
APS are sensors that implement a buffer per pixel. Currently, APS are the predominant devices, although in some cases PPS are also used.
Basic pixel structures
An APS has three transistors in a pixel, while a PPS has only one transistor. To achieve further improvement, an advanced APS that has four transistors in a pixel, the so-called 4T-APS, has been developed.
Pixel circuits
The in-pixel amplifier in APS enables non-destructive read of the photodiode charge at a faster speed and a generally higher signal-to-noise ratio (SNR) than PPS

## Slide 9
Operation of a photodetector comprises:
generation of free electron-hole pairs due to impinging light
separation and collection of electrons and holes
(c) production of an output signal through interaction with other components
Several popular silicon-based photosensing devices are
Photoconductors
PN and PIN photodiodes
Phototransistors
photogates

## Slide 10
PN junction photodiode
an important sensor for digital imaging
The potential voltage decreases when electrons accumulate. By measuring the voltage drop, the total amount of light power can be obtained.

## Slide 11: Active pixel sensor, 3T-APS
First, the reset transistor MRS is turned on
PD is reset to the value Vdd −Vth
Vth is the threshold voltage of transistor MRS
MRS is turned off and the PD is electrically floated
The accumulated charge changes the potential in the PD; the voltage of the PD,VPD ,decreases according to the input light intensity
After an accumulation time, the select transistor MSEL is turned on and the output signal in the pixel is read out in the vertical output line.
When the read-out process is finished MSEL is turned off and MRS is again turned on to repeat the above process.

## Slide 12
Sensor peripherals
Addressing
In CMOS image sensors, to address each pixel, a scanner or a decoder is used
Readout circuits
The voltage of a PD is read with a source follower (SF)
a follower transistor MSF is placed in a pixel and a current load Mb is placed in each column

## Slide 13
Thanks for your attention