## Slide 1: Reactors in ChemCAD
Joshua Condon, Richard Graver, Joseph Saah, Shekhar Shah

## Slide 2: Different Types of Reactor Models
Several options are given in ChemCAD for reactor unit ops
  Each type plays a specific role
  Engineer’s prerogative/responsibility to choose the correct one for the job
Types
  Stoichiometric, Equilibrium, Kinetic, and Gibbs

## Slide 3: Stoichiometric Reactor
The simplest reactor model in ChemCAD
  Used only for single reactions
  Great for a preliminary model of a process
  Normally want a better reactor model for later process flow diagrams
Basics
  Specify stoichiometry of reaction, thermal mode, key component, and fraction conversion

## Slide 4: Stoichiometric Example
Suppose we are adiabatically forming water from oxygen in the following reaction:
  H2 + ½ O2 -> H2O
Basis: 1 mole Oxygen and complete reaction

## Slide 5: Process Flow Diagram for Example

## Slide 6: Stoichiometric Reactor
Great for initial observations and calculations
However, may not give physical results
Better to use one of the other reactors when accuracy is needed

## Slide 7: Equilibrium Reactor
Simulates multiple reactions at once
Requires equilibrium data or conversion for each reaction
Uses ChemCAD component thermodynamic data
More complex version of the stoichiometric reactor
Assumes reaction is run to close to equilibrium
  Approximates a reactor with a high residence time
Estimates final conversion based on component equilibrium data and reaction stoichiometry

## Slide 8: Equilibrium Reactor Example
Steam reformer in methane to syngas process
  Reaction 1: CH4 + H2O ←→ 3 H2 + CO
  Reaction 2: CO + H2O ←→ CO2 + H2
Specify 2 reactions
Select thermal mode
  Adiabatic, isothermal, or specify heat duty

## Slide 9: Equilibrium Reactor Example
Select reactor type (standard, methanation, shift)
Methanation reactor provides all necessary stoichiometry and equilibrium data specifically for example reactions 1 and 2
Select conversion mode
  Reaction conversion ignores equilibrium data and uses a specified percent conversion
  Approach delta T calculates equilibrium conversion at a certain temperature above or below reactor T
  Approach fraction estimates conversion of reaction that does not completely reach equilibrium

## Slide 10: Equilibrium Reactor Example
Select base component (for example, CH4)
  Select conversion
Enter stoichiometric coefficients for reaction 1
Repeat for reaction 2
Not used in methanation or shift presets

## Slide 11: Kinetic Reactor Module Basics
Can be used to calculate the volume of a PFR or CSTR, given the fractional conversion of one component, or vise-versa.
Up to 300 simultaneous reactions can be input
Liquid, Vapor, or mixtures are allowed, but the reaction is only allowed to take place in one phase

## Slide 12: Included Assumptions
CSTR Assumptions
Perfect mixing
Uniform temperature, pressure, and composition throughout
Rate of reaction is constant
If thermal mode adiabatic, or a heat duty is specified, temperature is calculated
If temperature is specified, heat duty is calculated
PFR Assumptions
No axial mixing or axial heat transfer occurs
Transit times for all fluid elements from inlet to outlet are of equal duration
Can be operated in the five thermal modes of isothermal, adiabatic, specified temperature profile, and specified utility conditions

## Slide 13: Kinetic Reactor Design Equations
For a CSTR, the design equation is
For a PFR, the design equation is
ChemCAD solves the CSTR equation directly, and solves the PFR equation using numerical integration if the volume is specified

## Slide 14: Rate Expression
CHEMCAD’s kinetic reactor is programmed with a rate expression of the form:

## Slide 15: Kinetic Reactor Interface 1

## Slide 16: Kinetic Reactor Interface 2

## Slide 17: Gibbs Reactor
After setting up the Gibbs reactor, input the following operating conditions and reactor specifications:
Temperature
Pressure
Inlet flow rates
Thermal mode
Reaction phase

## Slide 18: Gibbs Reactor Interface

## Slide 19: Gibbs Reactor Matrix

## Slide 20: Gibbs Reactor Outputs
ChemCAD outputs:
Temperature
Pressure
Composition
Heat of Reaction (inerts that take up heat can be taken into account)

## Slide 21: Advantages vs. Disadvantages
Advantages
Allows all potential reaction to happen by employing an element matrix (ChemCAD generated) and then minimizes the Gibbs free energy of the products to obtain output compositions and conditions
Disadvantages
Relies heavily on the specified thermal mode and thermodynamic model, but it is not clear how close the actual reaction comes to equilibrium