## Slide 1: ECE 2202 Circuit Analysis II
Dr. Dave Shattuck
Associate Professor, ECE Dept.
Lecture Set #10
Real and Reactive Power
Shattuck@uh.edu
713 743-4422
W326-D3

## Slide 2: Overview of this Lecture Set Real and Reactive Power
In this set of lecture notes, we will cover the following topics:
Definitions of Real and Reactive Power
Related Terminology
Usefulness of Reactive Power
Notes: You can click on the blue text to jump to the subject that you want to learn about now.

## Slide 3: Textbook Coverage
This material is introduced in different ways in different textbooks. Approximately this same material is covered in your textbook in the following sections:
Electric Circuits 6th Edition by Nilsson and Riedel: Sections 10.1 through 10.3
Electric Circuits 10th Edition by Nilsson and Riedel: Sections 10.1 through 10.3
Notes: You should also read these sections in your text. This material is intended to complement your textbook coverage, not replace it.

## Slide 4: Real Power and Reactive Power
We have determined the formulas for power when we have sinusoidal voltages and currents.
Now we are going to use these formulas to develop a way of approaching systems with sinusoidal sources that allow us to improve the performance of large electric motors, while at the same time reducing the loss of power in the transmission lines that carry the power from generating stations. We will find that:
A new concept called reactive power is a measure of the power that will be returned from the load to the source later in the same period of the sinusoid.
Reducing this reactive power in the load is a good thing.
Using phasor analysis will make it relatively simple to find this reactive power.
The power lines, which connect us from distance power generating systems, result in lost power. However, this lost power can be reduced by adjustments in the loads. This led to the use of the concept of reactive power.

## Slide 5: AC Circuit Analysis Using Transforms
Let’s remember first and foremost that the end goal is to find the solution to real problems. We will use the transform domain, and discuss quantities which are complex, but obtaining the real solution is the goal.

## Slide 6: Power with Sinusoidal Voltages and Currents
It is important to remember that nothing has really changed with respect to the power expressions that we are looking for. Power is still obtained by multiplying voltage and current.
The fact that the voltage and current are sine waves or cosine waves does not change this formula.

## Slide 7: Power as a Function of Time
We start with the equation for power as a function of time, when the voltage are current are sinusoids. We derived this in Lecture Set 10. We found that
The terms set off in red and green above have meaning and are useful, and so we will give them names.

## Slide 8: Definition of Real Power
We define the term in red to be the Real Power. We use the capital letter P for this. Note that we have already shown that this is the average power as well.

## Slide 9: Definition of Reactive Power
We define the term in green to be the Reactive Power. We use the capital letter Q for this. The meaning for this will be explained in more depth later.

## Slide 10: Meaning of Reactive Power – Part 1
For most students, the meaning of Real Power, P, is fairly clear. Real Power is the average power. The Reactive Power, Q, is much less obvious. To explain it, we will begin by noting that in the phasor domain, we have

## Slide 11: Meaning of Reactive Power – Part 2 (Resistive Case)
Let’s look at some special cases. Take the case where our circuit is purely resistive, that is, it could be modeled using only resistors. In this case the impedance is real, which means that q is equal to zero. We get that
In the resistive case, where q is equal to zero, this reactive power is zero.

## Slide 12: Meaning of Reactive Power – Part 3 (Inductive Case)
Let’s look at another special case. Take the case where our circuit is purely inductive, and could be modeled using only inductors. In this case the impedance is positive and imaginary, and q is equal to 90°. We get that
In the inductive case, where q is equal to 90°, the real power is zero. This should make sense, since with inductors energy is stored in the magnetic field, but later returned to the circuit.

## Slide 13: Meaning of Reactive Power – Part 4 (Capacitive Case)
Let’s look at a third special case. Take the case where our circuit is purely capacitive, and could be modeled using only capacitors. In this case the impedance is negatve and imaginary, and q is equal to -90°. We get that
In the capacitive case, where q is equal to -90°, the real power is zero. This should make sense, since with capacitors energy is stored in the electric field, but later returned to the circuit.

## Slide 14: Meaning of Reactive Power – Part 5 (Conclusion)
So, we have the following situation. The Real Power, P, is the average power, and is the power associated with resistances. The inductors and capacitors take power in during the first half cycle of a sinusoid, but then give all of that power back in the second half cycle. The Reactive Power, Q, is used as a measure of the energy that is given to the inductors and capacitors, and then returned later.

## Slide 15: Meaning of Reactive Power – (Note)
The Reactive Power, Q, is used as a measure of the energy that is given to the inductors and capacitors, and then returned later. It can be shown that the energy given in the first half cycle is Q/w. This energy is returned from the inductors and capacitors in the second half cycle. The Reactive Power is important in applications relating to transfering power over transmission lines.

## Slide 16: Power Terminology - 1
Several quantities are used so often in power calculations that they are given specific names. The first definition, the Power Factor Angle, involves the phase angle between voltage sinusoid and the current sinusoid. We have used the symbol q for this here. This is shown assuming that the phase angle of the current sinusoid, i(t), is zero. Some textbooks use arbitrary phases for current and voltage, and call them qi, and qv. In this case, the angle of interest would be the angle of the voltage with respect to the angle of the current, or qv- qi.
This special symbol indicates that we are defining a new quantity.

## Slide 17: Power Terminology - 2
Several quantities are used so often in power calculations that they are given specific names. The second definition, the Power Factor, is the cosine of the phase angle between voltage sinusoid and the current sinusoid. Again, we define it using both of the possible notations for the phase angles. Remember that the definitions at right are the ones that we will use in these notes, where we assume that the phase of the current, qi, can be set to zero.
Note that pf is used as a common abbreviation for power factor.

## Slide 18: Power Terminology - 3
Several quantities are used so often in power calculations that they are given specific names. The third definition, the Reactive Factor, is the sine of the phase angle between voltage sinusoid and the current sinusoid. It should be clear that while the power factor was the coefficient in the Real Power, the Reactive Factor is the coefficient for Reactive Power.
Note that rf is used as a common abbreviation for reactive factor.

## Slide 19: Power Terminology - 4
Several quantities are used so often in power calculations that they are given specific names. When we have an inductor, the phase of the impedance, q, is positive and equal to 90°. When we have a combination of passive elements where the inductances are dominant, this phase will be positive, but typically not 90°. We call this situation an inductive circuit, or an inductive load.
Note that in this case the sin(q) will be positive, so the reactive power Q that is absorbed will be positive.

## Slide 20: Power Terminology - 5
Several quantities are used so often in power calculations that they are given specific names. When we have a combination of passive elements where the inductances are dominant, this phase will be positive, but typically not 90°. This means that the current lags the voltage, that is, the current appears to be behind the voltage if they are plotted on the same axes. When this happens, when we have an inductive load, we say we have a lagging power factor.
Note that in this case the sin(q) will be positive, so the reactive power Q that is absorbed will be positive. We say that Reactive Power is being absorbed.

## Slide 21: Power Terminology - 6
Several quantities are used so often in power calculations that they are given specific names. When we have an capacitor, the phase of the impedance, q, is negative, and equal to -90°. When we have a combination of passive elements where the capacitances are dominant, this phase will be negative, but typically not -90°. We call this situation an capacitive circuit, or an capacitive load.
Note that in this case the sin(q) will be negative, so the reactive power Q that is absorbed will be negative.

## Slide 22: Power Terminology - 7
Several quantities are used so often in power calculations that they are given specific names. When we have a combination of passive elements where the capacitances are dominant, this phase will be negative, but typically not -90°. This means that the current leads the voltage, that is, the current appears to be ahead of the voltage if they are plotted on the same axes. When this happens, when we have an capacitive load, we say we have a leading power factor.
Note that in this case the sin(q) will be negative, so the reactive power Q that is absorbed will be negative. We say that Reactive Power is being delivered.

## Slide 23: Usefulness of Reactive Power
When we have inductive loads, such as motors, connected by long power lines, there is the potential for energy loss. In this case, we have energy that is being transmitted through the line to the load, only to be returned back through the line, from the load to the source. This causes energy to be lost. If the load can be adjusted to appear like a resistor, then this energy does not need to flow back and forth through the transmission lines, reducing the losses.
The solution is to connect capacitors near the motors. This makes the loads look like they are resistors. What happens is that the energy needed by the inductors are provided by the capacitors, moving back and forth between them. Thus, this energy only needs to travel through the transmission line once.
Reactive Power is a way to keep track of this phenomenon. By minimizing the Reactive Power, we can reduce losses.

## Slide 24: Absorbing and Delivering Reactive Power
We are familiar with the idea of a resistor, which absorbs positive power. That is, the voltage times the current, in the passive sign convention, gives the power absorbed by the resistor, which will be positive.
Using this concept, we say that when we use the passive sign convention, if the Reactive Power we solve for is positive, we will say that Reactive Power is being absorbed. Similarly, if Reactive Power is negative, we will say that Reactive Power is being delivered. We can show that, because of the phases, inductors absorb positive Reactive Power, and capacitors deliver positive Reactive Power.

## Slide 25: Absorbing and Delivering Reactive Power – Note
We can show that, because of the phases, inductors absorb positive Reactive Power, and capacitors deliver positive Reactive Power.
It is very important to remember that, in fact, inductors and capacitors do not deliver or absorb power, on average. They take power in, store it, and then return it. The Reactive Power is a measure of how power is stored temporarily in sinusoidal systems, and the sign indicates whether it was stored in electric fields or magnetic fields.

## Slide 26: So what is the point of all this?
This is a good question. First, our premise is that since electric power is usually distributed as sinusoids, the issue of sinusoidal power is important.
The quantities real and reactive power, that we have described here, are very different. Real power is the average power, and has direct meaning. Reactive power is a measure of power that is being stored temporarily. The sign tells us of the nature of the storage. Using these concepts, we can make changes which can improve the efficiency of the transmission of power.
All of this is made even more useful, when we see how phasors can make the calculation of real and reactive power easier.
Go back to Overview slide.