## Slide 1: Algae as a Biofuel
Advisors: Dr. Kauser Jahan Dr. William Riddell
Fall 2010

## Slide 2: Results Fall 2010
Using Algae as Fuel
Large Scale Algae Cultivation
Light Intensity Study
Nitrate Concentration Study
Future Work

## Slide 3: Biofuels and Algae
Concern about global warming has increased focus on biofuels
Currently biofuels are primarily from food & oil products
Algae is a promising source of biofuel
a For meeting 50% of all transport fuel needs of the United States.
b 70% oil (by wt) in biomass.
c 30% oil (by wt) in biomass.
Notes: Mention that using food for feedstock causes competition with food crops=> prices go up
Algae is grown suspended in water=> requires less area to grow

## Slide 4: Characteristics of Algae
Simple cell structure facilitate rapid growth
Over 50,000 species, 30,000 have been studied
Adaptable to a variety of environments
High lipid yield
Chemical composition CO0.48H1.83N0.11 P0.01
http://ucsdnews.ucsd.edu/thisweek/2008/01/images/photo-algae.jpg
http://images.businessweek.com/ss/08/05/0508_biofuels/image/algae.jpg
Notes: Allow for growth in many conditions and climates
Can be promising for developing countries as well

## Slide 5: Important Factors for Algae Growth
Most Important
  Light Intensity
  CO2 Concentration
  Nitrate Concentration
Other Factors
  Temperature
  pH
  Agitation/Mixing

## Slide 6: Scenedesmus dimorphus
Scenedesmus dimorphus is a unicellular bean shaped algae and 10 um in size.
This is one of the preferred species for oil yield, particularly for biodiesel.
Efficient in removal of nitrogen and phosphorus from wastewater-as such can also be used to treat wastewater and also for biodiesel source
Problems with Scenedesmus is that it is heavy, and forms thick sediments if not kept in constant agitation.
Protein 8-18% Carbohydrate 21-52% Lipid 16-40% Based on dry weight

## Slide 7: Large Scale Algae Cultivation
2 vats, 5 – 12 Liters of Algae Culture
  scenedesmus dimorphus
Temperature: 28 – 29° Centigrade
Light Intensity: 600 – 900 footcandles
Nitrate Concentration: 0.25 grams/Liter
  Bold Basal’s Growth Medium
CO2 Concentration: ~2ppm
Constant aeration and stirring
Notes: Mention that one vat contained algae from last semester, one contained new algae sample ordered from UTEX this semester

## Slide 8: Light Intensity Experiments
Three light intensities studied
  400, 600, and 800 foot candles
Two samples for each intensity
  Second sample has twice the concentration of first sample
Samples isolated from outside light sources
Samples stirred at 85 – 100 RPM
Temperature, Optical Density, and pH recorded twice a week

## Slide 9: Light Intensity Setup

## Slide 10: Light Intensity Growth Curves
Chart: Growth Curve of Full-Concentration Samples at Various Light Intensities
| 1 | 3 | 8 | 10 | 15 | 17 | 22 | 24 | 29 | 36 | 38 | 43
400 foot candles | 0.113 | 0.119 | 0.1926 | 0.229 | 0.31667 | 0.338 | 0.477 | 0.53 | 0.7266 | 1.1873 | 1.298 | 1.5603
600 foot candles | 0.1136 | 0.124 | 0.2016 | 0.2496 | 0.3186 | 0.3603 | 0.4683 | 0.532 | 0.653 | 1.2543 | 1.364 | 1.77
800 foot candles | 0.1156 | 0.134 | 0.216 | 0.3013 | 0.3643 | 0.3727 | 0.529 | 0.6123 | 0.7216 | 1.266 | 1.3823 | 1.599
Doubling Times
400 ft-c:
0.0643/day
600 ft-c:
0.0657/day
800 ft-c:
0.0559/day

## Slide 11: Light Intensity Lipid Yields
 | Max Lipid Yield | Average Lipid Yield
400 ft-c | 24.60% | 13.26%
600 ft-c | 13.30% | 8.00%
800 ft-c | 14.56% | 10.60%
Bligh and Dyer Method of Lipid Extraction

## Slide 12: Nitrate Concentration Experiments
6 Samples
  Ranging form 0.0 g/L to 0.5 g/L Nitrate, at 0.1 g/L intervals
Light Intensity: ~800 footcandles
Temperature: ~19 ° Centigrade
Stirred at 85 – 100 RPM
Temperature, Optical Density, and pH recorded twice a week
Study Still in Progress

## Slide 13: Growth Curve For Nitrate Study
Doubling Times
Deficient:
0.090/day
0.1 g/L:
0.150/day
0.2 g/L:
0.127/day
0.3 g/L:
0.144/day
0.4 g/L:
0.147/day
0.5 g/L:
0.078/day
Chart: Growth Curves of Nitrate Study
| 1 | 3 | 8 | 15 | 17 | 22 | 24
Nitrate Deficient | 0.0436 | 0.0583 | 0.1396 | 0.3893 | 0.443 | 0.5993 | 0.6273
0.1 g/L Nitrate | 0.0436 | 0.0646 | 0.1453 | 0.367 | 0.402 | 0.7333 | 0.7863
0.2 g/L Nitrate | 0.0456 | 0.067 | 0.1323 | 0.292 | 0.338 | 0.465 | 0.5516
0.3 g/L Nitrate | 0.0423 | 0.0556 | 0.134 | 0.3166 | 0.3506 | 0.5513 | 0.6056
0.4 g/L Nitrate | 0.0446 | 0.056 | 0.141 | 0.309 | 0.3326 | 0.519 | 0.646
0.5 g/L Nitrate | 0.0456 | 0.05433 | 0.1343 | 0.3166 | 0.3503 | 0.448 | 0.4933

## Slide 14: Conclusions about Scenedesmus Dimorphus
Light Intensity Study:
  Optimum Light Intensity 400 ft-c to 600 ft-c
  Since growth rates are similar=>More economic to use 400 ft-c
  Excess exposure to light is detrimental to growth rate and lipid yield
Nitrate Concentration Study:
  Optimum Nitrate Concentration between 0.1 g/L and 0.4 g/L
  Nitrogen from atm diffuses into solution in Deficient Solution
  Excess Nitrate also seems to be detrimental to algae growth
  Study still underway

## Slide 15: Future Work
Complete Nitrate Concentration Study
Work with Chemistry Department to improve Lipid Extraction Techniques
Mixed Culture Studies
CO2 concentration studies
Research various methods of CO2 delivery

## Slide 16: Future Work Continued
Develop Models to Predict Growth Rate and Lipid Content
Microalga Scenedesmus obliquus as a potential source for biodiesel production (Mandal & Mallick, 2009)

## Slide 17: Questions?

## Slide 18: Bold Basal’s Growth Medium