## Slide 1: The Minimum Rank Objective Function with Hysteresis
draft-ietf-roll-minrank-hysteresis-of-01
Omprakash Gnawali and Philip Levis
IETF 80
Prague, Czech Republic

## Slide 2: The Minimum Rank Objective Function with Hysteresis (MRHOF)
Applicable metrics
  Listed in I-D.ietf-roll-routing-metrics
  Additive
  Global
  Metric minimization as routing objective
Based on experiences with ETX
  Might be applicable to latency and other metrics

## Slide 3: Metric Minimization
Compute the Path metric and parent
  At the root
    cur_min_path_metric = MIN_PATH_METRIC
  On other nodes
    candidate_min_path_metric(i) = Link metric to a candidate i + Path metric from i to the DAG root
    cur_min_path_metric = Min{candidate_min_path_metric(1..n)}
    Parent = candidate whose cost is equal to cur_min_path_metric
Examples
  ETX: Paths with the smallest expected transmit count
  Latency: Least latency paths

## Slide 4: Hysteresis
Link metric can have jitter
  Example: ETX jitter due to changing link quality
  Can cause churn in the topology
Hysteresis delays the effects
  Short-term and small changes in link properties should not trigger path recomputation
Change parent if the new path metric is better by at least PARENT_SWITCH_THRESHOLD

## Slide 5: Computing Rank from Cost
Metric | Rank
Node Energy | 255 – Cost
Hop Count | Cost
Latency | Cost/65536
Link Quality Level | Cost
ETX | Cost
Rank undefined for these metrics
  Node state and attributes
  Throughput
  Link color

## Slide 6: Discussions
Parent set
  Next version will allow for more than one parent
  Rank based on path cost for the “longest” path
    Follows DIO processing rules in RPL
  Parent set size
    “Stretch” of rank from preferred parent rank?
    Configuration parameter?

## Slide 7: Parent set size concern
For a neighbor to be in the parent set, the node must maintain its Rank
  Additional 2 bytes per parent per DAG
  State/efficiency tradeoff
Increasing Rank (and available parent set) can require obtaining Rank values
  Unicast DIS?
  Link-local multicast DIS?

## Slide 8: Recommendations for Efficient Implementation of RPL
draft-gnawali-roll-rpl-recommendations-01
Omprakash Gnawali and Philip Levis
IETF 80
Prague, Czech Republic

## Slide 9: Goal
Many RPL configuration parameters
  timers, optional mechanisms, buffer sizes, …
Guidelines for efficient implementation
  Collect the experiences from experiments and deployments
Explain how certain parameters change the performance

## Slide 10: Trickle Parameters
Minimum Interval
  Small value encouraged
  Many DIOs in the queue is not helpful
Maximum Interval
  The larger the better
  Experiences with max interval of several hours
Redundancy Constant
  Small constant (e.g., 1-3) is typically adequate

## Slide 11: Route Poisoning
Does not prevent loops
No guarantee that it will work
  Lossy links
Tradeoff: complexity for incremental expedience in topology repair
  It is possible to detect and repair loops in tens of milliseconds

## Slide 12: Flushing Neighbor Information
Should avoid flushing neighbor information as much as possible
Can take a lot of time (and energy) to rebuild
Do not flush the table if the route is lost
  Link qualities to the neighbors might still be valid

## Slide 13: Data-path Slowdown During Repair
Advisable to increase the time between data packet transmission during repair
  Yields the channel to control traffic
  Greatly improves inconsistency repair
Can lead to higher latency and buffer overflow at the edges

## Slide 14: Path Cost Minimization vs Stability
Stable paths not always a requirement
  For UDP flows, churn is not harmful
Minimize/stabilize path cost (Rank) instead of maximizing path stability
  But very rapid path changes to minimize cost can also be harmful (MRHOF) -- tradeoff